## Slide 1: Evaluation of PAPR in WUR FDMA transmission
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
May 2018

## Slide 2: Introduction
The concept of FDMA scheme for WUR transmission was decided in last f2f meeting[1].
  Each 20MHz only contain one 4MHz sub-channel for wake-up signal transmission.
  Similar to 11ax’s 20MHz only operation, one wake-up receiver can stay in one of the sub-channel in wide bandwidth.
In this contribution, we evaluate the PAPR of WUR frame in FDMA transmission.
  For the WUR FDMA transmission, we assume that the phase rotation defined in [2] is applied on the whole WUR frame.
  Because WUR portion can be well designed to reduce the PAPR, the worst PAPR of WUR frame maybe bounded on 20MHz portion[3].
Also, we suggest how to reduce the Worst PAPR of entire WUR frame.

## Slide 3: PAPR of WUR PPDU
In order to increase the power efficiency, worst PAPR across whole PPDU should be minimized.
Here, we can consider the PAPR of two part separately.
  first part that is transmitted by using the 20MHz band.
    L-STF and L-LTF have been designed to have a lower PAPR
    But, L-SIG has not been optimized to have a lower PAPR due to length field which has various value.
    Also, BPSK Mark can have large PAPR due to random generation.
  Second part that is transmitted by using OOK waveform.
    In the single band, the OOK waveform is generated by using the 13 continuous subcarriers.
    And, as shown in [4], we checked that PAPR of OOK waveform was smaller than conventional OFDM symbol which was transmitted using the 20MHz band.
      The range of worst PAPR is form 2dB to 4.2dB.
In next slides, we investigate the PAPR of L-SIG and BPSK MARK symbol of WUR PPDU on WUR FDMA transmission.

## Slide 4: Contents of L-SIG
The LSIG is consist of the following fields
According to the definition of WUR frame format[2], we can consider the various length for the L-LENGTH field in L-SIG.
  The value of L-length field is described in Appendix.
Then the possible cases for the LSIG are
  Rate 4bits: 1 1 0 1 ( 6Mbps is assumed)
  Reserved 1 bit: 0
  Length 12 bits: herein, we considered the 18 cases for evaluation
  Parity 1 bit: determined on the other bits
  Tail 6 bits: 0 0 0 0 0 0

## Slide 5: PAPR of L-SIG
PAPR of L-Preamble according to BW and WUR frame format.
  PAPR of L-SIG is almost 4 - 6dB larger compared with the PAPR of WUR payload consisted of OOK waveform[3] in 20MHz.
    Phase rotation is applied to the results
It is difficult to optimize the PAPR by using the remaining few bit in this fields because almost bit fields in L-SIG are determined. but it may be fine because the WUR frame length has limited values so the worst PAPR is not higher than existing L-SIG PAPR.
BW | L-STF | L-LTF | L-SIG (dB)
 |  |  | worst PAPR
20MHz | 2.2394 | 3.1658 | 7.9454
40MHz | 5.2497 | 5.7938 | 9.9982
80MHz | 4.348 | 5.3962 | 9.6569

## Slide 6: PAPR of BPSK Mark
In [2], BSPK Mark is described like as
  A 20 MHz OFDM symbol, with tone spacing 312.5 kHz and BPSK, and of duration 4 us, is present immediately after the L-SIG field and right before the narrow band portion of any WUR PPDU.
There is no sequence defined for one BPSK symbol. and, it can cause the high PAPR of WUR PPDU due to using a sequence by implementation dependent.

## Slide 7: Optimization of PAPR
In order to reduce overall PAPR of WUR PPDU, we can consider the following
  The PAPR of BPSK Mark should not be higher than worst PAPR (PAPR of L-SIG).
    As shown in previous results, even though Phase rotation is applied on BPSK MARK symbol, from 20% to 30% PAPR of BPSK mark can larger than that of L-SIG in WRU transmission.
  So, to optimize the PAPR of BPSK mark, we can take account of the replacement of BPSK mark with L-SIG.
    repeating of the L-SIG does not require any hardware change and can be implemented simplify.
    But, it may occur the minor power consumption of 11ax device because repeated L-SIG is used for packet classification of 11ax.

## Slide 8: Conclusion
We investigated the PAPR of WUR frame in FDMA transmission
  Also, we checked that the PAPR of BPSK MARK can be higher than the Worst PAPR of L-SIG.
For the optimization of PAPR of entire WUR PPDU, we took into account the Non-WUR portion (i.e. L-SIG and BPSK Mark)
  By Replacing the BPSK Mark with L-SIG symbol, PAPR of BPSK Mark is bounded with that of L-SIG.
    It can be implemented simplify
Therefore, for the optimization of PAPR of WUR PPDU, we suggest the replacement of BPSK Mark with L-SIG symbol.

## Slide 9: Straw Poll #1
Do you agree that the BPSK Mark symbol which is located after L-SIG is replaced with L-SIG symbol?
  Y
  N
  A

## Slide 10: Reference
[1] IEEE 802.11-17/0575r10 Specification Framework for Tgba
[2] IEEE P802.11-REVmd™/D1.0, February 2018
[3] IEEE 802.11-18/802r0 PAPR Investigation on Multi-band Transmission
[4] IEEE 802.11-17/1625r6 Efficient FDMA MU Transmission Schemes for WUR WLAN

## Slide 11: Appendix
Phase rotation for wide bandwidth
  For the wide bandwidth transmission in Wi-Fi system, the phase rotation is defined as follows.

## Slide 12: Appendix
The value of L-length field
  L-length field in L-SIG is calculated as follows
  L-length field according to each case
Definition of case |  | L_length (octets) | Definition of case |  | L_length (octets) | Definition of case |  | L_length (octets)
case0 | FB=0, HDR | 192 | case6 | FB=6, HDR | 336 | Case12 | FB=12, HDR | 480
case1 | FB=0, LDR | 672 | case7 | FB=6, LDR | 1248 | Case13 | FB=12, LDR | 1824
case2 | FB=2, HDR | 240 | case8 | FB=8, HDR | 384 | Case14 | FB=14, HDR | 528
case3 | FB=2, LDR | 864 | case9 | FB=8, LDR | 1440 | Case15 | FB=14, LDR | 2016
case4 | FB=4, HDR | 288 | case10 | FB=10, HDR | 432 | Case16 | FB=16, HDR | 576
case5 | FB=4, LDR | 1056 | case11 | FB=10, LDR | 1632 | case17 | FB=16, LDR | 2208

## Slide 13: Appendix
The CDF of PAPR for BPSK Mark symbol