## Slide 1: Preamble Punctured WUR FDMA Transmission
Date: 2018-05-04
Authors:

## Slide 2: Recap: FDMA MU Wakeup Operations
Each 20MHz only contain one 4MHz sub-channel for Wake-Up Signal transmission.
Similar to 11ax’s 20MHz-only STA operation, one WUR receiver can stay in one of the sub-channel in a wide bandwidth.
L-LTF
L-SIG
BPSK-Mark
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #o
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #n
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
L-STF
L-STF
Wake-Up Signal for WUR STA #n
Wake-Up Signal for WUR STA #m
L-STF
L-STF
Secondary 20MHz
FDMA MU Wakeup Operation using 40MHz
FDMA MU Wakeup Operation using 80MHz

## Slide 3: Channel Access Procedure for WUR FDMA Transmission
Once a WUR Mode Setup that enabled the FDMA MU Wakeup Operations is completed,
  In a WUR mode, during the WUR Duty Cycle, the non-AP STA shall listen on the WUR in the negotiated WUR channel specified by WUR Mode Setup frame.
  In the below figure, STA2, STA3, and STA4 are using the FDMA MU Wakeup Operations
802.11 Main Radio of STA1, 2, 3, and 4
WUR of STA1, 2, 3, and 4
Power Off
WUR RX of STA4 is activated
WUR RX of STA4 is activated
WUR RX of STA3 is activated
WUR RX of STA3 is activated
WUR RX of STA2 is activated
WUR RX of STA2 is activated
WUR RX of STA1 is activated
WUR RX of STA1 is activated
Primary 20MHz
Secondary 20MHz
Secondary 40MHz

## Slide 4: Channel Access Procedure for WUR FDMA Transmission
During the WUR RX activated time of the non-AP STA, the AP may transmit Wakeup frames to the non-AP STA in the negotiated WUR channel specified by WUR Mode Setup frame if the WUR channel is idle.
802.11 Main Radio of STA1, 2, 3, and 4
WUR of STA1, 2, 3, and 4
Power Off
WUR RX of STA4 is activated
WUR RX of STA4 is activated
WUR RX of STA3 is activated
WUR RX of STA3 is activated
WUR RX of STA2 is activated
WUR RX of STA2 is activated
WUR RX of STA1 is activated
WUR RX of STA1 is activated
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
802.11 Main Radio
WUR TX
Wakeup to STA4
Wakeup addressed to STA4
Wakeup to STA3
Wakeup addressed to STA3
Wakeup to STA2
Wakeup addressed to STA2
Wakeup to STA1
Wakeup addressed to STA1
PIFS
PIFS
PIFS
Back-off
PIFS
PIFS
PIFS
Back-off

## Slide 5: Channel Access Procedure for WUR FDMA Transmission
The FDMA MU Wakeup Operations has following constraints.
  If the PHY-CCA.indication(BUSY, {secondary}) is issued from the PHY, the AP can’t transmit Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 40/80 MHz channels even though the secondary 40/80 MHz channels are idle.
  If the PHY-CCA.indication(BUSY, {secondary40}) is issued from the PHY, the AP can’t transmit Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 80 MHz channels even though the secondary 80 MHz channels are idle.

## Slide 6: Channel Access Procedure for WUR FDMA Transmission
The FDMA MU Wakeup Operations has following constraints.
  If the AP has no pending Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 20 MHz channel, the AP can’t transmit Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 40/80 MHz channels.
  If the AP has no pending Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 40 MHz channel, the AP can’t transmit Wakeup frames to the non-AP STA whose the negotiated WUR channel is in the secondary 80 MHz channels.

## Slide 7: Preamble Punctured WUR FDMA Transmission
When a WUR channel assigned from non-primary channels is busy, an AP does not transmit any signal to the corresponding WUR channel but it can transmit Wakeup frames on other idle channels.
  I.e., The Legacy preamble (L-STF, L-LTF, L-SIG, BPSK-Mark) and the Wake-up Signal are not transmitted on the corresponding the WUR channel.
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #o
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
L-STF
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
CCA Busy
CCA Busy

## Slide 8: Preamble Punctured WUR FDMA Transmission
When a WUR channel assigned from non-primary channels is idle but there is no pending Wakeup frames to transmit in the WUR channel, an AP does not transmit any signal to the corresponding WUR channel but it can transmit Wakeup frames on other idle channels.
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #o
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
L-STF
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
CCA idle but no pending Wakeup frames
CCA Idle but no pending Wakeup frames

## Slide 9: Conclusion
When the AP supports the preamble punctured HE MU PPDU transmission, the proposed preamble punctured WUR FDMA transmission can be easily supported though the basic primitives of the 802.11ax.
  The CCA of the preamble punctured WUR FDMA transmission is based on per20MHzbitmap.

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-1625-06-00ba-efficient-fdma-transmission-schemes-for-wur-wlan.pptx

## Slide 11: Straw Poll 1
Do you support the following preamble punctured WUR FDMA transmission?
  When an AP that supports the preamble punctured HE MU PPDU transmission on the 802.11 main radio meets one of the following conditions on a WUR channel assigned from non-primary channels,
    busy
    idle but there is no pending Wakeup frames to transmit in the WUR channel
  the AP does not transmit any signal to the corresponding WUR channel but it can transmit Wakeup frames on other idle channels.