## Slide 1: On NGV Channel Models
Date: 2018-05-08
Authors:

## Slide 2: Introduction
IEEE NGV study group has been formed to study the evolution of 802.11 technology for next-generation V2X communications [1].
Channel models needs to be developed for performance evaluation and proposal selection for NGV standard.
We discuss the scenario and possible channel models in this contribution.

## Slide 3: What scenarios NGV should consider?
Vehicle-to-Vehicle (V2V)
  Usage: collision avoidance safety systems.
  Channel Types: Rural, Highway, Urban, LOS and NLOS.
Vehicle-to- Pedestrian (V2P)
  Usage: safety alerts to pedestrians, bicyclists, etc.
  Channel Types: Rural, Urban, LOS and NLOS
Vehicle-to- Infrastructure (V2I)
  Usage: traffic signal or traffic conditions
  Channel Types: Microcells for Urban and Rural
Key Characteristics for NGV channel models
  Doppler, Shadowing by other vehicles/buildings/trees and inherent nonstationary.

## Slide 4
11p channel model needs to be improved
A comprehensive study of V2V channels was conducted in [2] and it called for improvements for IEEE 802.11p standard and channel modelling.
Channel modelling and measurements for V2V and V2I by WiMAX and 3GPP [3] were conducted after 11p.
  V2I channel models are quite different from V2V and V2P because of antenna heights, shadowing effect, etc..
Worst cases for Doppler shift also need to be considered.
  Maximum Doppler spread in V2V scenarios can be up to 4 times higher than the Doppler frequency caused by a vehicle's velocity.

## Slide 5
V2V and V2P channel models for NGV
Note that NGV channel models for V2V and V2P should be different from 3GPP [4].

## Slide 6
V2V and V2P channel models for NGV
In [5], V2V channel models for the following five scenarios had been proposed by summarizing the measurements from different research institutes.
  Rural LOS, Urban Approaching LOS, Street Crossing NLOS, Highway LOS, Highway NLOS
 | Tap1 | Tap2 | Tap3 |  | Units
Power | 0 | -14 | -17 |  | dB
Delay | 0 | 83 | 183 |  | ns
Doppler | 0 | 492 | -295 |  | Hz
Profile | Static | HalfBT | HalfBT |  | 
Table 5: Rural LOS Parameters
 | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -8 | -10 | -15 | dB
Delay | 0 | 117 | 183 | 333 | ns
Doppler | 0 | 236 | -157 | 492 | Hz
Profile | Static | HalfBT | HalfBT | HalfBT | 
Table 6: Urban Approaching LOS Parameters
 | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -3 | -5 | -10 | dB
Delay | 0 | 267 | 400 | 533 | ns
Doppler | 0 | 295 | -98 | 591 | Hz
Profile | Static | HalfBT | HalfBT | HalfBT | 
Table 7: Crossing NLOS Parameters
 | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -10 | -15 | -20 | dB
Delay | 0 | 100 | 167 | 500 | ns
Doppler | 0 | 689 | -492 | 886 | Hz
Profile | Static | HalfBT | HalfBT | HalfBT | 
Table 8: Highway LOS Parameters
 | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -2 | -5 | -7 | dB
Delay | 0 | 200 | 433 | 700 | ns
Doppler | 0 | 689 | -492 | 886 | Hz
Profile | Static | HalfBT | HalfBT | HalfBT | 
Table 9: Highway NLOS Parameters
252 km/hr max differential
252 km/hr max differential
119km/hr max differential
126km/hr max differential
144km/hr max differential

## Slide 7
Channel Model for NGV V2I
We can borrow the channel model from 3GPP with minor modifications as NGV V2I models [3].
(b) V2I operation
Parameters | Outdoor to Outdoor
Pathloss | PL_B1_tot(d) = max(PLfreespace(d), PL_B1(d)) where d is distance between UEs PLfreespace is free space path loss (Eq. 4.24 in [6]), PL_B1 is the Winner + B1b ([7] Table 4-1) channel model for hexagonal layout with the following offsets LOS offset = 0 dBc NLOS offset = -5 dBc While calculating Winner + B1 pathloss the following values shall be used h_BS = h_MS = 1.5m, h_BS' = h_MS' = 0.8m
LOS Probability | Winner II-B1 ([6] Table 4-7)
Shadowing standard deviation | 7 dB log-normal
Shadowing correlation | i.i.d.
Fast Fading | ITU-R IMT UMi ([8] Annex 1.3.2) LOS and NLOS

## Slide 8: Summary
We propose to adopt the C2C channel model in [5] as the NGV V2v and V2PChannel models.
We propose to adopt the 3GPP V2V outdoor to outdoor channel model in [3] as the NGV V2I channel models.

## Slide 9: Reference
[1] Hongyuan Zhang and etc., “802.11 For Next Generation V2X Communications”, IEEE 802.11-18/0513r2.
[2] C.F. Mecklenbrauker, etc., , “Vehicular channel characterization and its implications for wireless system design and performance,” vol. 99, No. 7, July 2011, Proceeding of IEEE.
[3] “Study on LTE Device to Device Proximity Services”, 3GPP TR 36.843, V12.0.1 (2014-03)
[4] “Study on LTE-based V2X Services”, 3GPP TR 36.885, V14.0.0 (2016-06)
[5] “IEEE 802.11 Regulatory SC DSRC Coexistence Tiger Team V2V Radio Channel
Models”, 802.11-14/0259r0.