## Slide 1: NGV SG PAR Discussions
Date: 2018-05-08
Authors:

## Slide 2: Introduction
In [1] the motivation of forming NGV SG was stated.
A baseline PAR proposal is in doc 11-18-861 [2]
Discussion point on “Scope” session of PAR proposal:
  Throughput gain
  Target Doppler (speed)
  Longer range
  Operation Band

## Slide 3: 1. Throughput Gain over 11p
In [3] some PHY feasibility was discussed.
To achieve more advanced use cases beyond basic safety, we think that the main goal of NGV is to improve the throughput in the most aggressive Doppler environment.
  Higher achievable MCS
  Longer packet length.
As shown in [3], by picking some existing PHY technologies in other amendments, in the aggressive Doppler environment we should be able to get ~2x throughput improvement from 11p observed on top of MAC.
PAR Scope may state the quantitative throughput gain over 11p in aggressive Doppler environment.

## Slide 4: 2. Target Doppler
11p PAR states that: “…operating at speeds up to a minimum of 200 km/h…”.
CV2X target is vehicle absolute speed of 250km/h, and relative speed of 500km/h.
  No materialized difference from 11p in real operation.
Propose to have the same speed requirement of 250km/h in NGV’s PAR scope section.

## Slide 5: 3. Longer Range
11p PAR says: “…for communication ranges up to 1000 meters…”.
Actual range is dependent on Tx output power and Tx/Rx implementations.
As analyzed in [1][3], it should be easy to find some “low hanging fruits” from existing amendments that achieve longer range than 11p.
It may not be worthwhile to come up with a detailed range in the PAR, but instead just say “longer range than 11p”.

## Slide 6: 4. Operation Band
It is natural to reuse the same band and channelization as DSRC in 5.85~5.925GHz band.
There was some discussions [3][4] for “protecting” the incumbent 11p/DSRC operation in the collision avoidance safety channel (Ch172), which is practically the only channel that 11p devices are deployed.
  11p is dedicated for safety and it requires robustness.
In PAR should we say NGV PHY is excluded from Ch172?
An alternative is not to state channel exclusion in PAR, and leave the discussion to the TG stage.
  NGV may still introduce multiple-antenna 1SS cases, where it may define the CSD value, so technically NGV PHY spec may still cover Ch172, even if NGV PPDU is disallowed in this channel.
  Efficient coex method to allow NGV PHY in Ch172? Again, this is likely a TG topic

## Slide 7: SP1
Do you agree that NGV PAR scope defines 2x throughput gain over 11p in the aggressive Doppler channel with highest vehicle operating speed at minimum of 250Km/h ?

## Slide 8: SP2
Which of the following options regarding the operation band in the NGV PAR scope do you prefer:
  Option-1: PAR Scope states that Ch172 is not in the scope of NGV, and NGV PHY is not allowed in Ch172.
  Option-2: PAR Scope does not mention channel exclusion within 5.85~5.925GHz band, and leave the discussions in TG stage.

## Slide 9: Reference
[1] Hongyuan Zhang et. al., “802.11 For Next Generation V2X Communications”, IEEE 802.11-18/0513r2.
[2] Hongyuan Zhang et. al., 11-18-0861-00-0ngv-IEEE-802.11-NGV-SG-Proposed-PAR
[3] Hongyuan Zhang et. al., 11-18-0860-00-0ngv-NGV-PHY-Feasibility-Discussions
[4] Onn Haran, et. al., 11-18-0xxx-00-0ngv-802.11ngv-High-level- Requirements