## Slide 1: Addressing in VL Wake-up frame
Date: 2018-05-07
Authors:

## Slide 2: Background
While receiving a WUR frame, WUR STA obtains information in the order of the frame format
As soon as the STA recognizes that the receiving frame is not intended to it, it can simply stop receiving and discard the frame before it checks the FCS
  E.g., address mismatch, protocol mismatch
Early discarding of unintended WUR frame is beneficial for WUR STAs
  Avoiding power consumption on receiving and processing WUR frame
    The airtime of the Frame Body could range from 32us to 2ms
  Increasing chance to resynchronize to intra BSS WUR frames

## Slide 3: Inefficiency in addressing of VL Wake-up frame
In the current draft spec,
  The Address field of the WUR wake-up frame is set to 0 when multiple WIDs are included in the frame body of the frame
Since all WUR APs set the same address value for VL Wake-up frame, WUR STA cannot distinguish whether the receiving VL Wake-up frame is sent from the associated AP or OBSS AP
  Whenever an AP transmits a VL Wake-up frame, all VL-capable OBSS STAs should check the Frame Body field
The power consumption of OBSS STA will increase
FC Length Present: 1
Address
(0)
OBSS STA
Multiple WUR IDs (STA1, STA2)
TD Control
FCS
STA1
STA2
AP1
AP2
OBSS STA receive procedure
Receive, No matched WID found Discard

## Slide 4: Proposed modification
Using a common address value for VL Wake-up frame has no benefit
  Address 0 does not give any information on identification
  WUR STA can be informed that multiple WIDs are included in the Frame Body using the Type field and Length Present field
We propose to use the TXID for the Address field of VL Wake-up frame
  An OBSS STA can discard the frame as soon as it gets the Address field value
FC Length Present: 1
Address
(0)
OBSS STA
No matched WID Discard
Multiple WUR IDs (STA1, STA2)
TD Control
FCS
STA1
STA2
AP1
(TXID1)
AP2 (TXID2)
OBSS STA receive procedure
FC Length Present: 1
Address
(TXID1)
Identified as an OBSS frame
Discard
Multiple WUR IDs (STA1, STA2)
TD Control
FCS
Start Receiving
Start Receiving

## Slide 5: Additional Addressing rule for VL Wake-up frame
If all WUR STAs listed in the Frame Body belong to the same Group ID, AP can set the Address field of the Wake-up frame to that Group ID
  Intra BSS STA not identified by the Group ID can discard the Wake-up frame as soon as it checks the Address field
  In such case, the overall power consumption of intra BSS STAs can be greatly reduced
Also, the utility of Group ID can be improved
  AP can wake up a part of STAs in the same group
  More flexible Group ID assignment is possible
FC Length Present: 1
Address
(0)
STA6
Multiple WUR IDs (STA1, STA2)
TD Control
FCS
STA1
STA2
TXID1
STA4 receive procedure
FC Length Present: 1
Address
(GID1)
Receive, Frame intended to other STAs
Discard
Multiple WUR IDs (STA1, STA2)
TD Control
FCS
GID1: {STA1, STA2, STA3}
No matched WID Discard
Start Receiving
STA4
STA5

## Slide 6: Example of AP/STA behavior
AP has pending buffered BU for multiple WUR STAs
  If the WUR STAs have a common GID, AP sets the Address field of VL Wake-up frame to the GID
    Only the STAs with the same GID will process the Frame Body
  Otherwise, the Address field is set to the TXID
    All WUR STAs in the BSS will process the Frame Body
A STA receives a VL Wake-up frame
  The STA match the Address field with its TXID and GIDs assigned by the AP
    Same requirement with ML Wake-up frame reception
  If not matched, discard the frame
  If matched, process the Frame Body

## Slide 7: Conclusion
The current addressing rule of VL Wake-up frame causes unnecessary processing of Wake-up frame from OBSS AP
In order to reduce the power consumption of WUR STA, we proposed that
  The Address field of VL Wake-up frame is set to the transmit ID
Also, to achieve additional power saving gain, we proposed that
  The Address field of VL Wake-up frame is set to the group ID if all WUR STAs listed in the Frame Body belong to that group ID

## Slide 8: Strawpoll 1
Do you agree the following?
  The Address field of the WUR Wake-up frame is set to the transmit ID when multiple WIDs are included in the Frame Body field of the frame

## Slide 9: Strawpoll 2
Do you agree the following?
  The Address field of the WUR Wake-up frame is set to either the transmit ID or the group ID when multiple WIDs are included in the Frame Body field of the frame
    If the Address field is set to the group ID, the Frame Body field contains more than one WUR IDs of the WUR STAs identified by that group ID.