## Slide 1
Overview of CV2X Requirements
Date: 2018-05-07
Authors:
Name | Affiliations | Address | Phone | email
Bahar Sadeghi | INTEL | 2111 NE 25th Ave Hillsboro, OR 97124 USA | +1-503-803-2471 | Bahareh.Sadeghi@intel.com

## Slide 2: Abstract
This submission provides an overview of 3GPP Rel 14 and 15 service requirements for CV2X, specifically summary of
  TS 22.185 (Rel 14)
  TS 22.186 (Rel 15)
This submission is intended for information only

## Slide 3: Rel 14 (TS 22.185)
V2X Definition
  Vehicle-to-Vehicle (V2V)
  Vehicle-to-Infrastructure (V2I)
  Vehicle-to-Network (V2N)
  Vehicle-to-Pedestrian (V2P)

## Slide 4: Requirements
Density
  Control the area and the size of the area where the messages are being distributed.
  Distribute information in a resource efficient way to large numbers of UEs supporting V2X application.
  Support a high density of UEs supporting V2X application.
Latency
  Max latency for transfer of messages between two UE supporting V2V/P (directly or via RSU):100ms
  Max latency for particular usage (pre-crash) 20ms
  Max latency between UE supporting V2I and RSU: 100ms
  E2e delay of less than 1000ms between UE and V2N server
Message size & frequency
  Transfer of periodic broadcast messages of 50-300 bytes between 2UEs that support V2V (not including security components)
  Transfer of event-triggered messages of up to 1200 bytes
  Message transmission frequency of maximum 10 per sec per UE
Range and speed
  Range providing ample response time, e.g., 4 sec
  Relative speed of 500Km/h
  Absolute speed 250km/h

## Slide 5: Rel 15 (TS 22.186)
To enhance 3GPP support for V2X scenarios in the following five areas:
  General Aspects: interworking, comm-related requirements valid for all V2X scenarios
  Vehicles Platooning
  Vehicles Platooning enables the vehicles to dynamically form a group travelling together. All the vehicles in the platoon receive periodic data from the leading vehicle, in order to carry on platoon operations. This information allows the distance between vehicles to become extremely small, i.e., the gap distance translated to time can be very low (sub second). Platooning applications may allow the vehicles following to be autonomously driven.
  Advanced Driving
  Advanced Driving enables semi-automated or fully-automated driving. Longer inter-vehicle distance is assumed. Each vehicle and/or RSU shares data obtained from its local sensors with vehicles in proximity, thus allowing vehicles to coordinate their trajectories or maneuvers. In addition, each vehicle shares its driving intention with vehicles in proximity. The benefits of this use case group are safer traveling, collision avoidance, and improved traffic efficiency.
  Extended Sensors
  Extended Sensors enables the exchange of raw or processed data gathered through local sensors or live video data among vehicles, RSUs, devices of pedestrians and V2X application servers. The vehicles can enhance the perception of their environment beyond what their own sensors can detect and have a more holistic view of the local situation.
  Remote Driving
  Remote Driving enables a remote driver or a V2X application to operate a remote vehicle for those passengers who cannot drive themselves or a remote vehicle located in dangerous environments. For a case where variation is limited and routes are predictable, such as public transportation, driving based on cloud computing can be used. In addition, access to cloud-based back-end service platform can be considered for this use case group.

## Slide 6: General Requirements (not a complete list)
Control communication range for a message
Optimize communication for two UEs in a group and in proximity
Support confidentiality and integrity of messages transfer among a group
Support relative lateral position accuracy of 0.1 m
Support high connection density – worst case estimate 3100 to 4300 cars/sq km
Enable a UE supporting a V2X application to obtain network access via another UE supporting V2X application.
An RSU shall be able to communicate with up to 200 UEs supporting a V2X application.

## Slide 7: Platooning
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message/ Sec) | Max end-to-end latency (ms) | Reliability (%) (NOTE 5) | Data rate (Mbps) | Min required communication range (meters) (NOTE 6)
Scenario | Degree |  |  |  |  |  |  | 
Cooperative driving for vehicle platooning Information exchange between a group of UEs supporting V2X application. | Lowest degree of automation | [R.5.2-004] | 300-400 (NOTE 2) | 30 | 25 | 90 |  | 
 | Low degree of automation | [R.5.2-005] | 6500 (NOTE 3) | 50 | 20 |  |  | 350
 | Highest degree of automation | [R.5.2-006] | 50-1200 (NOTE 4) | 30 | 10 | 99.99 |  | 80
 | High degree of automation | [R.5.2-007] |  |  | 20 |  | 65 (NOTE 3) | 180
Reporting needed for platooning between UEs supporting V2X application and between a UE supporting V2X application and RSU. | N/A | [R.5.2-008] | 50-1200 | 2 | 500 |  |  | 
Information sharing for platooning between UE supporting V2X application and RSU. | Lower degree of automation | [R.5.2-009] | 6000 (NOTE 3) | 50 | 20 |  |  | 350
 | Higher degree of automation | [R.5.2-0010] |  |  | 20 |  | 50 (NOTE 3) | 180
NOTE 2: This value is applicable for both triggered and periodic transmission of data packets. NOTE 3: The data that is considered in this V2X scenario includes both cooperative manoeuvres and cooperative perception data that could be exchanged using two separate messages within the same period of time (e.g., required latency 20ms). NOTE 4: This value does not including security related messages component. NOTE 5: Sufficient reliability should be provided even for cells having no value in this table NOTE 6: This is obtained considering UE speed of 130km/h. All vehicles in a platoon are driving in the same direction. |  |  |  |  |  |  |  | 
5 UEs in a group , relative longitudinal position accuracy of less than 0.5m, for platooning reliable comm between a UE and 19 others

## Slide 8: Advanced Driving
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message/Sec) | Max end-to-end latency (ms) | Reliability (%) (NOTE3) | Data rate (Mbps) | Min required Communication range (meters) (NOTE 4)
Scenario | Degree |  |  |  |  |  |  | 
Cooperative collision avoidance between UEs supporting V2X applications. |  | [R.5.3-001] | 2000 (NOTE 5) | 100 (NOTE 5) | 10 | 99.99 | 10 (NOTE 1) | 
Information sharing for automated driving between UEs supporting V2X application. | Lower degree of automation | [R.5.3-002] | 6500 (NOTE 1) | 10 | 100 |  |  | 700
 | Higher degree of automation | [R.5.3-003] |  |  | 100 |  | 53 (NOTE 1) | 360
Information sharing for automated driving between UE supporting V2X application and RSU | Lower degree of automation | [R.5.3-004] | 6000 (NOTE 1) | 10 | 100 |  |  | 700
 | Higher degree of automation | [R.5.3-005] |  |  | 100 |  | 50 (NOTE 1) | 360
Emergency trajectory alignment between UEs supporting V2X application. |  | [R.5.3-006] | 2000 (NOTE 5) |  | 3 | 99.999 | 30 | 500
Intersection safety information between an RSU and UEs supporting V2X application. |  | [R.5.3-007] | UL: 450 | UL: 50 |  |  | UL: 0. 25 DL: 50 (NOTE 2) | 
Cooperative lane change between UEs supporting V2X applications. | Lower degree of automation | [R.5.3-008] | 300-400 |  | 25 | 90 |  | 
 | Higher degree of automation | [R.5.3-009] | 12000 |  | 10 | 99.99 |  | 
Video sharing between a UE supporting V2X application and a V2X application server. |  | [R.5.3-010] |  |  |  |  | UL: 10 | 
NOTE 1: This includes both cooperative manoeuvers and cooperative perception data that could be exchanged using two separate messages within the same period of time (e.g., required latency 100ms). NOTE 2: This value is referring to a maximum number of 200 UEs. The value of 50 Mbps DL is applicable to broadcast or is the maximum aggregated bitrate of the all UEs for unicast. NOTE 3: Sufficient reliability should be provided even for cells having no values in this table NOTE 4: This is obtained considering UE speed of 130km/h. Vehicles may move in different directions. NOTE 5: These values are based on calculations for cooperative maneuvers only. |  |  |  |  |  |  |  | 

## Slide 9: Extended Sensors
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message /Sec) | Max end-to-end latency (ms) | Reliability (%) | Data rate (Mbps) | Min required communication range (meters)
Scenario | Degree |  |  |  |  |  |  | 
Sensor information sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-001] | 1600 | 10 | 100 | 99 |  | 1000
 | Higher degree of automation | [R.5.4-002] |  |  | 10 | 95 | 25 (NOTE 1) | 
 |  | [R.5.4-003] |  |  | 3 | 99.999 | 50 | 200
 |  | [R.5.4-004] |  |  | 10 | 99.99 | 25 | 500
 |  | [R.5.4-005] |  |  | 50 | 99 | 10 | 1000
 |  | [R.5.4-006] (NOTE 2) |  |  | 10 | 99.99 | 1000 | 50
Video sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-007] |  |  | 50 | 90 | 10 | 100
 | Higher degree of automation | [R.5.4-008] |  |  | 10 | 99.99 | 700 | 200
 |  | [R.5.4-009] |  |  | 10 | 99.99 | 90 | 400
NOTE 1: This is peak data rate. NOTE 2: This is for imminent collision scenario. |  |  |  |  |  |  |  | 

## Slide 10: Remote Driving
Communication scenario description | Req # | Max end-to-end latency (ms) | Reliability (%) | Data rate (Mbps)
Information exchange between a UE supporting V2X application and a V2X Application Server | [R.5.5-002] | 5 | 99.999 | UL: 25 DL: 1

## Slide 11: Summary
Range: 1000m
Relative speed: 500 Km/h
Absolute speed: 250 Km/h
Density: ~4500 cars /sq Km
Latency: 100ms
Special cases: 20ms or lower (10, 5, 3 ms)
Message size: variable; 50-300 bytes for safety, upto 12Kbytes
Transmit rate: 10-100 message per sec (inverse relation to packet size)