## Slide 1: High-level requirements of NGV
Date: 2018-05-08
Authors:

## Slide 2: Abstract
Backward compatibility with 802.11p can’t be compromised
  Physical layer enhancements should be applied in very specific scenarios for assuring the backward compatibility
802.11p has a minor specification gap (diversity)
Multi-channel use-cases will expand

## Slide 3: Backward Compatibility
802.11p vehicles and infrastructure are deployed globally
  Cadillac CTS is available for purchase since 2017
  VW announced mass-scale deployment from 2019
  Toyota announced mass-scale deployment from 2021
  Some infrastructure is already deployed and will expand significantly
The essence of cooperative safety communication is backward compatibility
  Far more important than potential 2dB sensitivity improvement
European Parliament voted for backward compatibility:
  2. Highlights the need for a clear legal framework to support the deployment of C-ITS and welcomes a future delegated act under the ITS Directive (Directive 2010/40/EU) to ensure the continuity of services, deliver interoperability and support backward compatibility;

## Slide 4: 802.11p Specification Gap
802.11p doesn’t specify antenna diversity
Solutions in market do support antenna diversity
  RX diversity: MRC
  TX diversity: CDD
  Recommendation: 802.11ngv specification should formalize the de-facto implementations

## Slide 5: Antennas Installation Considerations
The majority of vehicles have a single 802.11p antenna
  OEMs will try to avoid a second antenna due to cost implications: cabling, amplification, handling
  A second antenna will be used only when absolutely needed to assure 360°coverage
  Recommendation: don’t impose two antennas solution
Correlation between two 802.11p antennas is low
  MIMO for V2V is likely unfeasible, but might be feasible for I2V (when RSU is tall)
  STBC for V2V would improve link budget, yet not backward compatible
  Recommendation: consider STBC, but not MIMO, as part of PHY enhancements

## Slide 6: 7 Channels Are Allocated
Channel Number | Src. and dest. | Application Types
Reserved: 5 MHz (lower 5 MHz of DSRC spectrum) |  | 
172 (5.855 to 5.865 GHz) | VV IV | V2V safety, situational awareness Intersection safety
174 | IV | IV safety and mobility Miscellaneous/private use (non-priority)
176 | PV IP IV | VRU SCMS
178 | IV | WAVE Service Advertisements Broadcast-based applications
180 | VI VV | Future non BSM-based V2V safety (e.g. CACC) Mobility applications
182 | IV | Miscellaneous/private use (non-priority) SCMS IV safety and mobility applications
184 (5.915 to 5.925 GHz) | VI/V PI/V | Public Safety Public Transit
  SAE J2945/0 Channel List

## Slide 7: Physical Layer Compatibility Suggestion
Mode | Use-case | Candidate channels | Method of operation
Legacy | Channel is used Existing broadcast services | 172, 178 | 802.11p only
Greenfield | Channel is currently unused Expecting new broadcast and unicast services | 174, 180, 182 | 802.11ngv
Mixed | Channel is partially used | 176 | Existing broadcast services continue to use 802.11p Unicast and new services will use 802.11ngv (with fallback option to 802.11p)
  Table is subject to change as new DSRC services can be introduced before 802.11ngv specification is completed

## Slide 8: Multi-channel Operation
Multi-channel use-cases will expand
Other channels shall not harm safety channel
  IEEE1609.4 defines multi-channel operation but doesn’t consider cross-channel interferences
  While transmitting, vehicle reception might be disabled
  Transmitting vehicle might harm nearby vehicles reception of other channels
X
X

## Slide 9: Multi-channel Operation Options
Do nothing
  Control timing of service channel transmissions to avoid missing important safety messages
  For example, concurrent transmission of safety and non-safety messages
  Other?
  Recommendation: study limitations of multi-channel operation, and potential mitigation mechanisms
  Study is in 802.11 domain even if specification might eventually fall within IEEE1609 scope