## Slide 1: Discussion on WUR (802.11ba) States
Date: 2018-05-24
Authors:

## Slide 2: Abstract
This contribution provide a first draft state diagram for the 802.11ba non-AP STA and some supporting discussion.

## Slide 3: Assumptions
For a STA with a WURx – WUR mode is only available if the STA is in a legacy Power Management mode and has negotiated a WUR mode with its associated AP.
To insure assumption 1: WUR mode can only be negotiated with the associated AP once the STA is in Power Management mode, therefore the negotiation occurs when the STA is in the Awake state.
A STA in Power Management mode can only transmit or receive PRC frames when it is in Awake mode
The PRC of STA is in WUR mode (WURx Awake or WURx Doze) is unable to transmit or receive frames
A STA in WUR mode (a subset of Power Management mode) can only receive WUR frames in WURx Awake state.
A STA in WUR mode, in WURx Doze state can not receive or send any frames.

## Slide 4: Therefore there are Six Allowed Non-AP STA States:
UnAssociated
  STA PRC is active – PPDUs can be received and transmitted – infrastructure BSS services are not available.
Associated
  STA PRC is active – PPDUs can be received and transmitted – the STA has access to the services provided by the infrastructure BSS
Awake
  STA PRC is active and associated – PPDUs can be received and transmitted.
Dose
  STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
WURx Awake
  STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
  WUR is active, WUR PPDUs can be received
WURx Dose
  STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
  WUR is not active, WUR PPDUs can not be received

## Slide 5: 802.11ba Non-AP STA State Diagram

## Slide 6: Changing State
Unassociated can go to: Associated via association.
Associated can go to: Unassociated via disassociation, a different Associated State via reassociation. An associated STA can also go to Power Save Mode and move to Awake.
Awake can go to: Dose via the configured power save mode. An awake STA can renegotiate or end Power Save Mode. An awake STA can also go to WUR PS Mode and move to WUR Awake.
Dose can go to: Awake
WURx Awake can go to: WURx Doze via the configured WRU mode. Receive a WUR awake PPDU and move to Awake, or an WUR STA can suspend WRU mode and move to Awake
WURx Doze can go to: WUR Awake

## Slide 7: References