## Slide 1: NGV Use Case Template
Date: 2018-06-10
Authors:

## Slide 2: Abstract
This document is a proposed template to describe use cases for NGV
In this initial version, four representative use cases are included. Additional use cases are expected to be added in future versions of this document, while refining the sample use-cases
The goal is to derive a clear set of requirements from the use cases

## Slide 3: Terminology
  Backward Compatible – Ability to decode IEEE802.11p messages, and transmitting messages decoded by IEEE802.11p devices
  Co-existence – Ability of IEEE802.11p devices not to transmit while non-IEEE802.11p messages are transmitted

## Slide 4: 1. Basic Safety Messages (BSM)
Overview: All vehicles periodically (typ. 10HZ) broadcast a message containing its basic information. Based on received messages, driver is alerted of an upcoming safety risk
  Channel 172 is used in US. Channel 180 is used in EU
Deployment timeline: IEEE802.11p solutions are deployed now, with de-facto solutions to missing requirements. Enhanced range solution are likely to be adopted by the market once available
Requirements:
  Antenna diversity
  Up to 500km/h relative speed operation
  It is desired to increase IEEE802.11p range. NHTSA DSRC NPRM defines 300m minimal communication range, which is hard to satisfy in urban NLOS. Target would be 25% length increase over IEEE802.11p in this case
Limitations:
  Full backward compatibility, able to decode and understand messages of 11p
  Maintaining channel load
  Maintaining fairness

## Slide 5: 2. Sensor Sharing
Overview: Vehicles periodically broadcast all detected objects from all sensors, and receive objects from all other vehicles
  Sensor sharing message is under definition. Actual packet length is TBD, but expected to be much longer than BSM because many objects can be detected by many sensors
  The channel is yet to be determined
Deployment timeline: >2023 (expected)
Requirements:
  Number of transmitted bytes per packet is higher (>50%) than IEEE802.11p under same conditions (duration, PER, range, wireless channel) for maintaining transmission time as current IEEE802.11p BSM
Limitations:

## Slide 6: 3. Multi-Channel Operation
Overview: Concurrent multi-channel operation, where one channel is safety channel, and the second is non-safety
Deployment timeline: Now (most pilot deployments); >2023 (OEMs installations – expected)
Requirements:
  High availability of safety channel
    Minimal same-vehicle cross-interference – blinding self-vehicle safety channel by non-safety channel transmissions
    Minimal cross-vehicles interference – blinding near-vehicle from receiving a safety message coming from a far vehicle
  High utilization of all channels
Limitations:

## Slide 7: 4. Infrastructure Applications
Overview: Safety and non-safety data from infrastructure to vehicles
Deployment timeline: Now
Requirements:
  High throughput
Limitations:
  Existing applications should maintain backward compatibility
  IEEE802.11p vehicles may be capable to upgrade to support new applications

## Slide 8: Requirements Summary
Backward compatible mode
  Antenna diversity
  Up to 500km/h relative speed operation
  Longer range (nice to have)
Potential non-backward compatible mode
  High throughput
  High channel utilization
  Migration to backward compatible mode
Multi-channel operation
  High availability of safety channel
  High utilization of all channels

## Slide 9: References