## Slide 1: Channel Access for WUR FDMA
Date: 2018-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
The concept of FDMA transmission scheme has been proposed in the current SFD [1], [2]
  Each 20MHz only contains one 4MHz sub-channel for wake-up signal transmission
As long as WUR FDMA follows primary transmission rule, some problems need to be dealt with
In this contribution, we suggest how to operate when there are WUR PPDUs only on secondary channels and the secondary channels are busy during PIFS

## Slide 3: Problem definition
Assume the AP wants to wake up STA2, which is residing on S20 channel
According to the primary transmission rule, the WUR AP shall look into its WUR primary channel even when the AP transmits a WUR frame only for STAs on WUR secondary channel while the AP does not have a buffered WUR packet on the primary channel
  The WUR PPDU shall include any WUR signal (i.e., null frame or all padding frame) on the primary channel in [3, 4]
In this situation, what if the secondary channels are busy during PIFS?
The procedure for this case needs to be clarified
P20
S20
WUR signal
WUR of STA1 in P20 channel
WUR of STA2 in S20 channel
AP wants to wake up only STA2
WUR packet buffered
AIFS
[AC]
Backoff
PIFS
: Channel idle
: Channel busy

## Slide 4: Option 1: Re-invoke backoff procedure immediately
When an AP has a WUR frame to be sent only on a secondary channel and the back-off counter is 0, if the secondary channel is busy during PIFS, the AP does not send the WUR PPDU and invokes the backoff procedure again with the same CW
  Between the backoffs, channel status of the secondary channel might not vary
WUR PPDU
WUR PPDU
P20
S20
: Channel idle
: Channel busy
AIFS
[AC]
Backoff
AIFS
[AC]
Backoff
PIFS
PIFS
WUR packet buffered
AIFS
[AC]
Backoff
PIFS

## Slide 5: Option 2: Re-invoke backoff procedure after timeout
When an AP has a WUR frame to be sent only on a secondary channel and the back-off counter is 0, if the secondary channel is busy during PIFS, the AP does not send the WUR PPDU and invokes the backoff procedure after a timeout with the same CW
  Compared to option 1, the trial number of EDCA may decrease but the latency on the secondary channel may be longer
  If the duration for timeout is long enough, channel status of the secondary channel might be changed from busy to idle
P20
S20
WUR PPDU
WUR PPDU
Timeout
AIFS
[AC]
Backoff
WUR packet buffered
PIFS
PIFS
AIFS
[AC]
Backoff
: Channel idle
: Channel busy

## Slide 6
A WUR FDMA PPDU is sent only when there is a WUR frame to be sent on the primary channel
Simple but a STA on a secondary channel will suffer longer delay
  The STA will receive a WUR frame until there is a WUR frame to be sent on primary channel
  The STA will still not receive a WUR frame when the secondary channel might be busy or the STA might be not within On-duration
    In this case, the STA will wait for long time for receive the WUR FDMA PPDU for the STA (See the Appendix)
Option 3: Transmit a WUR PPDU with a buffered frame on primary channel
P20
S20
WUR PPDU
WUR packet buffered
PIFS
AIFS
[AC]
Backoff
WUR packet buffered
WUR PPDU
Latency

## Slide 7: Summary
We mentioned that the problem which can occur when there are WUR PPDUs only on secondary channels and the channels are busy during PIFS should be handled
We suggested three ways to resolve it
  Option 1: Re-invoke backoff procedure immediately
  Option 2: Re-invoke backoff procedure after timeout
  Option 3: Transmit a WUR PPDU with a buffered frame on primary channel

## Slide 8: Straw Poll
Which option do you prefer to resolve the problem?
  Option 1: Re-invoke backoff procedure immediately
  Option 2: Re-invoke backoff procedure after timeout
  Option 3: Transmit a WUR PPDU with a buffered frame on primary channel

## Slide 9: References
[1] 11-17/0575r11, “Spec framework”
[2] 11-17/1625r6, “Efficient FDMA Transmission Schemes for WUR WLAN”
[3] 11-18/0822r2, “WUR FDMA Channel Access”
[4] 11-18/0963r1, “Spec Text for WUR FDMA Channel Access”

## Slide 10
An example of Option 3
Appendix
P20
S20
WUR PPDU
WUR PPDU
AIFS
[AC]
Backoff
WUR packet buffered
PIFS
PIFS
AIFS
[AC]
Backoff
WUR packet buffered
WUR packet buffered
WUR PPDU
Latency
: Channel idle
: Channel busy