## Slide 1: WUR Discovery Period Announcement
Date: 2018-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
WUR discovery frame is defined in the current 11ba draft [1]
Using WUR discovery frame, WUR STAs can scan nearby APs with extremely low power consumption [2]
  WUR STAs can know where to scan and what to look for by means of WUR Discovery element [3]
In this contribution, we suggest the WUR Discovery Period subfield, which can help WUR STAs how long they should scan on WUR discovery channels

## Slide 3: Problem definition
In [3], a WUR AP shall periodically transmit WUR Discovery frames
  However, a value of discovery period has not specified yet
  A WUR STA would scan discovery channels for a long time unnecessarily
  Or, a WUR STA would scan discovery channels for a period that is too short to receive the WUR discovery frame
Therefore, the WUR Discovery Period needs to be delivered to WUR STAs
  A WUR STA can decide reasonable waiting time to receive WUR discovery frame on a channel

## Slide 4: Proposed method
Defining the WUR Discovery Period subfield
  The WUR Discovery Period should be delivered via WUR AP subfield (refer to [3])
  If a WUR STA may save the information of the AP which the STA has ever associated to, then the STA can scan for a certain period using the saved information of discovery (When Transmitting WUR AP is set to 1)
  Once a WUR STA receives the WUR Neighbor AP element, it can use the WUR Discovery Period to scan several discovery channels (When Transmitting WUR AP is set to 0)
 | Element ID | Length | Element ID Extention | WUR AP Information Set
Octets: | 1 | 1 | 1 | variable
 | WUR Discovery Operating Class | WUR Discovery Channel | WUR AP Count | WUR AP List
Octets: | 1 | 1 | 1 | variable
WUR Discovery element
 | Bitmap Control | Short-SSID | BSSID | WUR Discovery Period
Octets: | 1 | 0 or 4 | 0 or 6 | 0 or 2
 | Transmitting WUR AP | Short-SSID Present | BSSID Present | WUR Discovery Period Present | Reserved
Bits: | 1 | 1 | 1 | 1 | 4

## Slide 5: Proposed size for WUR Discovery Period
The size of the WUR and PCR Beacon Period is 2 octets and the unit is TU
  So, the maximum period is about 67 sec
WUR Discovery frame may be supposed to transmit similar to WUR and PCR beacons
Hence, 2 octets (in TU) is enough for the WUR Discover Period subfield

## Slide 6: Straw Poll
Do you agree to insert the WUR Discovery Period subfield into the WUR Discovery element and WUR Discovery Period Present subfield into the Bitmap Control?
  Y
  N
  A

## Slide 7: References
[1] “IEEE P802.11ba/D0.3”
[2] 11-17/0029r10, “WUR Usage Model Document”
[3] 11-18/1082r1, “Spec text update for WUR Discovery”