## Slide 1: Spec text clarification for FDMA
Date: 2018-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have defined FDMA operation in WUR
  A WUR STA may be allocated in one of multiple WUR FDMA channels by a WUR AP
  The allocated channel affects performance of corresponding STA especially when the STA operates in WUR duty cycle mode
  So we have to clarify channel allocation rule

## Slide 3: FDMA text
Followings are current specification text for FDMA [1][2]
  31.9 WUR FDMA operation
    (The second paragraph) When a WUR AP receives a WUR Capabilities element of which the WUR Channel Switching subfield of the WUR Capabilities Information field is equal to 1, the WUR AP shall set the WUR Channel Offset subfield of the WUR Parameters field of the WUR Mode element that it transmits to any value as defined in Table 9-262c (Subfields of WUR Parameters field from WUR AP), subject to the negotiated WUR duty cycle schedule does not overlap with the TWBTTs at which the WUR AP schedules for transmission WUR Beacon frames.

## Slide 4: FDMA and WUR Beacon
A WUR AP manages duty cycle operation of WUR STAs by adjusting starting time and channel offset
TWBTT are not overlapped with on duration of all WUR operating STAs

## Slide 5: Duty Cycle in FDMA
If a WUR STA wants to operate WUR mode with the WUR always on, there are some issues to be clarified
  The WUR STA may set On duration length and Duty cycle period are identical during WUR mode signaling
  The WUR STA should be allocated to a WUR channel where the WUR beacon is transmitted
    If not, the WUR STA cannot receive the WUR beacon frame
    However, the current text does not seem to explain it
  Nevertheless, we need to modify the draft text to clarify the channel assignment and WUR beacon transmission
    It is not ‘duty cycle’ but ‘on duration’ that shall not overlap with TWBTT

## Slide 6: Proposed change
We propose text modification as following
  When a WUR AP receives a WUR Capabilities element of which the WUR Channel Switching subfield of the WUR Capabilities Information field is equal to 1, the WUR AP shall set the WUR Channel Offset subfield of the WUR Parameters field of the WUR Mode element that it transmits to any value as defined in Table 9-262c (Subfields of WUR Parameters field from WUR AP), subject to the negotiated on duration of WUR duty cycle schedule does not overlap with the TWBTTs at which the WUR AP schedules for transmission WUR Beacon frames if the value of WUR Channel Offset subfield is not 0.
  Note: When a WUR AP receives a WUR Mode element from a WUR non-AP STA that wants to have WURx always in WURx awake state, the WUR AP needs to set the WUR Channel Offset subfield of the WUR Parameters field of the WUR Mode element to 0, which is the only option to satisfy the condition.

## Slide 7: Summary
In this submission, we have suggested spec text modification to clarify duty cycle operation in FDMA
  If a WUR STA wants to operate WUR mode with the WUR always on, the WUR STA shall not be allocated to a WUR channel where the WUR beacon is not transmitted
  It is not ‘duty cycle’ but ‘on duration’ that shall not overlap with TWBTT in current spec text

## Slide 8: References
[1] IEEE P802.11ba™/D0.3
[2] 11-18-1105-00-00ba-proposed-text-for-wur-mac-revision.docx

## Slide 9: Straw poll
Do you agree to following modification for TGba D0.3
  Modify following text in sub-clause 31.9 WUR FDMA operation
    When a WUR AP receives a WUR Capabilities element of which the WUR Channel Switching subfield of the WUR Capabilities Information field is equal to 1, the WUR AP shall set the WUR Channel Offset subfield of the WUR Parameters field of the WUR Mode element that it transmits to any value as defined in Table 9-262c (Subfields of WUR Parameters field from WUR AP), subject to the negotiated on duration of WUR duty cycle schedule does not overlap with the TWBTTs at which the WUR AP schedules for transmission WUR Beacon frames if the value of WUR Channel Offset subfield is not 0.
    Note: When a WUR AP receives a WUR Mode element from a WUR non-AP STA that wants to have WURx always in WURx awake state, the WUR AP needs to set the WUR Channel Offset subfield of the WUR Parameters field of the WUR Mode element to 0, which is the only option to satisfy the condition.