## Slide 1: Potential L2 security options for UL BCS
Date: 2018-07-02
Authors:

## Slide 2: Abstract
A full security threat analysis is in scope of TG.
Depending on the result of the threat analysis, the TG may make the following conclusions:
No L2 security needed
L2 data encryption needed (Confidentiality)
Verification of sender/destination address needed (Integrity)
The following slides outline possible solutions.
Note: the goal of this presentation is solely to provide potential solutions to facilitate the PAR and CSD development. The solution will be developed in TG.
Note: replay attacks addressed in previous contribution

## Slide 3: UL Options
Assumption: E2E security (confidentiality and/or integrity) is in place.
However, there may be DOS attacks, severity and level of risk for DOS attacks need to be understood, depending on that one of these options may be considered
  Option 1: Server address & STA identity signed by CA
  Option 2: L2 authentication
  Option 3: L2 encryption
  Option 4: Option 1 + Option 3
STA
AP
Server
Router
Data
Data
Data
Server Address
Bahar Sadeghi, Intel

## Slide 4: Option 1: Server address is signed by CA
STA is pre-installed with the Server address & CA certificate
With each packet transmission, STA includes the Server address signed by the CA
AP verifies the STA identity/server address using the certificate before forwarding the data
STA
AP
Server
Router
Data
Data
Data
Server Address
Digital signature

## Slide 5: Option 2: L2 authentication
STA is pre-installed with the Server address
STA generates public/private key and signs the data (and server address)
With each packet transmission, STA includes the public key
AP verifies the STA using the public key before forwarding the packet.
Note: mechanisms for verification of the public key by AP required
Note: both STA & AP may use a shared secret key
STA
AP
Server
Router
Data
Data
Data
Server Address
Public Key
Private Key

## Slide 6: Option 3: L2 encryption
STA is pre-installed with the Server address & a public key
AP is pre-installed with a private key
STA encrypts data (and server address) using the public key
AP verifies the payload (and address) using the private key before forwarding the packet.
Note: both STA & AP may use a shared key
Note: If key update is needed STA may receive updated public key distributed by AP
STA
AP
Server
Router
Data
Data
Data
Server Address
Public Key
Private Key
encrypted

## Slide 7: Option 4: Server address signed by CA and L2 encryption
AP is pre-installed with the CA certificate
STA is pre-installed with the Server address & CA certificate
STA & AP use a shared key or a pre-installed private/public key pair.
Data transmissions are signed by private key
AP uses shared/private key to decrypt the packet and verifies the STA identity, and the destination address using the certificate
STA
AP
Server
Router
Data
Data
Data
Server Address
Public Key
Digital signature
Private Key
encrypted

## Slide 8: Summary
One possible solution has been shown for different security requirements that may emerge from the security threat analysis to be conducted by TG.
By use of digital signature by CA, the AP can
  Verify the identity of the STA
  Verify the destination (IP) address of the data is not corrupted
  Decide based on the signature / identity of the STA, whether to forward the packet
  Decide based on the server (IP) address if the packet should be forwarded