## Slide 1: Group Delay for Group Addressed Wake Up Frames
Date: 2018-07-09
Authors:

## Slide 2
Abstract
In this contribution, we discuss the need to indicate the group delay for groups of STAs that may be woken up by group addressed wake up frames.

## Slide 3: Introduction
TGba agreed to use group-addressed wake up frames to wake up a number of STAs
  The Address field of the WUR Wake-up frame is set to
    —The group ID when the frame is group addressed [1]
    The purpose of wake up may be to transmit a group addressed packet to a group of STAs using PCR
  The AP may transmit a WUR Wake-up frame to a non-AP STA to indicate that group addressed buffered BU(s) are available for the STA via the PCR. [1]
However, different STAs may wake up at different times
  Different STAs have different PCR transition delays
  A STA indicates its PCR Transition Delay to its AP in WUR Capabilities elements
In this contribution, we discuss the benefit to indicate group delays when STAs are expected to be woken up using group addressed wake up frames

## Slide 4: PCR Transition Delay and Wake Up Time
STAs have different PCR Transition Delays
When a STA receives a group-addressed wake up frame, it begins the PCR transition immediately
  STAs wake up at different times
After waking up, STAs may wait for group addressed PCR packets such as data packets, trigger frame, etc.:
  An AP that transmits a WUR Wake-up frame to a non-AP STA that indicates the availability of group addressed buffered BU(s) via the PCR, …, the AP shall ensure that the following condition is met:
    —The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted WUR Wake-up frame indicating buffered group addressed BU(s) of PCR has expired [1]
  An AP that sends a WUR Wake-up frame to the STA(s) may send a Trigger Frame to solicit response frames from one or more STAs. [1]

## Slide 5: Wake Up Time and Energy Wastage
Different wake up time can cause unnecessary energy wastage
  STAs wake up at different times
  STAs may waste energy by keeping their PCR component on for an unnecessarily long duration, as shown in the figure below
  It is desirable to reduce awake time for STAs’ PCR to optimize for power consumption

## Slide 6: Approaches to Reduce Awake Time (1/3)
Two Options to reduce wasted awake time:
  1. AP only groups STAs with similar PCR Transition Delays
    STAs wake up with similar PCR transition delay; less wasteful PCR awake time
  2. AP can indicate max group delay for a group of STAs during Group assignment
    STAs delay PCR wake up to match max group delay to ensure all STAs in the group wake up around the same time as shown in the figure below

## Slide 7: Approaches to Reduce Awake Time (2/3)
Option 1: AP only groups STAs with similar PCR Transition Delays
  STAs wake up with similar PCR transition delay; less wasteful PCR awake time
Advantage of Option 1:
  Implementation based, no extra signaling/negotiation is needed
Disadvantage of Option 1:
  Not always possible
  Grouping of STAs may often be based on application and service need, not based on device characteristics
  Very restrictive on grouping of STAs

## Slide 8: Approaches to Reduce Awake Time (3/3)
Option 2: AP indicates max group delay for a group of STAs during Group assignment
  STAs may delay PCR wake up to match max group delay
Advantage of Option 2:
  Help STAs conserve energy by not keeping PCR on for an unnecessarily long period
  Improve key performance metric for WUR STAs
Disadvantage of Option 2:
  Needs extra signaling
    Likely in PCR WUR Mode Setup frames
    The AP is already aware of the Max Group Delay
  Not expected to be a big burden

## Slide 9: Conclusion
Current design of wake up procedure using group-addressed wake up frame may lead to unnecessary energy waste
  STAs wake up at different time due to different PCR transition delay
  STAs need to wait for group-addressed data or trigger frame until every STA in the group is awake
We discussed two options to reduce wasteful PCR awake time
  Option 1: AP only groups STAs with similar PCR transition delay
    Restrictive and not always possible
  Option 2: AP indicates max group delay to STAs; STAs delay PCR wake up to match max group delay
    E.g., during group assignment, e.g., in WUR Mode Setup frames
Option 2 efficiently reduces STAs’ PCR awake time while requiring some additional signaling on PCR

## Slide 10
References
[1] IEEE P802.11ba Draft 0.3, May 2018
[2] IEEE P802.11RevMD Draft 1.0, Feb. 2018

## Slide 11: SP 1
Which option do you prefer for reducing wasteful PCR awake time for a group of STAs woken up by a group addressed wake up frame?
  1: AP only assigns STAs with similar PCR Transition delay to the same group
  2: AP indicates the max group delay for a group of STAs
  3. Abstain
  Option 1/2/3:

## Slide 12: SP 2
Do you agree that the max group PCR transition delay should be indicated for a group of STAs during group assignment in WUR Mode Setup frames?
  Y/N/A: