## Slide 1: Spectral line suppression for MC-OOK
Date: 2018-07-09
Authors:

## Slide 2: Abstract
In [1], it was shown that spectral lines appear in MC-OOK because the same OFDM symbol is used always for the ‘on’ part.
[1] also proposed a method to eliminate the spectral lines, by binary randomization of the phase. Each OFDM symbol is given a binary phase rotation at random.
In this presentation we discuss an alternative method and investigate the impact of spectral line suppression on the TX power in PSD limited scenarios.

## Slide 3: Simulation assumptions
Data part only, 8K data bits
8X oversampling
LDR
  64 FFT
  OFDM symbol [1,1,1,-1,-1,-1, 0, -1,1,-1,-1,1,-1] from ref [2]
HDR
  32 FFT
  OFDM symbol [1, 1, 1, 0, -1, 1, -1] from ref [1]

## Slide 4: Recap: Spectral lines in MC-OOK
  Power computed using the periodogram (rectangular window) assuming total TX power is 30 dBm.
Data rate | Max Power in 3 kHz when Total TX power is 30 dBm (dBm)
Low | 17.9
High | 19.8
FCC limit (8 dBm) exceeded

## Slide 5: Cyclic shift randomization
Cyclic Shift (CS) randomization is a symbol randomization technique
Similar to CSD, but in time instead of across antennas
A set of cyclic shifts is pre-defined (e.g. 8 cyclic shifts)
A cyclic shift is chosen pseudo-randomly for each OFDM symbol
Note that
  A linear feedback shift register can be used to generate pseudo-random cyclic shifts
  The method works well for multi-antenna transmission, in conjunction with e.g. CSD

## Slide 6: Illustration of cyclic shift randomization

## Slide 7: Examples of cyclic shifts
The following delay values have been used in the simulations. These values have been designed to give sufficient spectral line suppression.
LDR: 0, -400, -800, -1200, -1600, -2000, -2400, -2800 ns
HDR: 0, -200, -400, -600, -800, -1000, -1200, -1400 ns
Caveat: There are combinations of delay values which leave residual spectral lines in the PSD because of failure to remove temporal correlations in some of the tones. Hence, the delays should be designed to ensure that spectral lines are sufficiently suppressed. See the Appendix for an example.

## Slide 8: Suppression of spectral lines in MC-OOK
Data rate | Randomization Method | Max Power in 3 kHz when Total TX power is 30 dBm (dBm) | Headroom to 8 dBm FCC limit (dB)
Low | Binary phase randomization [1] | 3.0 | 5.0
Low | Cyclic shift randomization | 1.2 | 6.8
High | Binary phase randomization [1] | 2.8 | 5.2
High | Cyclic shift randomization | 1.6 | 6.4
CS randomization  1.2-1.8 dB larger headroom to FCC limit

## Slide 9: Illustration of PSD with symbol randomization
The periodogram has been averaged over 30kHz for illustration purposes only

## Slide 10: PSD limited scenarios
According to [3], 4.3.2.3.3 “For equipment using wide band modulations other than FHSS, the maximum Power Spectral Density is limited to 10 dBm per MHz.”
Under the constraint above, the total TX power depends on the randomization method
Data rate | Randomization Method | Total TX power (dBm)
Low | Binary phase randomization [1] | 14.5
Low | Cyclic shift randomization | 15.6
High | Binary phase randomization [1] | 14.8
High | Cyclic shift randomization | 15.6
CS randomization  gain 0.8-1.1 dB in TX power

## Slide 11: Coherent reception of CS randomized MC-OOK
The channel needs to be estimated only for 1 OFDM symbol
Coherent detection can be performed with the aid of e.g. matched filtering, with a complexity similar to that of binary phase randomization

## Slide 12: Observations
CS randomization allows the optimization of the OFDM symbol for performance in PA limited scenarios, while ensuring good performance in PSD limited scenarios
CS randomization can yield significant gain in TX power when local geographic regulations impose limits on the PSD
CS randomization may give a larger headroom to the FCC limits than binary phase randomization
CS randomization does not change the PAPR of MC-OOK
CS randomization does not increase the complexity of coherent reception

## Slide 13: References
[1] WUR Power Spectral Density, IEEE 802.11-18/0824r1, S. Shellhammer et al.
[2] OOK Waveform Generation Follow-up, IEEE 802.11-18/0421r0, E. Park et al.
[3] Wideband transmission systems; Data transmission equipment operating in the 2,4 GHz ISM band and using wide band modulation techniques; ETSI EN 300 328 V2.1.1 2016-11

## Slide 14: Appendix
Example of a set of delays that leave residual spectral lines
Max power in 3 kHz when total TX power is 30 dBm: 10 dBm