## Slide 1: System Level Simulation Results of Full Duplex Transmission
Date: 2018-07-02
Authors:

## Slide 2: Introduction
Full Duplex (FD) technology is investigated as a candidate of key technology for the next generation of Wi-Fi [1-3].
Some initial results have been shown in [2] to demonstrate the throughput enhancement with interference cancellation.
This presentation is to provide more system level simulation results to show the throughput gain of FD based on the NS3 simulation platform.

## Slide 3: Simulation Assumptions
Number of AP: 1, 4
Number of STAs per BSS: 10
BSS Range: 10m
Bandwidth: 20MHz @ 2.4GHz
Self interference cancelation (SIC): 80dB~120dB
Traffic model: full buffer
Packet size: 1500 bytes
Data MCS: link adaptation
Antenna#: AP 1, STA 1
STA position: random (uniform distribution) within a certain BSS range
BSS Range

## Slide 4: Transmission procedure
Baseline:
  EDCA based transmission
Full Duplex:
  Trigger frame initiates every transmission
    Symmetric case (both AP and STA have FD capability)
    Asymmetric case (only AP has FD capability)
Trigger
Data 1
BA 1
Data 2
BA 2
AP
STA
Trigger
Data 1
BA 1
BA 2
AP
STA1
Data 2
STA2
Symmetric case
Asymmetric case

## Slide 5: Simulation architecture
When start transmission, the AP should decide whether to send a Trigger frame
  Considering self interference and mutual interference, if the predicted sum rate of the two FD links (UL+DL) is higher than the link without using FD, then send a Trigger frame
If needed, send the Trigger frame, followed by data transmission
STA side: send data after receiving the Trigger frame
AP side
STA side

## Slide 6: Simulation Results (symmetric FD)
Setting:
  Mode: symmetric FD
  AP number = 1
  STA number per BSS = 10
  SIC = 80, 90, 100, 110, 120dB
Result:
  110dB SIC is needed to achieve maximum throughput gain
  Up to 125% throughput gain can be obtained
Throughput gain definition:
  throughput gain = (FD throughput – EDCA throughput)/EDCA throughput

## Slide 7: Simulation Results (symmetric FD)
Setting:
  Mode: symmetric FD
  AP number = 4
  STA number per BSS = 10
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  Up to 194% throughput gain can be obtained
  More throughput gain can be achieved comparing with the single BSS case

## Slide 8: Simulation Results (asymmetric FD)
Setting:
  Mode: asymmetric FD
  AP number = 1
  STA number per BSS = 2 (simple setting)
    STA1 is 1 meter away from the AP (near)
    STA2 is 5 meters away on the other side (far)
    Using near-far paring, the DL transmission to STA1 can have relatively high SINR, in which case we can see more FD gain
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  29%~44% throughput gain can be obtained in simple scenario
STA1
STA2
1 m
5 m

## Slide 9: Simulation Results (asymmetric FD)
Setting:
  Mode: asymmetric FD
  AP number = 1
  STA number per BSS = 10 (random setting)
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  27% throughput gain can be obtained

## Slide 10: Conclusion
Through NS3 based system level simulation, we demonstrate that a large amount of throughput gain can be achieved by using FD transmission
In the symmetric FD case, more than 100% throughput gain can be obtained
In the asymmetric FD case, 27%~44% throughput gain is achievable.
Further optimization may be needed to increase the throughput gain (e.g., more precise power control)

## Slide 11: References
[1] IEEE 802.11-18/0191r0, 802.11 Full Duplex
[2] IEEE 802.11-18/0549r0, Full Duplex for 802.11
[3] IEEE 802.11-18/0448r1, Full Duplex Benefits and Challenges

## Slide 12: Appendix

## Slide 13
[2] IEEE 802.11-18/0549r0, Full Duplex for 802.11
With Full Duplex Echo Cancellation
Without Full Duplex
Echo Cancellation
Assumptions: 5GHz UNI-I, 4x4 MU-MIMO capable AP, 80MHz Channel Bandwidth, ZFBF receiver