## Slide 1: NGV Ranging Discussions
Date: 2018-07-08
Authors:

## Slide 2: Use Cases Related Ranging
Ranging measurement between cars (V2V):
  Find the range between cars when other technology is not applicable
Locationing of car (V2I):
  Find the car’s location when other technology is not applicable.
  Example: the “Urban canyon” scenario, where GPS is not available or not accurate.

## Slide 3: Recap: Ranging/Locationing in 802.11
11mc: FTM based ranging
  Multiple TXOPs for one ranging (one Action (FTM Request, FTM) and its acknowledgment in one TXOP)
  Applicable to associated/unassociated STAs
11az: NDP SU ranging
  At least Three TXOPs for one ranging (11az FTM Request + Ack, 11az FTM + Ack, UL NDPA + UL NDP + DL NDP + DL measurement feedback)
  Applicable to associated/unassociated STAs
11az: NDP MU ranging
  one negotiation + multiple MU NDP measurement where each measurement is in one TXOP
  Applicable to associated/unassociated STAs with one AP
11az: snoop-based ranging
  variant of NDP MU ranging
  Listening STAs need to decode Trigger frame

## Slide 4: Possible Enhancement for NGV Ranging
NDP based ranging
Decreasing the number of TXOPs for each non-snoop based ranging
Enabling decoding of Trigger for snoop-based NDP ranging
Either OCB based or BSS based MAC may be used for ranging.