## Slide 1: LMR AoA Feedback
Date: 2018-07-10
Authors:

## Slide 2: Background
Angular in Tgaz
  Subsection for sub 7 GHz angular removed from SFD
  Now only specific support for AoD/AoA in DMG/eDMG
Existing Angular
  Sub 7 GHz AoA already implemented using proprietary receive array processing
  Does not need specific protocol support
  Usually at APs, can be used in network-centric localization
  Would be beneficial also in client-centric localization
There is a need to share AoA Measurements from AP with STA
  RSTA-ISTA LMR is an obvious place to feed back per packet (NDP) AoA measurements

## Slide 3: AoA Feeback in LMR
Angle-of-Arrival (AoA)
  Can be measured on each NDP
  Could be fed back in LMR
Format
  2 octets Azimuth/Elevation
  Alternatively re-use AoA results field