## Slide 1: NGV Terminology
Date: 2018-07-12
Authors:

## Slide 2: Terminology
  Interoperability – IEEE802.11p devices to be able to decode at least one mode NGV transmissions, and NGV devices to be able to decode IEEE802.11p transmissions
  Co-existence – IEEE802.11p devices to be able to detect NGV transmissions (and hence defer from transmissions during NGV transmissions causing collisions) and vice versa
  Backward compatibility – Ability of NGV devices to operate in a mode in which they can interoperate with IEEE802.11p devices
  Fairness – Ability of IEEE802.11p devices to have the same opportunities as NGV devices to access the channel

## Slide 3: NGV Device Modes
TX: New PHY
11p device is aware of messages but can’t decode (coexistence)
TX: 11p messages
11p device decodes messages
(interoperate)
Mode transition
(backward compatibility)
RX: Both NGV and 11p messages

## Slide 4: NGV Transmit Mode Transitions
Transmit mode may change packet-by-packet
  Mode is determined according to transmitted service and discovery of IEEE802.11p vehicles registered to the service
  NGV device may use a different TX mode per service
  TX mode used for service may change dynamically according to IEEE802.11p discovery
Mode determination layer requires further study
  Service-aware layer (i.e. IEEE1609 in US; ETSI ITS-G5 in EU) for advertised services
  PHY layer (i.e. NGV) for non-advertised services

## Slide 5: Enhanced Interoperable Mode
NGV interoperable mode may be enhanced if interoperability is maintained
Transmitter | Receiver | Performance
11p | 11p | Baseline
NGV | 11p | At least as good as baseline
11p | NGV | At least as good as baseline
NGV @11p mode | NGV | Improved

## Slide 6: Backward Compatible Network
NGV
11p