## Slide 1: NGV SG Use Cases (Next Generation V2X Study Group)
Date: 2018-07-10
Authors:

## Slide 2: Revision History
Revison | Time | Note
r0 | Jul, 2018 | First baseline revision
r1 | Sep, 2018 | Add aerial vehicle ITS application
r2 | Nov, 2018 | Add two train related use cases

## Slide 3: Abstract
As part of the effort to develop a PAR and 5C for Next Generation V2X (NGV), this document collects the use cases that have been discussed in NGV SG.

## Slide 4: Context: Creation of NGV SG in IEEE 802.11
In May 2018, IEEE and the IEEE Standards Association (IEEE-SA), announced the formation a new study group focused on advancing the technology and deployment of the IEEE 802.11 standard, commonly referred to as “Wi-Fi®”, in Vehicular Environments. The study group is in its initial stage, encouraging stakeholder participation to define the scope of IEEE 802.11 standard amendments that address next generation V2X requirements.
The IEEE 802.11 Next Generation V2X (NGV) Study Group is exploring ways to leverage more recent 802.11 technologies to address new applications of wireless access in vehicular environments, where new requirements for higher throughput, improved reliability and efficiency, and/or extended range are anticipated.
For more information, please visit IEEE 802.11 Next Generation V2X (NGV) Study Group

## Slide 5: Terminology
  Interoperability – IEEE802.11p devices to be able to decode at least one mode transmission of NGV device, and NGV devices to be able to decode IEEE802.11p transmissions
  Co-existence – IEEE802.11p devices to be able to detect NGV transmissions (and hence defer from transmissions during NGV transmissions causing collisions) and vice versa
  Backward compatibility – Ability of NGV devices to operate in a mode in which they can interoperate with IEEE802.11p devices
  Fairness – Ability of IEEE802.11p devices to have the same opportunities as NGV devices to access the channel

## Slide 6: NGV Device Modes
TX: New PHY
11p device is aware of messages but can’t decode (coexistence)
TX: 11p messages
11p device decodes messages
(interoperate)
Mode transition
(backward compatibility)
RX: Both NGV and 11p messages

## Slide 7: Use Cases

## Slide 8: 1. Basic Safety Messages (BSM)
Overview: All vehicles periodically (typ. 10HZ) broadcast a message containing their basic information. Based on received messages, driver is alerted of an upcoming safety risk
  BSM are broadcasted on Channel 172 in US and Channel 180 in EU
Deployment timeline: IEEE802.11p solutions are deployed now. De-facto solution is applied to transmit diversity
Requirements:
  Antenna diversity (transmit and receive)
  Nice to have:
  Increasing IEEE802.11p range. Target would be 25% range increase over IEEE802.11p for urban intersection
Limitations:
  Full backward compatibility, able to transmit, decode and understand 11p messages
  Maintaining channel load
  Maintaining fairness

## Slide 9: 2. Sensor Sharing
Overview: Vehicles periodically broadcast all detected objects from all sensors, and receive objects from all other vehicles
  Sensor sharing message is under definition. Actual packet length is expected to be longer than BSM because many objects can be detected by many sensors
  The channel is yet to be determined
Deployment timeline: >2023 (expected)
Requirements:
  Packet NGV should carry higher number (>50%) of transmitted bytes than IEEE802.11p packet under same conditions (packet duration, PER, range, wireless channel)
Limitations:

## Slide 10: 3. Multi-Channel Operation
Overview: Concurrent multi-channel operation
  One channel is safety channel, and the second is non-safety. Non-safety channel may impact driving decisions (for example, truck platooning)
  Non-safety channel may be receive only (V2I) or transmit / receive (truck platooning or coordinated maneuvering, for example)
Deployment timeline:
  Now (V2V + V2I in most pilot deployments)
  >2019 (V2V + Truck platooning)
  >2023 (V2V + V2I in OEMs installations; expected)
  > 2025 (V2V + V2V; expected)
Requirements:
  High availability of safety channel
    Minimal same-vehicle cross-interference – blinding self-vehicle safety channel by non-safety channel transmissions
    Minimal cross-vehicles interference – blinding near-vehicle from receiving a safety message coming from a far vehicle
  High utilization of all channels
Limitations:

## Slide 11: 4. Infrastructure Applications
Overview: Transmission of safety and non-safety data from infrastructure to vehicles
  High amount of data can be received in a short time, for example, CRL database or potentially HD map
Deployment timeline: Now
Requirements:
  High throughput (Packet NGV should carry higher number (>50%) of transmitted bytes than IEEE802.11p packet under same conditions)
Limitations:
  Infrastructure should select usage of IEEE802.11p or NGV packet based on application and capabilities of vehicles in proximity
  Higher layer (e.g. IEEE1609) protocol should be defined for version negotiation (out of NGV scope)

## Slide 12: 5. Vehicular Positioning & Location
Overview:
  Positioning of the vehicle wrt other road-users:
    Radar technology is not always accurate, especially in case of pedestrians/bikes. Measure accurate distance to other road-users based on known antenna position.
  Locating and navigating the car in locations with no GPS coverage, i.e., parking lots or urban canyon.
Requirements:
  Positioning:
    0.3m LoS accuracy, 10Hz typical refresh rate, with or without orientation.
    V2V, V2I and V2P operation, with variable refresh rate.
  Location: 1-2m NLoS positioning accuracy, 10hz refresh rate.
Limitations:
  Higher accuracy is normally achieved via larger bandwidth which allow higher channel resolutions.

## Slide 13: 6. Automated Driving Assistance
Overview: Coordinated vehicle maneuvers
  Vehicle shares their future path and potentially adjusts it according to paths of vehicles in proximity
Deployment timeline: >2025 (expected)
Requirements:
  Multi-channel operation, maximizing availability of safety and Automated Driving channels
  Packet NGV should carry higher number (>50%) of transmitted bytes than IEEE802.11p packet under same conditions (packet duration, PER, range, wireless channel)
Limitations:

## Slide 14: 7. Aerial Vehicle ITS Application
Overview:
  Aerial Vehicles provide road safety and traffic violation monitoring functions with LoS connectivity
  Aerial Vehicles can be deployed flexibly and dynamically to control heavy traffic congestion
Requirements:
  Vehicle to X communication includes Aerial Vehicle to X
  High Throughput to provide traffic video information from Aerial Vehicles to Authorities (police officers)
  Multi-Channel operation
  Short packet transmission latency
Limitations:
  Maintaining channel load
  Priority control

## Slide 15: 8. Train-to-Train
Overview
  Safety critical and for efficient operation
  Autonomous train protection & operation (ATP/ATO): collision avoidance, remote control, automatic coupling and train integrity; virtual coupling (platooning)
Deployment time line >2030
Requirements
  For a relative speed of 500 km/h (with directional antennas 800 km/h) and distance of 2000 m, NGV provides at least a data rate of 1 Mbps, a ranging accuracy of 1% of distance, and latency of 10 ms as well as supports reliability (SIL2)

## Slide 16: 9. Vehicle-to-Train
Overview
  Safety critical and for efficient operation
  Shared space at level crossings, shared spectrum for 5.9 GHz ITS band between V2X and urban rail communications
Deployment time line >2020
Requirements
  For a relative speed of 500 km/h and a distance of 2000 m, NGV provides at least a data rate of 1 Mbps, a ranging accuracy between 5% and 10% of distance, and a latency of 100 ms, as well as supports reliability (SIL2)
Limitations
  Interference between V2X and T2X limited while enabling safe cooperation

## Slide 17: References