## Slide 1: Items for Completing the PAR
Date: 2018-09-07
Authors:

## Slide 2: Abstract
There are statements in the current PAR draft (11-18/0861r6) which should be improved before the PAR is sent for approval.
These include:
Several Missing Items
  Things which should be fixed now so that they do not become obstacles for the Task Group
An Ambiguous Item
  A statement that is open to misinterpretation, and can easily be clarified
Editorial Corrections
  Things where the intent is correct, but the current wording is incorrect or incomplete

## Slide 3: Persistence of the PAR
A Study Group exists to generate two documents – a PAR and a CSD
The CSD is a supporting document, listing the justification for why the Executive Committee should approve the PAR
The PAR remains relevant until the standard is published
  The PAR not only defines what the Task Group is required to accomplish
  The PAR also places limits on what the Task Group is permitted to accomplish
  If our draft contains features outside the scope of the PAR, we should expect to receive ballot comments calling for removal of those features
    Such comments are extremely difficult to overcome, especially in the current political climate
  Therefore, we need to ensure that our PAR has sufficient scope

## Slide 4: The Need To Support New Use Cases
There have been several submissions which propose new use cases
  And even statements that NGV is only justified if it enables use cases which are not feasible under the existing standard
Some of these new use cases, for example map download and sensor sharing, are only practical if there is a mechanism to provide substantially faster transfers, and larger payloads, than the current standard
  The 60 GHz band is a potential place to add such a mechanism
Several of these new use cases require positioning and/or ranging
It is unclear whether these sorts of new use cases can be met under the current draft PAR
  It is better to modify the PAR now, than to risk being unable to include things later

## Slide 5: Three Items Missing in the Current Draft PAR
The ability to define V2X communication in the 60 GHz band
  Several of the proposed use cases require much more than doubling of available throughput
  The 60 GHz band has no interoperability constraints for V2X
  The first submission on using this band received a majority in a straw poll (31-25-21)
    Meaning there is interest, although not consensus, so further consideration should be allowed
The ability to define the use of 802.11 positioning for V2X communication
  Several of the proposed use cases require a positioning mechanism
  Extending 802.11 positioning mechanism(s) for OCB usage needs to be defined
A full statement of the backward compatibility constraints
  A set of definitions from document 11-18/1307r1 pertaining to compatibility between 802.11p and NGV were broadly supported in a straw during the July meeting (26-2)
  Only one of the four defined terms appears in the draft PAR
    Because 11-18/1307r1 was presented two days after the vote on the draft PAR in July

## Slide 6: Proposed Additions to the Project Scope (5.2.b)
This amendment defines modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) for vehicle to everything (V2X) communications for 5.9 GHz band as defined in clauses E.2.3 and E.2.4 of IEEE Std 802.11™-2016; and, optionally, in the 60 GHz frequency band (57 GHz to 66 GHz) as defined in clause E.1.
This amendment defines at least one mode that achieves at least 2 times higher throughput (measured at the MAC data service access point) than as in IEEE Std 802.11™-2016 operating at maximum mandatory MCS as defined in the 5.9GHz band (12 Mbps), in high mobility channel environments at speeds up to 250 km/h; this amendment also defines at least one mode that achieves at least 3dB lower sensitivity level (longer range), than that of the lowest rate defined in IEEE Std 802.11™-2016 operating in 5.9 GHz band; and this amendment defines procedures for at least one form of positioning in conjunction with vehicle to everything (V2X) communications.
This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.

## Slide 7: An Ambiguous Item
There are two possible interpretations of the phrase “… in high mobility channel environments at speeds up to 250 km/h”
  One interpretation is that this refers to the maximum speed which has to be handled. This interpretation implicitly limits individual vehicle speeds (for V2V) to 125 km/h
  The other interpretation is that this refers to the maximum speed of each vehicle, hence requires the PHY to handle closing speeds up to 500 km/h
Interpretation (1) is clearly inadequate for an NGV standard, as there are numerous highways where the legal speed limit exceeds 125 km/h
  For example, the posted speed limit for Texas Highway 130 is 85 miles/h (136.8 km/h) and for all of the interstate highways in west Texas is 80 miles/h (128.7 km/h)

## Slide 8: Proposed Clarification of the Project Scope (5.2.b)
This amendment defines modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) for vehicle to everything (V2X) communications for 5.9GHz band as defined in clauses E.2.3 and E.2.4 of IEEE Std 802.11™-2016; and, optionally, in the 60 GHz frequency band (57-66 GHz) as defined in clause E.1.
This amendment defines at least one mode that achieves at least 2 times higher throughput (measured at the MAC data service access point) than as in IEEE Std 802.11™-2016 operating at maximum mandatory MCS as defined in the 5.9GHz band (12 Mbps), in high mobility channel environments at vehicle speeds up to 250 km/h (closing speeds up to 500 km/h); this amendment also defines at least one mode that achieves at least 3dB lower sensitivity level (longer range), than that of the lowest rate defined in IEEE Std 802.11™-2016 operating in 5.9 GHz band; and this amendment defines procedures for at least one form of positioning in conjunction with vehicle to everything (V2X) communications.
This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.

## Slide 9: Some Editorial Corrections
Incorrect use of “MCS”
  It is incorrect to say “maximum mandatory MCS” because, for 802.11p, the acronym “MCS” does not apply.
  While “MCS” has been used in submissions since 2004, and standards since 802.11n-2009, the references in 802.11p-2010, and incorporated into 802.11-2012 and 802.11-2016, are to the OFDM PHY (e.g. 802.11a) in Clause 17, where term is “data rates” rather than “MCS”. Therefore, the proper phrasing is “maximum mandatory data rate”.
Incorrect use of “Mbps” – the data rates in 802.11-2016 use “Mb/s”
Missing statement of the channel width to which the data rates pertain
  The 12 Mb/s & 3 Mb/s rates are for 10 MHz channels, but there are also 20 MHz and 5 MHz
Confusing reference to the origin of vehicular provisions in 802.11
  Clause 5.5 states that WAVE technology is based on 802.11-2016, derived from 802.11a-1999, but goes on to state that WAVE technology has been available for “almost a decade”.
  There should be mention of 802.11p-2010, which is what “almost a decade” is referring to.

## Slide 10: Editorial Corrections to the Project Scope (5.2.b)
This amendment defines modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) for vehicle to everything (V2X) communications for 5.9GHz band as defined in clauses E.2.3 and E.2.4 of IEEE Std 802.11™-2016; and, optionally, in the 60 GHz frequency band (57-66 GHz) as defined in clause E.1.
This amendment defines at least one mode that achieves at least 2 times higher throughput (measured at the MAC data service access point) than as in IEEE Std 802.11™-2016 operating at the maximum mandatory data rate as defined in the 5.9GHz band (12 Mb/s in a 10 MHz channel), in high mobility channel environments at speeds up to 250 km/h; this amendment also defines at least one mode that achieves at least 3dB lower sensitivity level (longer range), than that of the lowest data rate defined in IEEE Std 802.11™-2016 operating in 5.9 GHz band (3 Mb/s in a 10 MHz channel); and this amendment defines procedures for at least one form of positioning in conjunction with vehicle to everything (V2X) communications.
This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.

## Slide 11: Editorial Corrections to the Need for the Project (5.5)
Current IEEE 802.11 wireless access in vehicular environments (WAVE) technology for V2X applications is based on IEEE Std 802.11™-2016 operating in 5.9GHz band, which was originally standardized as IEEE Std 802.11p™-2010, and which was, in turn, based on the OFDM PHY as defined in clause 17 of IEEE Std 802.11™-2016 (a.k.a. IEEE Std 802.11a™ -1999). WAVE technology has been available for almost a decade, and has been extensively tested and is a proven, mature technology.
During the past decade, IEEE 802.11 technology has improved, from the IEEE Std 80211a™-2009, to IEEE Std 802.11n™-2009, IEEE Std 802.11ac™-2013 and the ongoing IEEE P802.11ax™ amendment, with supported throughput increasing from 54 Mbps to close to 10 Gbps, as well as higher reliability and improved range. To address future needs for V2X communication technology and provide 802.11-based future-proof technology for V2X applications, the definition of new V2X mechanisms based on new and existing, proven IEEE 802.11 WLAN PHY/MAC technologies, are needed.

## Slide 12: Straw Poll 1
Do you favor extending the scope of the PAR to permit NGV to define V2X communication in the 60 GHz band?
Yes: 33
No: 6
Abstain: 3

## Slide 13: Straw Poll 2
Do you favor extending the scope of the PAR to permit NGV to define V2X positioning and/or ranging?
Yes: 23
No: 2
Abstain: 13

## Slide 14: Straw Poll 3
Do you favor having the PAR contain all four of the terms related to interoperability for NGV as presented in 11-18/1307?
Yes: 18
No: 2
Abstain: 13

## Slide 15: Straw Poll 4
Do you favor having an unambiguous statement of the high mobility speed requirement in the PAR?
Yes: 39
No: 0
Abstain: 3