## Slide 1: PAPR Investigation on FDMA Transmission Follow-up
Date: 2018-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], we studied phase rotation and PAPR for both legacy and WUR portions in the FDMA transmission
In this contribution, we propose phase rotation values which are applied to 20MHz sub-channels for the WUR portion in 40MHz and 80MHz FDMA transmissions
To this end, we further investigate the PAPR by considering three example sequences for the construction of 2us and 4us MC-OOK On symbols

## Slide 3: Assumption (1/2)
For 40MHz, we investigate PAPR for the full allocation case only, i.e., all sub-channels are allocated to the WUR PPDU transmission
For 80MHz, we consider the preamble puncturing mode
  There are various partial allocation cases as well as the full allocation case (2^4 cases)
  To obtain optimal phase rotation values, the minimax approach is applied, i.e., we first calculate the PAPR for all of the allocation cases by applying a certain phase rotation, choose the maximum PAPR among all allocation cases in that phase rotation, then repeat this procedure in other candidates of the phase rotation and finally compare those maximum PAPRs
  E.g., K allocation cases and L phase rotation candidates
PAPR for allocation case 1
PAPR for allocation case 2
PAPR for allocation case K
Phase rotation 1
…
…
Choose max PAPR
PAPR for allocation case 1
PAPR for allocation case 2
PAPR for allocation case K
Phase rotation L
…
Choose max PAPR
PAPR for allocation case 1
PAPR for allocation case 2
PAPR for allocation case K
Phase rotation 2
…
Choose max PAPR
Compare these PAPR and pick up the best phase rotation which minimizes the max PAPR

## Slide 4: Assumption (2/2)
To calculate the PAPR in each allocation case, we consider all ‘ON’ and ‘OFF’ combinations of sub-channels allotted to the WUR FDMA transmission
  The WUR PPDU structure used for the PAPR calculation is shown in Appendix A
The same OOK symbol length is used, i.e., all sub-channels are composed of either 2us or 4us OOK symbol
  When all sub-channels use the same data rate, we can consider all sub-channels are composed of either 2us or 4us OOK symbol for HDR or LDR, respectively
  When different data rates are used in sub-channels, we can consider all sub-channels consist of 2us OOK symbol, i.e., 4us OOK symbol for LDR is constructed by two consecutive 2us OOK symbols used for HDR

## Slide 5: Phase Rotation and PAPR for 40MHz (1/3)
4us On symbol
  Sequence Option 1 : [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
  Sequence Option 2 : [-9-5i -7+9i -1+1i 9+15i 15-9i -9+1i 0 1-9i 9-15i 15+9i -1+1i 9-7i 5+9i]/sqrt(170)
  Sequence Option 3 : [1 -1 1 -1 -1 1 0 -1 -1 1 1 1 1](1+1i)
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 8.0812 | 8.0231 | 8.0734 | 8.0761
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 7.0920 | 7.1939 | 7.1505 | 7.1724
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 8.2583 | 8.1696 | 8.2590 | 8.2563
Red: optimal phase rotation
Note : We assume 1, -1, j and –j as the coefficient of phase rotation and thus, in 40MHz, when the first coefficient is set to 1, there are only 4 candidates for phase rotation

## Slide 6: Phase Rotation and PAPR for 40MHz (2/3)
2us On symbol
  Sequence Option 1 : [1 0 1 0 1 0 0 0 -1 0 1 0 -1]
  Sequence Option 2 : [3+7i 0 1+15i 0 -5+13i 0 0 0 13-5i 0 -15-1i 0 7+3i]/sqrt(170)
  Sequence Option 3 : [1 0 1 0 -1 0 0 0 -1 0 -1 0 1]
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 8.2509 | 8.1682 | 8.2585 | 8.2581
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 6.5955 | 6.6416 | 6.6366 | 6.6044
Phase rotation | {1 1} | {1 -1} | {1 j} | {1 –j}
PAPR | 9.3301 | 9.3934 | 9.4167 | 9.4171
Red: optimal phase rotation

## Slide 7: Phase Rotation and PAPR for 40MHz (3/3)
In each sequence option, the difference in PAPR among all phase rotation candidates is quite small, even though either the phase rotation of {1 -1} or {1 1} is optimal in terms of PAPR
All of the PAPRs are also lower than the worst PAPR of the L-SIG shown in Appendix B
  L-SIG may have the highest PAPR in the WUR PPDU
Thus, in consideration of a simple implementation, the unified phase rotation between legacy and WUR parts is more preferable
The phase rotation {1 j} used for 11ac in 40MHz can be applied to the legacy preamble and we also propose to use this value for the WUR part

## Slide 8: Phase Rotation and PAPR for 80MHz (1/3)
4us On symbol
  Sequence Option 1 : [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
  Sequence Option 2 : [-9-5i -7+9i -1+1i 9+15i 15-9i -9+1i 0 1-9i 9-15i 15+9i -1+1i 9-7i 5+9i]/sqrt(170)
  Sequence Option 3 : [1 -1 1 -1 -1 1 0 -1 -1 1 1 1 1](1+1i)
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 11.0912 | 8.7850 | 8.7990 | 9.8415
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 10.1024 | 7.9045 | 7.8790 | 8.9549
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 11.2689 | 8.9642 | 8.9865 | 10.0197
Red: optimal phase rotation
Green: second best thing among four cases
Note : In 80MHz, there are 4^3 candidates for phase rotation when the first coefficient is set to 1, but we just show the results of four candidates including optimal and conventional ones as well as no phase rotation case

## Slide 9: Phase Rotation and PAPR for 80MHz (2/3)
2us On symbol
  Sequence Option 1 : [1 0 1 0 1 0 0 0 -1 0 1 0 -1]
  Sequence Option 2 : [3+7i 0 1+15i 0 -5+13i 0 0 0 13-5i 0 -15-1i 0 7+3i]/sqrt(170)
  Sequence Option 3 : [1 0 1 0 -1 0 0 0 -1 0 -1 0 1]
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 11.2612 | 8.9644 | 8.9851 | 10.0119
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 9.6052 | 7.3620 | 7.3496 | 8.4021
Phase rotation | {1 1 1 1} | {1 -1 -1 1} | {1 1 -1 -1} | {1 -1 -1 -1}
Max PAPR | 12.3404 | 10.1407 | 10.1253 | 11.1543
Red: optimal phase rotation
Green: second best thing among four cases

## Slide 10: Phase Rotation and PAPR for 80MHz (3/3)
In each sequence option, either the phase rotation of {1 -1 -1 1} or {1 1 -1 -1} is optimal in terms of PAPR and these values even have a similar PAPR
The conventional phase rotation {1 -1 -1 -1} also still has better PAPR than the worst PAPR of the L-SIG given in Appendix B but leads to much higher PAPR than those of the phase rotation values above
  Its PAPR is over 1dB worse than the optimal one in all options
For a simple implementation and unified solution, the conventional phase rotation {1 -1 -1 -1} can be applied, but in consideration of hardware efficiency, the phase rotation of {1 -1 -1 1} or {1 1 -1 -1} is more preferable

## Slide 11: Conclusion
We have investigated the PAPR and proposed phase rotation values for the WUR part in WUR FDMA
For 40MHz, we have proposed to use the conventional phase rotation {1 j}
For 80MHz, we have proposed to use {1 -1 -1 1} or {1 1 -1 -1}

## Slide 12: Straw Poll #1
Do you agree to use the phase rotation of [1 j] for the WUR portion encompassing WUR-Sync and WUR-Data fields in the 40MHz FDMA transmission?
Y/N/A : //

## Slide 13: Straw Poll #2
Do you agree to use the phase rotation of [1 -1 -1 1] or [1 1 -1 -1] for the WUR portion encompassing WUR-Sync and WUR-Data fields in the 80MHz FDMA transmission?
Y/N/A : //

## Slide 14: References
[1] IEEE 802.11-18/0802r1 PAPR Investigation on FDMA Transmission

## Slide 15: Appendix A – PAPR for WUR Portion
In 40MHz, to calculate the PAPR, we consider that the PPDU is composed of 4 ‘ON’ and ‘OFF’ combinations as follows
  If each ‘ON’ and ‘OFF’ combination occurs almost evenly in a practical WUR PPDU, this PPDU format may be reasonable for the PAPR calculation
  PAPR is calculated by applying each candidate of phase rotation
In 80MHz with the full allocation case, we consider that the PPDU is composed of 16 ‘ON’ and ‘OFF’ combinations
Sub-channel 1
Sub-channel 2
2us 4us 6us 8us for 7 length sequence
4us 8us 12us 14us for 13 length sequence
OFF ON ON OFF
ON OFF ON OFF
PAPR is measured by applying each candidate of phase rotation

## Slide 16: Appendix A – PAPR for WUR Portion
In 80MHz with the partial allocation case, we consider that the PPDU is composed of 2^n ‘ON’ and ‘OFF’ combinations
  n is the number of allocated sub-channels for the FDMA transmission
  E.g., Partial allocation with sub-channel 3 punctured in 80MHz

## Slide 17: Appendix B – PAPR for Legacy Preamble
Conventional phase rotation values are applied to the legacy preamble part
PAPR for L-STF and L-LTF [dB]
 | PAPR for 40MHz | Max PAPR for 80MHz
L-STF | 5.2497 | 6.8606
L-LTF | 5.7938 | 7.9370

## Slide 18: Appendix B – PAPR for Legacy Preamble
PAPR for L-SIG [dB]
  Following cases are considered for the PPDU length
Definition of case |  | L_length (octets) | Definition of case |  | L_length (octets) | Definition of case |  | L_length (octets)
case0 | FB=0, HDR | 192 | case6 | FB=6, HDR | 336 | Case12 | FB=12, HDR | 480
case1 | FB=0, LDR | 672 | case7 | FB=6, LDR | 1248 | Case13 | FB=12, LDR | 1824
case2 | FB=2, HDR | 240 | case8 | FB=8, HDR | 384 | Case14 | FB=14, HDR | 528
case3 | FB=2, LDR | 864 | case9 | FB=8, LDR | 1440 | Case15 | FB=14, LDR | 2016
case4 | FB=4, HDR | 288 | case10 | FB=10, HDR | 432 | Case16 | FB=16, HDR | 576
case5 | FB=4, LDR | 1056 | case11 | FB=10, LDR | 1632 | case17 | FB=16, LDR | 2208

## Slide 19: Appendix B – PAPR for Legacy Preamble
PAPR for L-SIG [dB]
 | PAPR for 40MHz | Max* PAPR for 80MHz |  | PAPR for 40MHz | Max* PAPR for 80MHz
Case 0 | 8.1208 | 12.0197 | Case 9 | 8.2288 | 12.3542
Case 1 | 9.7488 | 12.5525 | Case 10 | 8.6453 | 12.3543
Case 2 | 8.3897 | 12.3780 | Case 11 | 9.0901 | 12.3879
Case 3 | 7.6770 | 12.4025 | Case 12 | 8.6271 | 12.3233
Case 4 | 9.5330 | 12.3854 | Case 13 | 8.3736 | 12.7781
Case 5 | 8.1310 | 12.9298 | Case 14 | 8.6528 | 12.3494
Case 6 | 8.2794 | 12.3880 | Case 15 | 9.5472 | 12.3999
Case 7 | 8.2987 | 12.3392 | Case 16 | 9.1345 | 12.4066
Case 8 | 9.9882 | 12.3140 | Case 17 | 8.5720 | 12.4062
Red: maximum PAPR among all L_Length cases
Max PAPR for 80MHz : In each L_Length case for 80MHz, the table shows only the maximum PAPR among those of all allocation cases including full and partial allocation cases