## Slide 1: Overview of 802.11 ba Power Management in D0.4
Date: 2018-09-10
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Minyoung Park |  |  |  | 
Shahrnaz Azizi |  |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Ming Gan | Huawei |  |  | 
Suhwook Kim | LG |  |  | 
Lei Huang | Panasonic |  |  | 

## Slide 2: Abstract
This presentation explains the 802.11 ba power management in D0.4 and attempts to help people not involved in 11ba discussion understand the design.
11ba develops independent WUR negotiation status to enable WUR functionality and has no changes to transition rules between PS mode and Active mode currently defined for the PCR component.

## Slide 3: Existing 802.11 Power Management
  Two power states are defined for PCR
    Awake: STA is fully powered.
    Doze: STA is not able to transmit or receive and consumes very low power.
    See 11.2.1 General [1]
  Two power management modes are defined for non-AP STA:
    Active mode: The STA receives and transmits frames at any time. The STA remains in the awake state.
    Power save (PS) mode: The STA enters the awake state to receive or transmit frames. The STA remains in the doze state otherwise.
    See 11.2.3.2 Non-AP STA power management modes [1]

## Slide 4: High Level State Diagram for Existing 802.11 Power Management
Power Management Mode Diagram
  See 11.2.3.2 Non-AP STA power management modes [1]
  Note that the frame with PM bit solicits an immediate acknowledgement
Under PS Mode, Power State Diagram for PCR component
  See 10.48 Target wake time (TWT) [1] and 27.7 TWT operation for TWT [2] See 11.2.3.7 (Receive operation for STAs in PS mode) [1] for Ps-Poll and U-APSD
Active Mode
Frame exchange with PM bit set to 1.
Frame exchange with PM bit set to 0.
PS Mode
Awake
Transition based on power save protocol like TWT, Ps-Poll, U-APSD
Doze

## Slide 5: 802.11 ba Power Management – Design Concept
For non-AP STA, 802.11 ba adds a companion radio called WURx (WUR receiver) to receive WUR PPDU
To differentiate WURx with the PCR, the PCR of the non-AP STA is described as the PCR component of the non-AP STA
Additional power state for the companion radio, which are separated from the power states of PCR component, are defined
  WURx Awake: the WURx of the WUR non-AP STA is fully powered to receive WUR frame.
  WURx Doze: the WURx of the WUR non-AP STA is not able to receive WUR frame.
  See 31.6.2 non-AP STA operation
Independent WUR negotiation status is added to enable the WURx when power state of the PCR component of a non-AP STA is in the doze state and the PCR component has negotiated WUR Mode.
Active Mode
PS Mode
WUR Mode
WUR Mode Suspend
No WUR Negotiation

## Slide 6: 802.11 ba Power Management – Negotiation Status
The definition of 802.11 ba negotiation status is as follows to enable WURx when the non-AP STA’s power state of the PCR component is in the doze state
  WUR Mode status:
    AP and non-AP STA remember WUR negotiated parameters
    WURx is available based on duty cycle agreement when the PCR component of the non-AP STA is in doze state
    Additional rules on avoiding checking DTIM and is not required to awake in SPs
    See 31.6.2 non-AP STA operation and 31.6.3 AP operation [3]
  WUR Mode Suspend status:
    AP and non-AP STA remembers WUR negotiated parameters
    WURx power state is implementation specific
    No change for the existing rules of checking DTIM and awake in SPs
    See 31.6.2 non-AP STA operation and 31.6.3 AP operation [3]

## Slide 7: 802.11 ba Power Management – High level State Diagram for Negotiation Status
See 31.6.1 WUR Mode Setup [3] for all the details
Note that WUR Mode Setup frame and WUR Mode Teardown frame are WUR Action frame
Note that this state diagram is independent of Active mode/PS mode state diagram
WUR Mode
WUR Mode Suspend
No WUR Negotiation
WUR Mode Setup frame Request/Response exchange
WUR Mode Setup frame Request/Response exchange
WUR Mode Teardown frame
WUR Mode Teardown frame
WUR Mode Setup frame (Action Type field = Enter WUR Mode Suspend)
WUR Mode Setup frame (Action Type field = Enter WUR Mode)

## Slide 8: 802.11 ba Power Management – High level WURx Power State Diagram
After PCR component negotiates WUR Mode and the power state of the PCR component of the non-AP STA is in the doze state, transition between WURx Awake and WURx Doze is based on the WURx duty cycle agreement
  See 31.6.2 non-AP STA operation [3]
After PCR component negotiates WUR Suspend mode or the power state of the PCR component of the non-AP STA is in the Awake state or the non-AP STA is not associated, transition between WURx Awake and WURx Doze is implementation specific
  See 31.6.2 non-AP STA operation [3]
WURx Awake
Transition based on WURx duty cycle agreement
WURx Doze
WURx Awake
Implementation specific
WURx Doze

## Slide 9: Reference
[1] Draft P802.11REVmd D1.4
[2] Draft P802.11ax D3.1
[3] Draft P802.11ba D0.4