## Slide 1: EHT features for Multi-Band Operation
Date: 2018-09-06
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com
Insun Jang | LG Electronics |  | insun.jang@lge.com
Kiseon Ryu | LG Electronics |  | kiseon.ryu@lge.com
Suhwook Kim | LG Electronics |  | suhwook.kim@lge.com
HanGyu Cho | LG Electronics |  | hg.cho@lge.com

## Slide 2: Introduction
In the last meeting, [1] proposed some candidate features for improving efficiency in Wi-Fi system
  E.g., Flexible DL/UL, Scheduled channel access in 6GHz, etc.
In this contribution we introduce some operations for supporting those features

## Slide 3: Full Duplex over Multi-Band (1/4)
Recap of [1]: Full duplex over multi-band (FD-MB)(as called Flexible DL/UL in [1]) will be an candidate of multi-band operations for enhancing the efficiency
  AP can send/receive a frame to/from a STA via a band while the AP receives/sends a frame from/to another STA via another band
A band specific primary channel (BSPC) concept will be suitable for this operation
  e.g., one primary channel per band in multi-bands (see the next slide for details)
For more efficiency, a band can also be aggregated with another band when both bands are available (i.e., the channels are idle)
The channel access mechanism for multi-band operation has to be designed efficiently for supporting FD-MB as well as multi-band aggregation
DL to STA1
DL to STA 2
ACK
ACK
UL from STA1
ACK
DL
UL
DL
UL
Band1
Band2
AP↔STA1
AP↔STA2&3
DL to STA 3
ACK

## Slide 4: Full Duplex over Multi-Band (2/4)
Band Specific Primary Channel (BSPC)
  An EHT AP supporting the multiple bands has one primary channel per band called a Band Specific Primary Channel (BSPC)
  The AP can send a Beacon frame carrying the BSS parameters of the band via the BSPC to help STAs find the AP
  For FD-MB operation, independent back-off timer will work in each BSPC
    A frame TX starts via idle channels in the band when the corresponding BO timer becomes 0
      Note that a secondary channel is considered idle when the channel is idle during PIFS prior to the frame in legacy system
Band A
PCH
SCH(s)
Band B
PCH
SCH(s)
DL/UL frame (STA1)
DL/UL frame
(STA2)
PIFS
OBSS interference

## Slide 5: Full Duplex over Multi-Band (3/4)
For multi-band aggregation, AP may regard a BSPC with backoff timer (non-zero value) as a secondary channel
  E.g., when a backoff timer of a BSPC(A) is 0 and that of another BSPC (B) is not 0, if BSPC (B) is idle during a certain period (e.g., PIFS/AIFS), idle channels in the band (B) can be aggregated with idle channels in the band (A)
It’ll result in the peak throughput of AP
It might be useful for the specific band (e.g., 6GHz where the EDCA can be restricted)
Band A
(e.g., 5GHz)
PCH
SCH(s)
Band B
(e.g., 6GHz)
PCH
SCH(s)
DL frame (STA1)
DL Frame (STA2)
PIFS
OBSS interference
PIFS

## Slide 6: Full Duplex over Multi-Band (4/4)
An non-AP STA can also have multi-band capability and perform the FD-MB operation or multi-band aggregation
It will increase not only the resource efficiency but also the peak throughput of a STA although it increases the complexity of the STA
UL aggregation for a STA may also be considered
Band A
PCH
SCH(s)
Band B
PCH
SCH(s)
DL frame (STA1)
PIFS
Interference
PIFS
DL Frame (STA1)
DL frame (STA1)
UL frame
(STA1)
PIFS
Interference

## Slide 7: Scheduled Channel Access in 6GHz (1/3)
At the last meeting, [1] suggested 6GHz specific channel access method (i.e., scheduled only) for more resource efficiency
  In this case, STA can send a frame to AP only by AP’s controlling (Trigger frame)
In 6GHz, HE STAs are only legacy STAs in Wi-Fi
  HE AP might also restrict the EDCA access of HE STAs in 6GHz but it hasn’t been decided yet [2]
In this case UL efficiency depends on the smart AP controlling
If an AP triggers a STA without the enough information of the STA, the allocated resource may be wasted
  E.g., when the AP allocates UL resource to the STA, if the allocated RU is considered as busy, the STA can not use the resource
Therefore, AP need to know the information of the scheduled STAs as much as possible before the UL(as well as DL) scheduling

## Slide 8: Scheduled Channel Access in 6GHz (2/3)
Information in legacy system
  In legacy STA can report Buffer status information (BSR) or available bandwidth information (BQR) to the AP
  AP uses them for deciding the resource size/location or PPDU length
  Bandwidth information (BQR): for the size and location of the resource
    Newly defined in 11ax , based on only the result of physical CS
Information in EHT
  STA with multi-band capability can report to AP the information of 6GHz through 2.4/5GHz as fast as possible
  Channel status(e.g., Virtual CS)
    Based on the received NAV, AP doesn’t schedule the STA in 6GHz during the NAV
  Channel quality (e.g., RSSI)
    STA can report to AP its channel quality information of 6GHz via 2.4/5GHz additionally
    AP can use the received information before sending DL frame in 6GHz

## Slide 9: Scheduled Channel Access in 6GHz (3/3)
Example (NAV)
  AP does not allocate the UL resource to the STA1 in 6GHz until the NAV ends
  Instead of it, the AP can assign the UL resource to the STA1 in 2.4/5GHz
The information could also be used for improving more average throughput in the scheduled channel access environment together with EDCA operation
6GHz
band
2.4/5 GHz
band
STA1
6GHz
band
2.4/5 GHz
band
AP
NAV
Not schedule the STA1 in 6GHz
Trigger
UL frame
6GHz NAV

## Slide 10: Discussion
The multi-band operation can be more effectively designed
  Candidate features: Full Duplex over Multi-Band
    Need the specific multi-band rule (e.g., band specific primary channel concept, channel access rule for band aggregation)
For more efficient 6GHz operation,
  Candidate features: Scheduled channel access
    Need to know more STA’s information (e.g., NAV, RSSI) for better efficiency
We propose to add the objective related to the improvement of the average throughput per STA to the scope of the PAR

## Slide 11: Conclusion
We need to consider the following operations for enhancing the average throughput (or efficiency)
  For full duplex over multi-band: Band specific primary channel concept (one primary channel per band), Channel aggregation rule
  For scheduled channel access in 6GH: More STA Information (e.g., NAV, RSSI)
    STA with multi-band capability can report the NAV of a band through another band

## Slide 12: Reference
[1] 11-18-1171-00-0eht-view-on-eht-objectives-and-technologies
[2] 11-18-1211-00-00ax-mac-cr-subclause-27-16-1