## Slide 1: Railway Use Cases for NGV
Date: 2018-11-12
Authors:

## Slide 2: Abstract
Railway use cases also relevant to NGV besides road vehicle use cases:
Use Case 1: Onboard Train
  Wireless train control and monitoring system (TCMS), operator oriented services, customer services (passenger information services, connection to mobile hot spot for public internet)
Use Case 2: Train-to-Train
  Autonomous train protection & operation (ATP/ATO): collision avoidance, remote control, automatic coupling and train integrity; virtual coupling (platooning)
Use Case 3: Train-to-Trackside
  Signaling, operator oriented services, customer services (passenger information, …)
Use Case 4: Vehicle-to-Train
  Shared space in level crossings & shared spectrum

## Slide 3: Why Railways?
Definition of vehicle [1]:
A vehicle is a machine that transports people or cargo. Vehicles include
wagons, bicycles, motor vehicles (motorcycles, cars, trucks, buses),
railed vehicles (trains, trams),
watercraft (ships, boats),
amphibious vehicles (screw-propelled vehicle, hovercraft),
aircraft (airplanes, helicopters) and spacecraft.

## Slide 4: Why Railways?
Current situation in road traffic:
Very efficient use of roads
EU: 75% of freight, 82% of passengers
Many accidents, traffic jams, less energy efficient
Current situation in railways:
Very safe and energy efficient
EU: 18% of freight, 8% of passengers
Inefficient use of railways due to old and national safety system
[2]
[3]

## Slide 5: Why Railways?
Current situation in road traffic:
Large Market: 1.3 billion motor vehicles, 1.35 trillion $ trade (2015)
Current situation in railways:
Small Market: 6.2 million rail vehicles, without freight cars only 0.7 million, 167 billion $ (2015)
[2]
[3]
Society and politics: Shift traffic from road to rail [4]
 Need for highly efficient and safe railway operation with less infrastructure
 Reliable low-latency communications and ranging essential

## Slide 6: Railway terms
Rail vehicle: Wagon, railcar, locomotive, …
Consist: a single vehicle or a group of vehicles that cannot be uncoupled
Train: composition of one or a set of consists or rail vehicles that can be operated as an autonomous unit

## Slide 7: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) state-of-the-art [5][6]
  Inside rail vehicle or consist: Multifunction vehicle bus (MVB) or Ethernet consist network (ECN)
  Connecting multiple vehicles: wired train bus (WTB) or ethernet train backbone (ETB)
  Between consists or wagons mechanical and electrical couplers
Mechanical coupler
Electrical coupler
[7]

## Slide 8: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) state-of-the-art [5][6]
Mechanical coupler
Electrical coupler
Mechanical stress at coupler
leads to many connection failures!
[7]

## Slide 9: Use Case 1: Onboard Train
Wireless Train Control and Monitoring System (TCMS) [5][6]
[7]
[7]

## Slide 10: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) Data classes [6]:
    Process data= small dimension data (byte or bit) that are sent periodically [8]
    Message data= differ from process data for bigger size and not sent periodically [8]
    Supervisory data= as message data, not periodically, used for supervision and inauguration process [8]
    Stream data= big amount of data sent continuously
    Best Effort data= data rate and delivery time depend on traffic load

## Slide 11: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) [6]: Key performance attributes: Inside consist

## Slide 12: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) [6]: Key performance attributes: Inside train

## Slide 13: Use Case 1: Onboard Train
Train Control and Monitoring System (TCMS) [6]:
  Required bandwidth ~ 100 Mb/s in one train
  30 years innovation cycle
Operator oriented services
  Improve operational parameters of train, e.g. maintenance costs, vehicle availability, closed circuit television (CCTV)
  Required bandwidth ~ 1-10 Gb/s in one train
  10 years innovation cycle
Customer services
  Passenger comfort, e.g. public internet, passenger info portal; customer’s own devices, WiFi
  Required bandwidth ~ 1-10 Gb/s in one train
  5 years innovation cycle

## Slide 14: Use Case 1: Onboard Train
Overview
  Safety critical and for efficient operation
  Wireless train control and monitoring system (TCMS)
  Operator oriented services (CCTV, maintenance)
Deployment time line >2025
Requirements
  For a speed of 400 km/h and distance of 500m, NGV provides at least a data rate of 100 Mbps and latency of 1 ms and supports reliability (SIL2/3)
Limitations
  Communication range “onboard” train to avoid interference with other trains

## Slide 15: Use Case 2: Train-to-Train Enabling Future Applications
Collision avoidance [9]
Remote control, automatic coupling and train integrity [10]
Virtual coupling: Platooning [11]
Autonomous train protection & operation (ATP/ATO)

## Slide 16: Use Case 2: Train-to-Train Enabling Future Applications
Autonomous train protection & operation (ATO): Collision avoidance [9]
150 bit message

## Slide 17: Use Case 2: Train-to-Train Enabling Future Applications
Autonomous train operation (ATO): Collision avoidance [9]
150 bit message (excl. authentication and encryption)
Dense train station /shunting yard: 200 static & 25 moving trains, update rates 0.2 Hz static & 1 Hz moving train  Minimum message rate = 200 ∙ 0.2 Hz + 25 ∙ 1 Hz = 65 Hz
System data rate = 150 bit ∙ 65 Hz = 9.75 kbit/s
Communication range 5 km for 2 km breaking distance of train @ 200 km/h (~125 mph)
Sufficient for informing train driver as safety-overlay in addition to other safety measures
 Higher rates needed to include authentication and encryption also for stand alone system or autonomous operations

## Slide 18: Use Case 2: Train-to-Train Enabling Future Applications
1% of the distance accuracy threshold
Autonomous train operation (ATO): Remote control, automatic coupling and train integrity [10]
Communication and ranging for control
Ranging accuracy 1% of actual distance
6-sigma of Cramér–Rao lower bound (CRLB)
ITS-G5 (802.11p, 10 MHz), IR-UWB and mm-Wave (both 500 MHz bandwidth)

## Slide 19: Use Case 2: Train-to-Train Enabling Future Applications
Virtual coupling: Platooning [12]
Demonstration at Innotrans 2018 by Siemens, Bombardier, CAF
[11]

## Slide 20: Use Case 2: Train-to-Train Enabling Future Applications
Virtual coupling: Platooning [12]
Trains per platoon: 3/6/18 in rural/suburban/urban
Message rate 10 Hz
Message size 167 bytes
13.36 kb/s for one train broadcasting to platoon
40.08/80.16/240.48 kb/s for 3/6/18 trains per platoon in rural/suburban/urban
[10]
Update-Delay ( | 0.01 s | 0.1 s | 1 s | 10 s
Position uncertainty | 0.5e-5 m | 0.5e-2 m | 0.5 m | 50 m
Velocity uncertainty | 0.01 m/s = 0.036 km/h | 0.1 m/s = 0.36 km/h | 1 m/s = 3,6 km/h | 10 m/s = 36 km/h
 | 0.01 s | 0.1 s | 1 s | 10 s
 | 0.5e-5 m | 0.5e-2 m | 0.5 m | 50 m
 | 0.01 m/s = 0.036 km/h | 0.1 m/s = 0.36 km/h | 1 m/s = 3,6 km/h | 10 m/s = 36 km/h

## Slide 21: Use Case 2: Train-to-Train
Overview
  Safety critical and for efficient operation
  Autonomous train protection & operation (ATP/ATO): collision avoidance, remote control, automatic coupling and train integrity; virtual coupling (platooning)
Deployment time line >2030
Requirements
  For a relative speed of 500 km/h (with directional antennas 800 km/h) and distance of 2000 m, NGV provides at least a data rate of 1 Mbps, a ranging accuracy of 1% of distance, and latency of 10 ms as well as supports reliability (SIL2)

## Slide 22: Use Case 3: Train-to-Trackside
Signaling: Safe operation of trains
  European Train Control System (ETCS)
    GSM-R, future railway mobile communication system (FRMCS) using LTE/5G or WLAN
    FRMCS traffic analysis [13]: ETCS, ATO, telemetry, remote control, critical video transmission
  Positive Train Control (PTC) [14]
  Communication Based Train Control (CBTC) [15]
    Application standard
    802.11b/g or LTE @ 1.8 GHz as well as proprietary solutions @ 5.9 GHz, e.g. based on 802.11a with 5MHz channels
Scenario for Reference Train | Train-to-Trackside (Uplink) |  | Trackside-to-Train (Downlink) | 
Critical Video Transmission | Yes | No | Yes | No
Future Evolution [Mbps] | 7.42 | 3.46 | 4.38 | 0.42
Co-Existence / Mitigation [Mbps] | 3.49 | 0.19 | 3.50 | 0.20

## Slide 23: Use Case 3: Train-to-Trackside
Signaling: Safe operation of trains
  European Train Control System (ETCS)
    GSM-R, future railway mobile communication system (FRMCS) using LTE/5G or WLAN
  Positive Train Control (PTC) [14]
  Communication Based Train Control (CBTC) [15]
    Application standard
    802.11b/g or LTE @ 1.8 GHz as well as proprietary solutions @ 5.9 GHz, e.g. based on 802.11a with 5MHz channels
  Remote train operation in degraded mode for autonomous train operation (ATO)
Issues:
  In urban areas capacity problems
  Dedicated links (link setup, link loss) to access points/base stations
   Broadcast to multiple access points for redundancy, lower latency

## Slide 24: Use Case 3: Train-to-Trackside
Overview
  Safety critical and for efficient operation
  Signaling of European Train Control System (ETCS), Positive Train Control (PTC), Communication Based Train Control (CBTC), Remote train operation in degraded mode for autonomous train operation (ATO)
Deployment time line >2025
Requirements
  For a speed of 400 km/h and distance of 2000 m, NGV provides at least a data rate of 100 Mbps (50 Mbps without critical video), absolute position accuracy of 2 m cross and 0.5 m along track with at least 99% reliability, and latency of 100 ms as well as supports reliability (SIL4)

## Slide 25: Use Case 4: Vehicle-to-Train
Shared space: Level crossings
  Basic safety message/ CAM
  Long breaking distance of trains compared to cars, e.g. 250m @ 100 km/h (62 mph) compared to 50m
  Need for increased communication range
Shared spectrum
  EC Mandate for regulation:
    Shared spectrum use of 5.9 GHz ITS band between V2X and urban rail communications
    Spectrum segregation not an option
[16]

## Slide 26: Use Case 4: Vehicle-to-Train
Overview
  Safety critical and for efficient operation
  Shared space at level crossings, shared spectrum for 5.9 GHz ITS band between V2X and urban rail communications
Deployment time line >2020
Requirements
  For a relative speed of 500 km/h and a distance of 2000 m, NGV provides at least a data rate of 1 Mbps, a ranging accuracy between 5% and 10% of distance, and a latency of 100 ms, as well as supports reliability (SIL2)
Limitations
  Interference between V2X and T2X limited while enabling safe cooperation

## Slide 27: Summary
Railway use cases also relevant to NGV besides road vehicle use cases:
Use Case 1: Onboard Train
  Wireless train control and monitoring system (TCMS), operator oriented services, customer services (passenger information services, connection to mobile hot spot for public internet)
Use Case 2: Train-to-Train
  Autonomous train protection & operation (ATP/ATO): collision avoidance; remote control of automatic coupling and train integrity; virtual coupling (platooning)
Use Case 3: Train-to-Trackside
  Signaling, operator oriented services, customer services (passenger information, …)
Use Case 4: Vehicle-to-Train
  Shared space in level crossings & shared spectrum

## Slide 28: References
Source wikipedia https://en.wikipedia.org/wiki/Vehicle
Souce wikipedia https://commons.wikimedia.org/wiki/File:Autobahn_A8_bei_Holzkirchen.JPG
Source wikipedia https://commons.wikimedia.org/wiki/File:Gleise_zu_Z%C3%BCrich_HB_2010.jpg
Shift2Rail https://shift2rail.org/
Juan Moreno García-Loygorri, Javier Goikoetxea, Eneko Echeverría, Aitor Arriola, Iñaki Val, Stephan Sand, Paul Unterhuber, del Rio, Francisco (2018) The Wireless Train Communication Network: Roll2Rail Vision. IEEE Vehicular Technology Magazine. 2018. DOI: 10.1109/MVT.2018.2844408 ISSN 1556-6072
Roll2Rail. (2015). D 2.1 Specification of the Wireless TCMS. Public deliverable. [Online]. Available: http://www.roll2rail.eu/Page.aspx?CAT=DELIVERABLES&IdPage=45291e18-8d8f-4fd6-99f8-5d4b7a519b9c
Source CONNECTA Report Summary https://cordis.europa.eu/result/rcn/200968_en.html
IEC 61375-2-3:2015 Train Communication Network (TCN) – Part 2-3:Train Communication Profile
Lehner, Andreas und Rico Gracía, Cristina und Strang, Thomas (2011) A multi-broadcast communication system for high dynamic vehicular ad-hoc networks. International Journal of Vehicle Information and Communication Systems, Vol. 2 (No. 3/4), Seiten 286-302, Inderscience Publishers, DOI: 10.1504/IJVICS.2011.044267, ISSN 1471-0242. https://www.inderscienceonline.com/doi/pdf/10.1504/IJVICS.2011.044267

## Slide 29: References
Soliman, Mohammad und Sand, Stephan und Schmidhammer, Martin und Staudinger, Emanuel (2017) Effect of Non-Integer Delay on Ranging Accuracy for Ultra-Reliable Systems. ICL GNSS 2017, 27-29 June 2017, Nottingham, England. http://elib.dlr.de/114201/
Unterhuber, Paul und Sand, Stephan und Soliman, Mohammad und Siebler, Benjamin und Lehner, Andreas und Strang, Thomas und Gera, Damini (2017) Wide Band Propagation in Train-to-Train Scenarios - Measurement Campaign and First Results. EUCAP 2017, 19.-24.März 2017, Paris, Frankreich. http://elib.dlr.de/111876/
Source Javier Goikoetxea’s tweet https://twitter.com/goikotrains/status/1038396656507670528
Nooijen, Jos (2018) Future Railway Mobile Communication System (FRMCS) Traffic Analysis V2 https://www.cept.org/Documents/fm-56/46006/fm56-18-065_frmcs-traffic-analysis-v220
M. Hartong, R. Goel and D. Wijesekera, "Communications Based Positive Train Control Systems Architecture in the USA," 2006 IEEE 63rd Vehicular Technology Conference, Melbourne, Vic., 2006, pp. 2987-2991.
IEEE 1474.1-2004 - IEEE Standard for Communications-Based Train Control (CBTC) Performance and Functional Requirements, P1474.1 - Standard for Communications-Based Train Control (CBTC) Performance and Functional Requirements
Source wikipedia https://commons.wikimedia.org/wiki/File:2018_Crozet,_Virginia_train_crash_2.jpg

## Slide 30: Straw Poll
Question: use cases relevant for NGV?
Y/N/Need more information:
27/0/18

## Slide 31: Straw Polls
Question: Do you agree to adopt the “Onboard Train” use case on slide 14 as one of NGV use cases?
Y/N/A: 10/8/15
Question: Do you agree to adopt the “Train-to-Train” use case on slide 21 as one of NGV use cases?
Y/N/A: 21/2/7
Question: Do you agree to adopt the “Train-to-Trackside” use case on slide 24 as one of NGV use cases?
Y/N/A: 12/4/14
Question: Do you agree to adopt the “Vehicle-to-Train” use case on slide 26 as one of NGV use cases?
Y/N/A: 24/0/10