## Slide 1: Technology Features for 802.11 EHT
Date: 2018-09-07
Authors:

## Slide 2: Abstract
802.11 has agreed to start an Extremely High Throughput (EHT) Study Group with the objectives [1]:
  to increase peak throughput and improve efficiency
  to support high throughput and low latency applications such as video-over-WLAN, gaming, AR and VR
In this contribution we,
  review different technologies;
  examine how they achieve the goals of the SG;
  highlight schemes within the technologies that may be studied
  and identify issues that may need to be resolved.

## Slide 3: Technologies
In the discussion leading to the formation of the SG, a variety of technologies were proposed with a goal to down-select to a manageable subset for rapid standardization.
To achieve the goals of peak throughput, efficiency improvement and reduced latency for high throughput applications, EHT should consider supporting the following technologies:
  MIMO Enhancement,
  Multi-AP transmissions,
  Multi-band/Multi-channel aggregation,
  Hybrid ARQ,
  Increased Bandwidth Transmission (320 MHz)

## Slide 4: MIMO Enhancements
11ax allows for up to 8 SS.
EHT should support up to 16 SS to increase peak throughput [2], [3], [4].
Potential Schemes
    Zero Forcing [3]
    Non-linear Precoding, e.g., Tomlinson-Harashima Precoding [6]
Some issues to be resolved:
  Feedback Overhead Reduction
    Feedback Compression [5]
    Use of reciprocity [2]
    Protocol modification [2]
  Efficient MU-MIMO procedures

## Slide 5: Multi-AP Transmission
11ax supports transmission to/from a single AP and spatial sharing between APs/STAs.
EHT should extend support to multi-AP transmission for improvement in efficiency, increase in peak throughput and reduce latency [7], [8], [9], [10].
Potential Schemes
    Dynamic AP selection
    Spatial or scheduling coordination for multiple AP transmission [10].
    Joint Precoding with Multiple APs [7], [8]
Some issues to be resolved:
  Connecting to multiple APs: Multiple AP association, STA and AP grouping
  Synchronization and Channel Estimation from Multiple APs e.g. STF and LTF design
  Effect of backhaul e.g. wired or wireless
  Feedback and Sounding for multiple AP support
  Over the air AP-AP coordination procedures

## Slide 6: Multi-band/Multi-channel Transmission
11ax supports channel aggregation (80+80) and FST
EHT should support multi-band/multi-channel transmission to increase peak throughput, efficiency and reduce latency [2], [4], [7], [9], [10], [11], [12], [13].
Potential Schemes
  Cooperative multi-band transmission including
    Multiband selection for low latency transmission (UEs with low latency requirement may select the band which is available);
    Multi-band aggregation/selection for high peak throughput (UEs with heavy payload may select the band which may provide higher throughput)
  Multi-band transmission with primary and assisted bands
  Multi-band Full Duplex
Some issues to be resolved:
  Depends on scheme e.g. synchronization, band selection etc

## Slide 7: Hybrid ARQ
11ax supports packet retransmission.
EHT should support Hybrid ARQ for increased reliability, efficiency and reduced latency [8], [9], [11].
Potential Schemes
    Chase Combining (CC) HARQ
    Incremental Redundancy (IR) HARQ
Some issues to be resolved:
  HARQ packet identification. Note that the HARQ redundancy versions should be self decodable and identifiable
  HARQ design should take into account the impairment type i.e. loss due to collision or due to AWGN e.g. use of ACK/NAK
  HARQ transmission protocol should account for delay e.g. HARQ retransmission with or without waiting or ACK/NAK

## Slide 8: Increased Bandwidth Transmission
11ax supports up to 160 GHz
EHT should support even higher bandwidth transmission (up to 320 GHz) for increased peak throughput [2], [4], [7], [9], [10], [11], [12], [13],
Some issues to be resolved:
  Identification of spectrum
  Extension of channel access to the larger bandwidth
  Schemes for multi-band aggregation to reach 320 GHz

## Slide 9: Conclusion
In this contribution, we have reviewed 5 technologies suitable for inclusion in 802.11 EHT including
  MIMO Enhancement: peak throughput increase
  Multi-AP transmissions: efficiency and peak throughput increase, latency reduction
  Multi-band/Multi-channel aggregation: efficiency and peak throughput increase, latency reduction
  Hybrid ARQ: reliability and efficiency increase, latency reduction
  Increased Bandwidth Transmission (320 MHz): peak throughput increase
For each technology, we have identified some potential schemes and some issues that need to be resolved for them to be successfully incorporated into EHT.

## Slide 10: References
11-18/1325r1, EHT TIG Closing Report - July 2018 Session, Michael Montemurro (BlackBerry),
11-18/1191r0, MU sounding improvements, Sigurd Schelstraete (Quantenna)
11-18/0818r3, 16 Spatial Stream Support in Next Generation WLAN, Sameer Vermani (Qualcomm)
11-18/1184r1, EHT discussions on throughput enhancemen, Tianyu Wu (Samsung)
11-15/1321r1, Reducing Explicit MIMO Compressed Beamforming Feedback Overhead for 802.11ax, Kome Oteri (InterDigital)
11-13/1090r2, Non-linear pre-coding for next generation WLAN, Zhanji Wu (BUPT)
11-18/1155r1, Multi-AP Enhancement and Multi-Band Operations, Jianhan Liu (Mediatek)
11-18/1116r0, Multi-AP-HARQ-for-EHT, Ron Porat (Broadcom)
11-18/1171r0, EHT objectives and technologies, Jinsoo Choi (LG)
11-18/1161r0, EHT technology candidate discussions, Hongyuan Zhang (Marvell)
11-18/1180r0, Discussion on EHT Study Group Formation, David Xun Yang (Huawei)
11-18/789r10, EXtreme Throughput 802.11, laurent cariou (Intel)
11-18/1190r1, Discussion on EHT timeline and scope, David Lopez-Perez (Nokia)