## Slide 1: WUR-Only Discovery Mode for WUR STAs
Date: 2018-09-11
Authors:

## Slide 2
Abstract
In this contribution, we discuss the benefits of having WUR-capable STAs conduct network discovery using only their WURx.

## Slide 3
Overview
Introduction
Benefits of WUR-only Discovery Mode
Changes needed to enable WUR-only Discovery mode
Conclusions

## Slide 4: Introduction
802.11ba targets classes of low power devices, such as IoT devices, many of which are only equipped with a coin battery
  IoT devices may, depending on the application, sleep for a long period of time, but need to be woken up within a short delay period
Currently, 802.11ba spec draft has defined the WUR operation mostly for the case when a STA is associated with an AP [1]
  A WUR non-AP enters WUR Mode (i.e., turning off its PCR and turning on its WUR) after explicit negotiation with its AP
  “If a WUR non-AP STA is in WUR Mode, then:
    —The existing negotiated service period between WUR AP and WUR non-AP STA for the WUR non-AP STA’s PCR schedule is suspended: “
WUR-capable STAs may benefit from a defined WUR-only network discovery process

## Slide 5: Benefits of WUR-only Network Discovery (1/2)
Low power devices may be in the unassociated state for a long period of time while
  In transition between warehouses (inventory tracking)
  In transition between facilities (personnel tracking)
  Out of range of one or more associable mobile APs (wearable devices)
A WUR-only Network scanning and discovery process may provide a lot of benefit for low power devices in the unassociated state
  Using the WURx for network scanning and discovery can greatly reduce energy consumption in scenarios where there are no suitable APs in the vicinity when compared to using the PCR for the same task.
  Power conservation may provide much longer expected operating life for low power devices
  It is likely that purchasers deploying WUR-capable devices will also be deploying WUR-capable APs to support the deployed devices.

## Slide 6: Benefits of WUR-only Network Discovery (2/2)
It is possible for WUR-capable devices to use existing WUR frames to perform WUR-only discovery.
  WUR Discovery frames/WUR beacons
WUR-only discovery mode would be useful as an optional mode to enable significant power saving before the STA is associated with an AP

## Slide 7: Changes Needed to Define WUR-only Discovery
Current 802.11ba spec draft has the following features [1]:
  “A WUR non-AP STA may use its WURx to scan WUR discovery channels. “
    Can enable WUR-only discovery mode
  A WUR non-AP STA enters WUR mode after successful frame exchange of WUR Mode Setup frames
    Restrictive to enable WUR-only discovery mode
Only small changes are needed to define WUR-only Discovery
  WUR-capable STAs can leverage existing 11ba features:
    WUR Discovery frames and procedures/WUR beacons
  Need to define how WUR-capable STAs can enter WUR mode, or a mode that is similar to WUR mode (WURx on and PCR off) when the STA is in the unassociated state
  Some configurations for the WURx may be needed: e.g., WUR parameters, target BSS/ESS, etc.
WUR-only discovery mode could be an optional feature when low power devices desire to conserve energy prior to association

## Slide 8: Conclusion
In this contribution, we discussed the benefit of a WUR-only Discovery mode that
  Will enable lower power devices to conserve energy prior to association
  Can de defined as an optional mode
Defining the WUR-only Discovery mode will only require minor specification additions:
  Leveraging existing features of WUR Discovery frame and procedures/WUR beacons
  Define a WUR-only Discovery mode where the WURx is on and the PCR is off
  Some configurations for WURx may be needed

## Slide 9
References
[1] IEEE P802.11ba Draft 0.4, Aug. 2018
[2] IEEE P802.11RevMD Draft 1.0, Feb. 2018

## Slide 10: SP 1
Do you agree that the WUR-only Discovery mode should be defined?
  Y:
  N:
  Need more information: