## Slide 1: Indicating Neighboring BSS’ Discovery Frame Offset
Date: 2018-09-11
Authors:

## Slide 2
Abstract
In this contribution, we discuss the need to provide the WUR Discovery frame offset for neighboring BSSs.

## Slide 3: Introduction
TGba has agreed to advertise Neighboring BSS’s Discovery information in the WUR Discovery element [1]
  Information includes Short-SSID, BSSID, WUR Discovery Period
  Such information is meant to make it easier for the WUR non-AP STA to receive the Discovery frame
However, WUR Discovery Period may be very long and WUR non-AP may need to monitor the medium for a long period of time to receive such frames
More precise information may help WUR non-AP to identify the timing of the WUR Discovery frame

## Slide 4: Need to Provide Neighboring BSS’s Discovery frame offset
WUR Discovery Period may be very long
  WUR Discovery Period can be indicated in 16 bits, and therefore may be 1 – 65536 TU long
  Each TU is 1024 us, so the WUR Discovery Period may be longer than 67s, much longer than the 100ms periods that are typical for regular beacons
Monitoring the medium using the WURx without knowing when the WUR Discovery frame is transmitted wastes energy
  Even if the WURx consumes less than 1mW, it is still better to turn off the WURx if there is no WUR Discovery frames to be received
It is easier to provide a more precise timing for the WUR Discovery frame by providing the Discovery frame offset for neighboring BSSs.
  Similar TBTT offsets for regular beacons provide efficiency and scheduling advantages for non-AP STA’s using Reduced Neighbor Reports
  Such offset may be optional, similar to the other fields in the WUR AP subfield in the WUR Discovery element

## Slide 5: Indicating WUR Discovery frame offset
The WUR Discovery frame offset may be included in the WUR Discovery element
  Optional 2-bytes element in the WUR AP subfield
  WUR Discovery frame offset in TUs, rounded down to the closest TU, from the transmitting AP’s TBTT
  Transmitting AP advertises its own WUR Discovery frame offset so that neighbor APs may include such information in their own WUR Discovery element
WUR non-AP STA may use such information to scan for relevant APs’ WUR Discovery frame

## Slide 6: Conclusion
In this contribution, we discussed the need to provide more precise timing for the neighboring BSS’ WUR Discovery frame
  WUR non-AP STA may conserve more energy by only monitoring the relevant BSS’ WUR Discovery frames with more precise timing
Such information can be included in the WUR Discovery element

## Slide 7
References
[1] IEEE P802.11ba Draft 0.4, Aug. 2018
[2] IEEE P802.11RevMD Draft 1.0, Feb. 2018

## Slide 8: SP 1
Do you agree that WUR Discovery frame offset should be included in the WUR Discovery element?
  Y/N/A:

## Slide 9: SP 2
Do you support to include the changes proposed in 11-18/1555r0 into the next 802.11ba draft?
  Y/N/A: