## Slide 1
Multiple WID WUR Frame Format
Date: 2018-09-09
Authors:

## Slide 2: Introduction
TGba has defined multiple WID Frame but not its specific format[1]
  Multiple WID frame can be indicated by setting address field to 0
    The Address field of the WUR Wake-up frame is set to 0 when multiple WIDs are included in the Frame Body field of the frame
The unit mismatch between Frame Body field length and WID may cause long padding bits
  D0.4 considers 16xL bits length of Frame Body field but multiple WID Frame requires 12xN bits Frame Body field
    At most 12 bits padding fields shall be padded
    192us of meaningless padding fields before FCS field
    At most 10 users can be awaken by the WUR frame
  Following structure shall be added based on current draft
    Frame Body field of the multiple WID Frame

## Slide 3: Frame structure for WUR Frame with Frame Body field
The Length/Misc field contains the Misc field when the Length Present field is set to 0.
Length/Misc subfield indicates the length of Frame body in units of 2 octets when Length Present field is set to 1
  The length of the Frame Body field is in units of octets and is equal to 2 x (L + 1), where L is the value of the Length subfield in the Frame Control field.
 | Type | Length Present | Length/ Misc. | Protected
Bits: | 3 | 1 | 3 | 1
 | Frame Control | Address | TD Control | Frame body | FCS
Bits: | 8 | 12 | 12 | variable | 16

## Slide 4: Frame structure for Multi-WID WUR Frame
A following structure shall be considered based on the current draft
  Opt 1: Padding bits appear in end Frame Body field of the multiple WID Frame because of the mismatch of the unit of length of Frame Body and the size of WID
  Without further optimization x padding bits have following values in opt 1
    4 for n=4m+1 (m = 0, 1, 2, …) case
    8 for n=4m+2 (m = 0, 1, 2, …) case
    12 for n=4m+3 (m = 0, 1, 2, …) case
    0 for n=4m+4 (m = 0, 1, 2, …) case
  Opt 2: Padding bits appear after each WID field in Frame Body field because each WID requires 2 octets for the simple MAC structure or adding user specific special feature
  4 bits padding for each WID, at most 32 bits padding which requires 512us air time
  Simplest but heavy overhead.
WID #1 | WID #2 | ∙∙∙ | WID #n | Padding
Bits : 12 12 12 x
WID #1 | Padding | ∙∙∙ | WID #n | Padding
Bits : 12 4 12 4

## Slide 5: Optimization method
Additional indication methods for Multi-WID WUR Frame could reduce padding overhead
  WUR frame is allowed to have Frame Body field with non zero Misc field
    Set 0 for Length Present field and number of user-1 for Misc field
    Number of user = M+1, 8 users at most
    M > 0 if the address field is set to 0, M=0 if the WUR frame if the address field is not set to 0
  Or make a different decoding rules for Length/Misc field if the type of WUR Frame is a Wake-up Frame (Number of STAs-1 instead of 16 octets)
No padding bits if WUR Frame can be generated by bit-by-bit
At most 4 bits if WUR Frame should be generated by octet-by-octet
  0 for M=2m (m = 1, 2, …) case
  4 for M=2m+1 (m = 0, 1, 2, …) case
Address field shall not set to 0 when there is a single target WUR STA
WID #1 | WID #2 | ∙∙∙ | WID #n | Padding
Bits : 12 12 12 x

## Slide 6: WUR Capabilities information
In the following types of WUR frame, nonzero frame body exists:
  WUR Wake-up frame with WID=0
  WUR Discovery frame
  WUR vendor specific frame
The Capabilities information, STA only indicates the support of the nonzero frame body
  There is no indication for individual type of WUR frame
 | PCR Transition Delay | Nonzero Length Frame Body Support | Group IDs Support | Protection Support | 20 MHz WUR PPDU with HDR Support | WUR Channel Switching Support | Reserved
Bits: | 8 | 1 | 2 | 1 | 1 | 1 | 2

## Slide 7: Suggestion
Adding 1 bit of receiving the WUR Wake-up frame with multiple WIDs in WUR capabilities field
  Use the reserved bits of WUR capabilities field
Following text modification is also suggested for length indication
  9.10.2.4 Frame Body field
  The Frame Body field is not present when the Length Present subfield of the Frame Control field is 0 (i.e., within ML WUR frames) and is present when the Length Present subfield of the Frame Control field is 1 (i.e., within VL WUR frames).
  The Frame Body field is not present unless the Length present field of the Frame Control field is set 1 or the WUR Frame is a wake-up frame with the non-zero Length/misc field of the Frame control field.
  9.10.3.2 WUR Wake-up frame format
  The Misc field of the WUR Wake-up frame with multiple WIDs contains the number of WIDs-1 in the Frame Body field if the Address field of the WUR Wake-up Frame is set to 0.
 | PCR Transition Delay | Nonzero Length Frame Body Support | Multiple WIDs Support | Group IDs Support | Protection Support | 20 MHz WUR PPDU with HDR Support | WUR Channel Switching Support | Reserved
Bits: | 8 | 1 | 1 | 2 | 1 | 1 | 1 | 21

## Slide 8: Conclusions
Frame structure of multiple WID Wake-up Frame shall be described in D1.0
Simple structure of multiple WID Wake-up Frame may have severe overhead due to its padding bits
Because 11ba is considering simple operations and small modifications on PCR operation, using the redundant bits for indicating any additional PCR operations is not suitable for concept of 11ba
The proposed method reduces its padding overhead and enables WURx to know whether it is multiple WID Wake-up Frame or not before decoding the address field.

## Slide 9: References
[1] IEEE Draft P802.11ba D0.4