## Slide 1
Multiple WID WUR Frame Format
Date: 2018-09-11
Authors:

## Slide 2: Introduction
TGba has defined multiple WID Frame but not its specific format[1]
  Multiple WID frame can be indicated by setting address field to 0
    The Address field of the WUR Wake-up frame is set to 0 when multiple WIDs are included in the Frame Body field of the frame
The unit mismatch between Frame Body field length and WID may cause long padding bits
  D0.4 considers 16xL bits length of Frame Body field but multiple WID Frame requires 12xN bits Frame Body field
    At most 12 bits padding fields shall be padded
    192us of meaningless padding fields before FCS field
    At most 10 users can be awaken by the WUR frame
  Following structure shall be added based on current draft
    Frame Body field of the multiple WID Frame

## Slide 3: Frame structure for WUR Frame with Frame Body field
The Length/Misc field contains the Misc field when the Length Present field is set to 0.
Length/Misc subfield indicates the length of Frame body in units of 2 octets when Length Present field is set to 1
  The length of the Frame Body field is in units of octets and is equal to 2 x (L + 1), where L is the value of the Length subfield in the Frame Control field.
 | Type | Length Present | Length/ Misc. | Protected
Bits: | 3 | 1 | 3 | 1
 | Frame Control | Address | TD Control | Frame body | FCS
Bits: | 8 | 12 | 12 | variable | 16

## Slide 4: Frame structure for Multi-WID WUR Frame
A following structure shall be considered based on the current draft
  Opt 1: Padding bits appear in end Frame Body field of the multiple WID Frame because of the mismatch of the unit of length of Frame Body and the size of WID
  Without further optimization x padding bits have following values in opt 1
    4 for n=4m+1 (m = 0, 1, 2, …) case
    8 for n=4m+2 (m = 0, 1, 2, …) case
    12 for n=4m+3 (m = 0, 1, 2, …) case
    0 for n=4m+4 (m = 0, 1, 2, …) case
  Opt 2: Padding bits appear after each WID field in Frame Body field because each WID requires 2 octets for the simple MAC structure or adding user specific special feature
  4 bits padding for each WID, at most 32 bits padding which requires 512us air time
  Simplest but heavy overhead.
WID #1 | WID #2 | ∙∙∙ | WID #n | Padding
Bits : 12 12 12 x
WID #1 | Padding | ∙∙∙ | WID #n | Padding
Bits : 12 4 12 4

## Slide 5: Optimization method
Additional indication methods for Multi-WID WUR Frame could reduce padding overhead
  WUR frame is allowed to have Frame Body field with non zero Misc field
    Set 0 for Length Present field and number of user-1 for Misc field (number of users in FB)
    Number of user = M+1 for M>0 (can be differentiated depending on Address Field policy of multi-WID WUR Frame), 8 users at most
    M > 0 if the Wake-up frame is multi-WID WUR Frame, M=0 if the Wake-up frame is single-WID WUR Frame
    The Address field does not need to have special value, one more STAs can be accommodated
No padding bits if octet alignment is not needed
At most 4 bits of padding if octet alignment is required
  0 for M=2m (m = 1, 2, …) case
  4 for M=2m+1 (m = 0, 1, 2, …) case
Length Present field may not be set to 1 for WUR Wake-up frame type
FC | Address | TD Control | WID #1 | ∙∙∙ | WID #n | Padding | FCS
Bits : 12 12 x
 | Type =1 | Length Present=0 | Misc. =n-1 or n | Protected
Bits: | 3 | 1 | 3 | 1
FC | Address | TD Control

## Slide 6: WUR Capabilities information
In the following types of WUR frame, nonzero frame body exists:
  Multi-WID WUR Wake-up frame
  WUR Discovery frame
  WUR vendor specific frame
The Capabilities information, STA only indicates the support of the nonzero frame body
  There is no indication for individual type of WUR frame
 | PCR Transition Delay | Nonzero Length Frame Body Support | Group IDs Support | Protection Support | 20 MHz WUR PPDU with HDR Support | WUR Channel Switching Support | Reserved
Bits: | 8 | 1 | 2 | 1 | 1 | 1 | 2

## Slide 7: Suggestion
Adding 1 bit of receiving the WUR Wake-up frame with multiple WIDs in WUR capabilities field
  Use the reserved bits of WUR capabilities field
  Or 11ba STAs with Nonzero Length Frame Body Support shall support Multi-WID WUR Wake-up Frame
Following text modification is also suggested for length indication
  9.10.2.4 Frame Body field
  The Frame Body field is not present when the Length Present subfield of the Frame Control field is 0 (i.e., within ML WUR frames) and is present when the Length Present subfield of the Frame Control field is 1 (i.e., within VL WUR frames).
  The Frame Body field is not present unless the Length present field of the Frame Control field is set 1 or the WUR Frame is a wake-up frame with the non-zero Length/misc field of the Frame control field.
  9.10.3.2 WUR Wake-up frame format
  The Misc field of the WUR Wake-up frame with multiple WIDs contains the number of WIDs-1 in the Frame Body field if the Address field of the WUR Wake-up Frame is set to 0.
 | PCR Transition Delay | Nonzero Length Frame Body Support | Multiple WIDs Support | Group IDs Support | Protection Support | 20 MHz WUR PPDU with HDR Support | WUR Channel Switching Support | Reserved
Bits: | 8 | 1 | 1 | 2 | 1 | 1 | 1 | 21

## Slide 8: Conclusions
Frame structure of multi-WID Wake-up Frame shall be described in TGba spec
Simple structure of multi-WID Wake-up Frame may have severe overhead due to its padding bits
Because 11ba is considering simple operations and small modifications on PCR operation, using the redundant bits for indicating any additional PCR operations is not suitable for concept of 11ba
The proposed method reduces its padding overhead and enables WURx to know whether it is multiple WID Wake-up Frame or not before decoding the address field.

## Slide 9: Straw Poll #1
Which option do you prefer?
  Option A : Capability on Multi-WID WUR Frame supporting shall be specified in D1.0
  Option B : Nonzero Length Frame Body Support includes Multi-WID WUR Frame support capability
    Every 11ba STA with Nonzero length FB capability shall support Multi-WID WUR Frame feature
Option A/Option B/Abstain
 | PCR Transition Delay | Nonzero Length Frame Body Support | Multiple WIDs Support | Group IDs Support | Protection Support | 20 MHz WUR PPDU with HDR Support | WUR Channel Switching Support | Reserved
Bits: | 8 | 1 | 1 | 2 | 1 | 1 | 1 | 21

## Slide 10: Straw Poll #2
Which option do you prefer?
  Option A : 12-bit WID + 4-bit padding for each WID as a multi-WID Wake-up Frame format
  Option B : Nx12-bit WID + small padding as a multi-WID wake-up Frame format
  Abstain
Option A/Option B/Abstain

## Slide 11: Straw Poll #3
Do you agree with the following?
  Wake-up type WUR Frame shall indicates its number of user with its misc field instead 2 octet based length field
    Length Present field is set to 0
    Length/Misc field has non-zero value for representing its number of WIDs in Frame Body
    At most 32 bits overhead could be reduced (=512 us)
    Because the frame can be distinguished before Address field decoding, Address field also can be utilized to accomodate an additional STA (WID instead of 0 value)
Y/N/A

## Slide 12: References
[1] IEEE Draft P802.11ba D0.4