## Slide 1: Performance Simulations
Date: 2018-09-10
Authors:

## Slide 2: Abstract
This presentation describes the stadium video distribution simulations.
Especially the point of view of:
How many device can be covered by a single AP?

## Slide 3: Assumptions
Tens of thousands of spectators in a stadium
Each spectator occupies 1m2 (1m * 1m)
All spectators watch the same video stream on their own devices.
A video stream consumes 2Mbps
1m
1m

## Slide 4: Unicast vs Broadcast
Unicast traffic is proportional to the number of users
Broadcast does not have ACK mechanism.
  A kind of inter-packet error correction will be used to reduce packet losses. e.g. transmitting the same packet multiple times.
number of users
traffic (Mbps)
Unicast (2Mbps/user)
Broadcast (3 times)
Broadcast (2 times)
Broadcast (1 time)

## Slide 5: Cell Size Estimation
To specify the practical cell size,
  Measured error rate
  Calculated cell size

## Slide 6: Error Rate Measurement
Host A and Host B exchange packets.
  Payload: 1408 byte
Host C captures packets.
  If FCS is incorrect, the frame is considered as error.
Not in a shielded room, just in a general office building.
  Much interference
Host A
Host B
AP
Host C
Move
Stable Communication
Capture

## Slide 7: Result
N > 1000 for each point
2.4GHz
  MCS 7 (n)
  ShortGI
  20MHz Bandwidth
  72.2 Mbps
  The result may be affected by interference from environment.
5.2 GHz
  MCS 7 (ac)
  ShortGI
  80MHz Bandwidth
  325.0 Mbps
Error Rate 0
when RX Power > -67dBm
RX Power (dBm)
Error Rate

## Slide 8: Cell Size
Assumptions
  TX power: 1mW or 10mW
  Antenna Gain: 0dBi
  Free Space (Friis transmission equation)
Distance (m)
RX Power (dBm)
-67
Frequency (GHz) | 2.4 |  | 5.2 | 
TX Power (mW) | 1 | 10 | 1 | 10
Distance (m) when RX Power = -67dBm | 22 | 70 | 10 | 35
Area (m2) = Number of Users | 1558 | 15579 | 332 | 3319
An AP can cover > 3000 users while existing IEEE 802.11 AP can associate with 2007 STAs.

## Slide 9: Conclusion
Broadcast can reduce traffic when many users access to the same contents.
Broadcast without association can reduce the number of APs for Broadcast Service.