## Slide 1: Performance evaluation of Real Time Communications over Wi-Fi
Date: 2019-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP RAS |  |  | khorov@frtk.ru
Dmitry Bankov | IITP RAS |  |  | bankov@iitp.ru

## Slide 2: Contribution
This document describes two ways of how to organize real-time communications in IEEE 802.11 networks and evaluates their performance in simple scenarios

## Slide 3: Outline
Preemptive Service
AX-like approach
Simulation results

## Slide 4: What makes Wi-Fi not Real-Time
Packet Delay = Queueing Delay + Packet Transmission Time
A real-time (RT) packet shall wait while at least the head-of-line packet is being transmitted
Maximal PPDU duration in 11ax exceeds 5 ms
Packet Transmission Time includes channel access time and PPDU duration (plus retries, if any)
Because of unlicensed spectrum, the channel may be busy with transmission of other devices

## Slide 5: Reducing Queueing Delay
Main idea: Stop transmitting a non-RT frame when an RT frame arrives.
This is similar to IEEE Std 802.1Qbu-2016
A STA can easily stop its own frame, but how to stop other frame transmissions

## Slide 6: Preemptive service. Own RT packet
Data
Time
Data
Time
Real Time Data
SIFS
Ack
RT packet arrives in the queue of the same STA
[1] WTSN (Wi-Fi Time Sensitive Networking) doc.:IEEE 802.11-17/1734r1
Main idea: to minimize channel access delay, stop transmitting a non-RT frame when a RT frame arrives.

## Slide 7: Preemptive service. Alien transmission
RT packet arrives in the queue of another STA
Channel is busy
Non-RT STA
RT STA
Data
Busy tone in the service channel
Time
Time
IFS
Data
SIFS
Ack
Data
The RT STA generates busy tone in the service channel when it has an RT frame.
Any ongoing transmissions should be cancelled.
If no busy tone is in the service channel, the RT frame can be transmitted PIFS after the main channel becomes idle. Otherwise, RT frames contend for the channel access according to EDCA (high priority queue)
[1] WTSN (Wi-Fi Time Sensitive Networking) doc.: IEEE 802.11-17/1734r1

## Slide 8: AX-like approach
Multi Station Block-Ack
TF
MSBA
TF
Frequency
Time
SIFS
SIFS
Trigger Frame
Resource Units
Assigned to specific STAs or Random Access (RA)
Other Transmissions
RU 1
RU 2
RU m
…
The AP periodically generates TF

## Slide 9: AX-like approach. Possible Algorithm
RU 1 is for RT Random Access
RU 2…m are used for usual DATA or RT DATA.
RU duration is short enough to allow 3 TX within delay budget.
Frequency
Time
TF
MSBA
RU 1
RU 2
RU m
…
TF
MSBA
RU 1
RU 2
RU m
…
TF
MSBA
RU 1
RU 2
RU m
…

## Slide 10: AX-like approach. Possible Algorithm
Time
RU 0
RU 1
RU 2
…
RU m
RU 0
STAs: 1, m+1 , …
STAs: 2, m+2 , …
…
STAs: m, 2m, …
RU 0
STAs: 2
STAs: m+2
STAs: 2m
STAs: m
RU 0
RU 1
RU 2
…
RU m
RT RA RU, idle
Non-RT RU
RT RU, idle
RT RU Collision
STAs 1, 2, m, 2m transmit RT frames
RT RU, success
Apart from that, STA m+2 transmits.
By default, the AP allocates 1 RUs for random access
In case of collision, the remaining m RUs are allocated for RA RT uniformly for those STAs, which might participate in the collision
If the number of RT STAs is greater than m, each RU is allocated for several STAs

## Slide 11: Performance evaluation
1 AP, 10 non-RT STAs transmitting frames in saturated mode
N RT STAs generate 32B frames (Poisson process with λ-1 = 50 ms)
All STAs use MCS5
If a frame is not delivered within 1ms, it is dropped.
Tdata= 0.9 ms (non-OFDMA), Trt= 0.06 ms, Period of RUs = 0,28ms, BW=40MHz, Nru=18
Packet loss ratio (both collisions and drops)
Portion of throughput for usual DATA