## Slide 1: Use Cases for NGV using High Data Rate
Date: 2018-11-12
Authors:

## Slide 2: Abstract
This submission proposes use cases for NGV SG, which are utilizing NGV’s high data rate. Includes:
  IP Traffic Offloading
  Shared Bird’s-Eye View

## Slide 3: IP Traffic Offloading
  DSRC/WAVE supports IPv6 over 11p
    Cloud-based applications are expected
Offload IP traffic from 11p to NGV
  distribute location dependent data
    map, advertisement
  download/upload delay tolerant data
    logs, sensor data for non/semi-real time usage, entertainment
Downloading 3D maps
Uploading sensor data

## Slide 4: IP Traffic Offloading
Overview: Offload IP traffic from 11p to NGV
  distribute location dependent data
  download/upload delay tolerant data
Deployment timeline:
  >2019 (5.9 GHz band)
  >2022 (60 GHz band)
Requirements:
  Packet NGV should carry higher number (>50%) of transmitted bytes than IEEE802.11p packet under same conditions (packet duration, PER, range, wireless channel)
Nice to have:
  Optional mmWave capability based on 11ad PHY to have >1Gbps
Limitations:

## Slide 5: Shared Bird’s-Eye View
Vehicles and infrastructures share their own views to each other to construct bird’s eye views
  For safety: blind spot monitoring
  For drivers/passengers: navigation, augmented reality
Bird’s-Eye View for Platoon (V2V)
Bird’s-Eye View for Intersection (V2I/V2X)

## Slide 6: Shared Bird’s-Eye View
Overview: Vehicles and infrastructures share their own views to each other to construct bird’s eye views
  the views are used for safety and driver/passengers usage
  example scenario: (1)around intersection; (2)around platoon
Deployment timeline: >2025 (expected)
Requirements:
  Packet NGV should carry higher number (>50%) of transmitted bytes than IEEE802.11p packet under same conditions (packet duration, PER, range, wireless channel)
Nice to have:
  Optional mmWave capability based on 11ad PHY to have >1Gbps for tens of vehicles near the intersection / lower latency for platooning
Limitations:
  Packet prioritization algorithm at higher layer to share radio resources with higher priority applications (e.g. BSM)

## Slide 7: References
[1] 11-18/0861r08 802.11 NGV Proposed PAR
[2] 11-18/1323r01 NGV SG Use Cases

## Slide 8: Straw Poll
Do you agree to adopt each of the use cases on slide 4 and 6 as one of NGV use cases?
Y/N/A