## Slide 1: Multi-channel interference mitigation
Date: 2019-01-14
Authors:
Ron Toledano, Autotalks

## Slide 2: Abstract
Interferences resulted from multi-channel operation reduce the effective communication range
Shown in IEEE802.11-18/1928r0
In multi-channel environment, each channel is used independently carrying traffic with arbitrary profile
Synchronizing channels, using carrier-aggregation like scheme, isn’t applicable
In this presentation we suggest multi-channel interference mitigation scheme
Ron Toledano, Autotalks

## Slide 3: Multiple Channels Interferences - Recap
Interference free multi-channel operation can’t be assured
Ron Toledano, Autotalks

## Slide 4: Unconstrained Operation  Chaos
Ron Toledano, Autotalks
TX Ch. 1
TX Ch. 2
Transmission ignores activity in other channels
As a result, two close vehicles can transmit concurrently
  All vehicles in proximity of one channel transmission will not receive the other channel transmission, despite its relevancy and relative short distance

## Slide 5: Constrained Operation  Spatial Coordination
Ron Toledano, Autotalks
TX Ch. 1
TX Ch. 2
Transmission considers activity in other channels
Concurrent transmission from close vehicles is prevented
  Important messages aren’t harmed

## Slide 6: Concept of Operation
Ron Toledano, Autotalks
Outside Ch1. interference range  Ch. 2 can transmit
TX Ch. 1
TX Ch. 2
Within Ch1. interference range  Delay Ch. 2 transmission

## Slide 7: Transmission Flow
Interference is quantified by RSSI level, reflecting target communication range
  Target range is determined by use-case, commonly 300 meters for safety
Real-time transmission deferral decision is needed
  V2X upper layer can configure decision parameters, but can’t perform real-time RSSI comparisons
  MAC can perform real-time RSSI comparisons based on information from PHY
Ron Toledano, Autotalks
Transmit
Delay transmission
Yes
Multi-channel interfere?
No

## Slide 8: Multi-Channel Interference Mitigation Layer
Adding MAC layer is suggested
  Required by any system: single radio or multi-radio
Ron Toledano, Autotalks
PHY
MAC
Multi-channel interference mitigation
V2X upper layer

## Slide 9: RSSI Based Decision
RSSI is indicative to distance
Upon transmit request, adjacent packet RSSI is compared with threshold
  If above threshold  Interference too strong. Vehicle is likely too close  Delay transmission
  If below threshold  Interference not harmful. Vehicle is likely far enough  Transmit
RSSI varies based on environment
  For example, truck on road, curve, building, etc…
  V2X upper layer can adjust the threshold based on expected RSSI in target range
Ron Toledano, Autotalks

## Slide 10: Adjacent Channel RSSI Measurement
Low complexity adjacent channel RSSI measurement is feasible
  Deducting energy based on main channel
  Measuring energy on a wider span
  Measurement performance targets can be set, such as detection of interferences stronger than -65dBm
Ron Toledano, Autotalks
Main Ch.
Adjacent Ch.
Adjacent Ch.
Wide-span energy measurement
Estimation based on main channel

## Slide 11: Zoom on Interface
Ron Toledano, Autotalks
V2X upper layer
Multi-channel interference mitigation
Config (Adjacent channel RSSI threshold(s))
Additional channels
PHY
Adjacent channel RSSI(s)
Delay TX

## Slide 12: Summary
Multi-channel interference mitigation would enable reliable multi-channel operation
Achieving efficient spatial utilization
Suggested mitigation scheme delays transmission based on adjacent channels RSSI
PHY estimates RSSI of adjacent channels
RSSI value(s) compared with threshold(s)
Threshold(s) is configured by V2X upper layer
Ron Toledano, Autotalks