## Slide 1: Coordinated Multi-AP Transmission for EHT
Date: 2019-01-13
Authors:

## Slide 2
Abstract
In this contribution, we discuss some additional Multi-AP coordinated technique details and perform a simple analysis to demonstrate the usefulness of the schemes.

## Slide 3: Introduction
Multi-AP Coordination Schemes have been discussed as candidate features for adoption in 802.11 EHT [1]
  Examples of different multi-AP schemes with some performance gains are discussed in [2]-[8]
In [2], a terminology for AP coordination was presented with two types discussed:
  Coordinated Techniques: Coordinated Beamforming and Coordinated OFDMA
  Joint Processing Techniques: Joint Process Transmissions including Joint BF to a single STA
This contribution will focus on coordinated techniques
  We will give some examples of coordinated techniques, show a simplified analysis of their performance and highlight some issues that need to be addressed to standardize them in EHT.

## Slide 4: Coordinated OFDMA
In Coordinated OFDMA, the APs coordinate to share OFDMA resources
Option 1 (Coordinated OFDMA): Each AP coordinates RUs for all its STAs (see [2])
  This may result in-efficient allocation of resources as both BSSs are limited to the resource they are assigned to.
Option 2 (Fractional Coordinated OFDMA): Each AP coordinates RUs for only interference limited STAs
  Non-interference limited STAs (center) may transmit/receive in all RUs
  Interference limited STAs (edge) may transmit in coordinated RUs
  For uplink, STAs may be scheduled (TRS) or compete for resource (UORA)
  For DL, non-interference limited STAs (center) may limit the transmit power in the secondary coordinated resource

## Slide 5: Coordinated OFDMA
Fractional Coordinated OFDMA
Coordinated OFDMA

## Slide 6: Issues to be Resolved
Need to identify the interference limited STAs
  May be estimated by the APs. One problem is that only the STA may know its interfering AP and be able to identify if it is interference limited
  May be estimated by each STA and its status fed back to the APs
Need synchronized transmissions for orthogonality
  This has been discussed in [2]

## Slide 7: Coordinated Beamforming and Nulling
In CB/N, each AP limits its transmitted interference to STAs in other BSSs while transmitting to its desired STA, usually by spatial domain nulling
There is no need for data at both APs but channel information to the other STA is needed
It conceptually extends the 802.11ax spatial-sharing schemes to the spatial domain.

## Slide 8: Issues
Identify and associate with serving and interfering APs
  Multi-AP Association procedures are needed
Channel information acquisition
  Generalize channel feedback procedure to enable feedback of information from a STA to both serving and interfering APs
  May need feedback compression to reduce overhead.
  Can use the same schemes as for the 16 SS feedback compression
Synchronization
  Requirements are low unless performing joint feedback to both APs simultaneously

## Slide 9: Simplified Performance Analysis
Baseline (14.4 bps/Hz) < COFDMA (16 bps/Hz) < FC-OFDMA (20 bps/Hz) < CB/N (32 bps/Hz)

## Slide 10: Conclusion
In this contribution, we proposed some additional detail in Multi-AP coordinated techniques and performed some simple analysis to demonstrate the usefulness of the scheme
We identified issues to be addressed in standardizing these schemes in EHT. These include:
  Multi-AP association
  Feedback
    Multi-AP sounding and feedback (coordinated beamforming)
    Interference-limited STA feedback (coordinated OFDMA)

## Slide 11
References
[1] 11-18/1231r1, EHT draft proposed PAR, laurent cariou (Intel), Nov. 2018
[2] 11-18/1926r2, Terminology for AP Coordination, Sameer Vermani (Qualcomm), Nov. 2018
[3] 11-18/1439r0, Distributed MU-MIMO, Ron Porat (Broadcom), Sep. 2018
[4] 11-18/1510r1, AP Coordinated beamforming for EHT, Hongyuan Zhang (Marvell), Sep. 2018
[5] 11-18/1509, Features for Multi-AP Coordination, Jianhan Liu (Mediatek), Sep. 2018
[6] 11-18/1576, Considerations on AP Coordination, Yang Bo [Boyce], Roger Marks, Lyu Yunping [Lily], Yuchen Guo [Jason] (Huawei), Sep. 2018
[7] 11-18/1962, Distributed MU MIMO Simulations, Ron Porat (Broadcom), Nov. 2018
[8] 11-18/1982, Consideration on multi-AP coordination for EHT, Kiseon Ryu (LG Electronics), Nov. 2018