## Slide 1: Indicating NGV Capabilities in MAC Header
Date: 2019-05-13
Authors:

## Slide 2: Abstract
NGV stations must have a means to detect each other
  It is highly desirable for this indication of NGV capability be included in legacy 802.11p frames sent by NGV stations so that NGV stations can detect each other while sending frames that are already required for legacy communication
  Any such indication must be encoded in a manner that does not affect interoperability, coexistence, backward compatibility, or fairness with legacy 802.11p stations
It is highly desirable that this means be extensible to multiple capabilities
  If NGV is successful, there will eventually be other generations of V2X enhancements
The Duration/ID field of the MAC header can be used for this purpose
  When this indication is included in 802.11p broadcast MPDUs sent in a 10MHz channel, up to 31 capability values are available, with 15 of these values also available for use in 802.11p unicast MPDUs and control frames in unicast frame exchange sequences

## Slide 3: Using the duration value to indicate NGV capabilities
In 802.11 OCB mode the duration value is the number of microseconds from the end of the current PPDU until the end of the current frame exchange sequence
  MPDUs with group addresses always have duration zero
  MPDUs with individual addresses have duration of aSIFSTime plus time to send the ACK
NGV-capable stations can add a Capability Indication Increment (CII) to the duration that would otherwise appear in an 802.11 OCB mode transmission, while retaining full interoperability and backward compatibility with 802.11p
  Duration increments less than aSIFSTime cannot affect channel access, because, even if such a value were used to update a station’s NAV, the resulting NAV setting will expire before the earliest time that the NAV is used by any coordination function
  For 802.11p operating in a 10MHz channel, duration increments in the range [0:31] are safe to use, because aSIFSTime is 32 microseconds

## Slide 4: Generating the Duration Field Value for Transmission
Legacy stations operating in OCB mode generate duration field values as specified in 802.11-2016
CII values in the range [1:15] shall be assigned (by the ANA) to indicate NGV, and post-NGV, capabilities
An NGV-capable station shall calculate the duration as currently specified, then generate the duration field value from the calculated duration as follows:
  For data and management frames, add the station’s assigned CII to the calculated duration
  For control frames, add the station’s assigned CII, plus 16, to the calculated duration
    The plus 16 is necessary to distinguish non-zero ACK frame durations which indicate NGV capabilities from ACK frame durations generated according to clause 9.2.5.7 of 802.11-2016

## Slide 5: Interpreting the Duration Field Value After Reception
A duration field value of zero indicates the frame was transmitted by a legacy (802.11p) capabilities
An NGV-capable station receiving a frame with a non-zero duration field value subtracts the duration that is expected for that type of frame under 802.11-2016, then interprets the difference according to the frame type of the reception:
  For data or management frames, the difference is the CII indicating capabilities of the station transmitting the frame
  For control frames, 16 is subtracted from the difference, after which:
    Negative results indicate the station transmitting the frame has legacy (802.11p) capabilities
    Positive results are the CII indicating capabilities of the station transmitting the frame

## Slide 6: Various Combinations of Station Capabilities
Red arrows show durations that indicate NGV capability, circles show CII portion Green arrows show durations that indicate legacy-only capability
time
SIFS
Unicast Data
ACK
Initiator: NGV
Responder: NGV
time
time
SIFS
SIFS
Unicast Data
ACK
Initiator: NGV
Responder: Legacy
SIFS
Multicast Data
SIFS
(Legacy=0)
SIFS
Unicast Data
ACK
Initiator: Legacy
Responder: NGV
SIFS
(Legacy=0)
SIFS
Unicast Data
ACK
Initiator: Legacy
Responder: Legacy
SIFS
Multicast Data
SIFS

## Slide 7: Proposed CII Value Assignments
The table below shows the initial set of proposed CII value assignments. CII 15 and 31 are escape values, reserved to invoke an extended capability indication mechanism (to be defined by a future Task Group that has run out of CII values).
Capability of Sending Station | CII Value in Data/Mgmt Frames | CII Value in Control Frames
Legacy (802.11p) Only | 0 | 
NGV (802.11bd) | 1 | 17
First generation after 802.11bd | 2 | 18
reserved for future enhancements | 3 - 14 | 19 - 30
Using extended capability indication | 15 | 31
Note: CII values [16:31] could be used in group-addressed Data and Management frames to indicate additional capabilities

## Slide 8: Summary
We propose to encode capabilities to support NGV, and subsequent V2X amendments, using assigned duration increment values that are distinguishable from the legacy duration field values (for the same frames), but are fully interoperable because the increment values are less than aSIFSTime
At least fifteen enhanced capability values can be represented in the duration fields of frames transmitted in a 10MHz channel, which leaves codes to indicate capabilities of future revisions beyond 802.11bd

## Slide 9: Straw Poll #1
Do you agree with the following?
  NGV stations should indicate capabilities in frames carried in 802.11p PPDUs using assigned capability indication increment values, added to the duration values that legacy-only stations would use in the equivalent frames?
Y: 12
N: 0
A: 20

## Slide 10: Straw Poll #2 – NOT TAKEN, RAN OUT OF TIME
Do you agree to add the following text into Section 3.4 of SFD?
  “NGV (and subsequent) capabilities shall be indicated by adding a Capability Indication Increment value to the calculated duration value for use in the duration fields of frames transmitted within legacy-compatible frame exchange sequences. The initial CII value assignments shall be as shown on slide 7 of 11-19/0083r2. The CII usage and interpretation rules shall be based on the material shown on slides 4 and 5 of 11-19/0083r2.”
Y:
N:
A: