## Slide 1: Additional game use case over WLAN
Date: 2019-01-15
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 |  | kazuyuki.sakoda(at)sony.com
William Carney | Sony |  |  | William.Carney(at)sony.com

## Slide 2: Introduction
Game is a primary application of RTA
Real-time mobile gaming and Wireless console gaming are introduced to the group [1][2]
This presentation introduces additional variants of these game application which requires low latency capability

## Slide 3: Recap: Real-time mobile gaming [1], [3]
Abstract model of the Real-time Mobile Gaming is as follows:
Game Server
AP
Internet
Game Client

## Slide 4: Recap: Real-time mobile gaming [1], [3]
Abstract model of the Real-time Mobile Gaming is as follows:
Game Server
AP
Internet
Game Client
Total Bandwidth: 100kbps~1Mbps
E2E latency: < 100msec
Latency: < 10msec
Latency: < 10msec

## Slide 5: Cloud stream gaming
This is a variant of the cloud gaming
Game console itself is located on the cloud (Game Server), and the video pictures are streamed to Game Clients
Requires >5Mbps @720p HD
Requirements for RTA should consider eventual migration to UHD
Game Server
AP
Internet
Game Client

## Slide 6: Cloud stream gaming
This is a variant of the cloud gaming
Game console itself is located on the cloud (Game Server), and the video pictures are streamed to Game Clients
Requires >5Mbps @720p HD
Requirements for RTA should consider eventual migration to UHD
Game Server
AP
Internet
Game Client
Bandwidth: >5Mbps
E2E latency: < 100msec
Latency: < 10msec
Latency: < 10msec
Bandwidth: ~100kbps
E2E latency: < 100msec

## Slide 7: Recap: Wireless Console Gaming [2], [3]
Abstract model of a Wireless Console Gaming is as follows:
Game Console
AP
Internet
Game Console
AP
Game Console
AP
Game Server
Internet

## Slide 8: Recap: Wireless Console Gaming [2], [3]
Abstract model of a Wireless Console Gaming is as follows:
Game Server
AP
Internet
Game Console
Bandwidth: 8~28kbps
E2E Latency: < 100msec??
Latency: < 10msec
Latency: < 10msec
Bandwidth: 45~70kbps
E2E Latency: < 100msec??
AP
Latency: < 10msec
Latency: < 10msec

## Slide 9: Remote play gaming
This is another type of wireless gaming, variant of the cloud streaming
Similar to a type of Wireless Console Gaming but streaming is used instead of command transfer
Requires >5Mbps @720p HD
Requirements for RTA should consider eventual migration to UHD
Game Console
AP
Internet
Game Client
AP

## Slide 10: Remote play gaming
This is another type of wireless gaming, variant of the cloud streaming
Similar to a type of Wireless Console Gaming but streaming is used instead of command transfer
Requires >5Mbps @720p HD
Requirements for RTA should consider eventual migration to UHD
Game Console
AP
Internet
Game Client
Latency: < 10msec
Latency: < 10msec
AP
Latency: < 10msec
Latency: < 10msec
Bandwidth: >5Mbps
E2E Latency: < 100msec
Bandwidth: ~100kbps
E2E Latency: < 100msec

## Slide 11: Summary
Some gaming application uses video streaming when delivering picture to the client
These gaming application have similar requirement to what are described in [1] and [2], in terms of latency, and frame loss ratio on reverse link
These gaming application requires higher bandwidth on forward link >5Mbps, as it uses streaming which also requires low latency capability

## Slide 12: Suggested action
Include the following requirements to the target spec:
  Reverse link:
    Bandwidth: ~100kbps
    End-to-End Latency: < 100msec
    Intra-BSS Latency: <10msec
Amend RTA report to include these use case by either:
  Add streaming type of game to the real-time gaming section, or
  Add gaming flavor of the use in real-time video section
  Forward link:
    Bandwidth: >5Mbps
    End-to-End Latency: < 100msec
    Intra-BSS Latency: <10msec

## Slide 13: Strawpoll (1)
Do you think it is reasonable to include streaming game application to the RTA report?
  Yes:
  No:
  Abstain:

## Slide 14: References
[1] 11-18/1234r0, “Real-time Mobile Game vs Wi-Fi,” Kate Meng
[2] 11-18/1449r0, “Real-time Console Game Network Profile,” Karthik Iyer, et. al.
[3] 11-18/2009r0, “IEEE 802.11 Real Time Applications TIG Report,” Kate Meng

## Slide 15: Remote play gaming
This is another type of wireless gaming, variant of the cloud streaming
Similar to a type of Wireless Console Gaming but streaming is used instead of command transfer
Requires >5Mbps @720p HD
Requirements for RTA should consider eventual migration to UHD
Game Console
Game Client
AP