## Slide 1: 11az Negotiation of LTF Repetitions in IFTMR/IFTM Exchange (overview)
Date: 2018-07-09
Authors:

## Slide 2: Motivation/Background
Secure TB and nTB ranging uses LTF repetition
  Number of LTF Repetition is not included in Ranging Parameters field of Ranging Parameters element (D0.5)
18-1818r2 extended the STA Info field included in the Ranging NDP Announce frame with UL Rep and DL Rep subfields to support LTF repetitions
  can be used in both in secure and non-secure, TB and nTB modes
  a similar extension to the User Info field of the Trigger Frame (Ranging Variant) is needed
However, the negotiation phase did not include the UL Rep and DL Rep parameters
In this presentation, we extend the Negotiation to set an upper bound for the values in the UL Rep and DL Rep values in the Ranging NDP Announcement.

## Slide 3: Rationale for Negotiation
If UL Rep and DL Rep are not negotiated, the transmitter of Trigger frame (Ranging Variant) or Ranging NDP Announcement frame uses UL Rep and DL Rep values that are chosen by the transmitter (of the Ranging NDP Announcement or the Trigger Frame (Ranging Variant))
  The other end is mandated to implement support for the worst case (8 repetitions)
  Support for worst case may not be needed in all cases
Negotiating UL Rep and DL Rep allows for the two ends to participate in the determination of the values that both ends support

## Slide 4: Updated Ranging Parameters element
 | Element ID (255) | Length | Element ID Extension | Ranging Parameters | Ranging subelements
Octets | 1 | 1 | 1 | 34 | variable
 | Status Indication | Value | Secure LTF Required | Secure LTF Support | Max UL Rep | Max DL Rep | RSVD | ISTA2RSTA LMRFeedback | Format and Bandwidth | Number of Antennas
bits | 2 | 5 | 1 | 1 | 3 | 3 | 2 | 1 | 6 | 8

## Slide 5: What is signaled in these subfields
Max DL Rep (per antenna, per spatial stream)
  In IFTMR: The MAXIMUM number of LTF Repetitions in the DL NDP frames (that the ISTA supports)
  In IFTM: this is the MAXIMUM number of LTF repetitions that the RSTA may include in DL NDP frames
    0 <= Number of DL LTF Repetitions <= Max DL Rep value in the corresponding IFTMR (non Secure nTB or non Secure TB)
    1 <= Number of DL LTF Repetitions <= Max DL Rep value in the corresponding IFTMR (Secure nTB or non Secure TB)
    This value is referred to as RSTA Assigned DL Rep
Note: the value for DL Rep subfield in the STA Info field of the Ranging NDP Announcement frame shall be in the range 0 <= DL Rep <= RSTA Assigned DL Rep; defining the number of HE-LTF field repetitions in the DL NDP frames exchanged in non-Secure nTB or TB Ranging exchange.
Note: the value for DL Rep subfield in the STA Info field of the Ranging NDP Announcement frame shall be set to RSTA Assigned DL Rep; defining the number of HE-LTF field repetitions in the DL NDP frames exchanged in Secure nTB or TB Ranging exchange.

## Slide 6: What is signaled in these subfields
Max UL Rep (per antenna, per spatial stream)
  In IFTMR: The MAXIMUM number of LTF Repetitions in the UL NDP frames (that the ISTA supports)
  In IFTM: this is the MAXIMUM number of LTF repetitions that the ISTA may include in UL NDP frames
    0 <= Number of UL LTF Repetitions <= Max UL Rep value in the corresponding IFTMR (non Secure nTB or non Secure TB ranging)
    1 <= Number of UL LTF Repetitions <= Max UL Rep value in the corresponding IFTMR (Secure nTB or Secure TB ranging)
    This value is referred to as RSTA Assigned UL Rep
Note: the value for UL Rep subfield in the STA Info field of the Ranging NDP Announcement frame and in the User Info field of the Trigger frame (Ranging Variant Sounding sub-variant) shall be in the range 0 <= UL Rep <= RSTA Assigned UL Rep; defining the number of HE-LTF field repetitions in the UL NDP frames exchanged in non-Secure nTB or non-Secure TB ranging exchanges.
Note: the value for UL Rep subfield in the STA Info field of the Ranging NDP Announcement frame and in the User Info field of the Trigger frame (Ranging Variant, Secure Sounding sub-variant) shall be set to RSTA Assigned Max UL Rep; defining the number of HE-LTF field repetitions in the UL NDP frames exchanged in Secure TB and nTB Ranging exchanges.

## Slide 7: Strawpoll
We support negotiation of the maximum number of HE-LTF Repetitions (RSTA assigned {UL|DL} Rep) to be used in the uplink and downlink directions as part of the IFTMR/IFTM exchange; and use the negotiated values to determine the corresponding
  values of the UL Rep and DL Rep subfields in the STA Info field of Ranging NDP Announcement frame for non Trigger based ranging and
  the values of the UL Rep User Info field of Trigger Frame (Ranging Variant – sounding and secure-sounding sub-variants) for Trigger based ranging
  where
  0 <= {UL|DL} Rep <= RSTA assigned {UL|DL} Rep (in non Secure mode TB and nTB modes)
  RSTA assigned {UL|DL} Rep (in Secure TB and nTB modes), where RSTA assigned {UL|DL} Rep >= 1
Y: N: Abstain:

## Slide 8: How does this all work?
At the end of a successful negotiation, the RSTA Assigned UL Rep and RSTA Assigned DL Rep are defined.
RSTA Assigned {UL|DL} Rep value shall be >= 1 for Secure nTB and TB sessions
In the STA Info field in the Ranging NDP Announcement frame at the start of the non-Trigger based ranging phase or the User Info field in the Trigger frame (Ranging variant – sounding and secure-sounding sub-variants) at the start of the Trigger based ranging phase, shall set the values of the
  UL Rep subfield to 0 < UL Rep <= RSTA Assigned UL Rep, in Non Secure TB and nTB ranging mode or to UL Rep = RSTA Assigned UL Rep in Secure TB and nTB ranging modes
  DL Rep subfield to 0 < DL Rep <= RSTA Assigned DL Rep, in Non Secure TB and nTB ranging mode or to DL Rep = RSTA Assigned DL Rep in Secure TB and nTB ranging modes