## Slide 1: Proposal for Uplink Broadcast Requirements
Date: 2019-01-10
Authors:

## Slide 2: Abstract
This presentation provides a preliminary security threat analysis and outlines requirements for uplink broadcast services.

## Slide 3: Security Threats
Threats | Category | Ranking | Notes
Attacker uses malicious STAs to bombard the server with fake packets | Availability | Low | Note1 : Not different from DoS attacks than can happy today by large number of fake devices sending IP packets to specific IP address and port Note2: To reduce impact of this DoS attack it may be possible for AP to do some filtering
Attacker sends a command to the server on behalf of a valid STA | Identity | High | 
Attacker (as man in the middle) modifies the packet sent by a valid STA | Integrity | High | 
Attacker replays the packet that was previously sent by a valid STA | Replay Attack | High | 
Attacker intercepts the packet form a valid STA to server and extracts important information about the user’s identity and behavior | confidentiality | High | 

## Slide 4: Security Requirements
STA (for outbound packets to the server)
  Shall be able to proof its identity to the server
  Shall be able to integrity protect packets sent to the server with replay attack prevention
  Shall be able to confidentiality protect user identity and content of the packets sent to the sever with replay attack prevention
Server (for inbound packets from STA)
  Shall be able to detect DoS attack and implement a recovery procedure
  Shall be able to verify the identity of the STA
  Shall be able verify the integrity of the packet with replay attack detection
  Shall be able decrypt the packet with replay attack detection
AP
  Should be able to verify the STA before forwarding the packets

## Slide 5: BCS Uplink Requirements
E2E security w/ confidentiality and integrity between STA and Server
AP should be able to verify the STA before forwarding the packets
No association/handshake with AP required