## Slide 1: What is a broadcast service?
Date: 2019-01-14
Authors:

## Slide 2: Abstract
What is a broadcast service?

## Slide 3: General – downlink broadcasts
For purposes of efficiency the AP shouldn’t broadcast all services all the time
AP shouldn’t jam/spam the wireless medium with frames that are of no interest/value to associated/nearby STAs
AP
STA1
STA2
STA3
Broadcast Services

## Slide 4: Downlink broadcasts BCS AP states
For purposes of efficiency the AP shouldn’t broadcast all services all the time
Maintain different states for the BCS at the AP
  Available at the AP, and actively transmitting
  Available at the AP, but not currently transmitting
  Are there other states?
AP
STA1
STA2
STA3
Active Services:
BCS1
BCS2
Available Services:
BCS1
BCS2
BCS3
BCS4
Broadcast Services

## Slide 5: Associated STAs – downlink broadcasts
For purposes of efficiency the AP shouldn’t broadcast all services all the time
Broadcast Services (BCS) should be a stateful concept
  AP tracks which STA is currently receiving the service
STAs involved in controlling particular BCS(s)
  Different models could be considered
  Could be a start/stop request
  Could be a request to subscribe/unsubscribe
AP
STA1
STA2
STA3
Active Services:
BCS1
BCS2
Available Services:
BCS1
BCS2
BCS3
Broadcast Services
Subscribed to:
BCS1
Subscribed to:
BCS1
BCS2
Subscribed to:
BCS2

## Slide 6: Broadcasts Unassociated
STA1 is a sensor broadcasting observed data
  Data is transmitted as a BCS service
STA2 and STA3 are receivers of that information
  Data is received as a BCS service
STA1
STA2
STA3
BCS Transmitter
BCS Receiver
BCS Receiver

## Slide 7: Broadcast Service ?
So what is a Broadcast Service?
It needs to be defined at Layer 2.
  Not based on IGMP, IGMP-snooping and all that interesting IP layer multicast tech
    But is it designed to better support it?
It should not be:
  Solely multicast addressed frames (we have those already)
Is it a new grouping of STAs?
  If so, how does this work?
  Create/Clear Down the group
  Signal to other STAs
  Control the group
Is it a grouping of the frames?
  Assuming group-addressed frames are used, what properties make a group/set of group addressed frames into something called a broadcast service?