## Slide 1: Simulation of NGV PHY
Date: 2019-03-11
Authors:

## Slide 2: Abstract
This contribution presents some aspects of NGV PHY simulation. Best practices and reference implementations are presented for:
Channel models
Oversampling
Power Amplifier (PA) model
Phase noise
Carrier Frequency Offset (CFO)
Open source 802.11p model available at https://github.com/u-blox/ubx-v2x

## Slide 3: Channel Models
Topic 1

## Slide 4: Channel models
The Car-2-Car channel models [1] are a good basis for the evaluation of PHY performance under time and frequency-selective propagation conditions
These are tap-delay models defined by a sets of delay, power and Doppler spectra
In [1], the Doppler spectra after the 1st tap are defined as “Half-Bathtub”
A more mathematically accurate description would be “Asymmetric Jakes” with limits [0, fd]

## Slide 5: Channel models
MATLAB’s comm.RicianChannel allows for such spectrum definitions per channel tap
A reference definition is available in the ubx-v2x model
 | Tap1 | Tap2 | Tap3 | Units
Power | 0 | -14 | -17 | dB
Delay | 0 | 83 | 183 | ns
Doppler | 0 | 492 | -295 | Hz
Profile | Static | HalfBT | HalfBT | 
Table 1: Rural LOS Parameters
Tap1
Tap2
Tap3
Fig. Example of Doppler spectrum per channel tap for Rural LoS

## Slide 6: Enhanced channel models
A set of even more challenging channel models have been proposed in [2]
A reference implementation is also available in the ubx-v2x model
Table 1: Rural LOS Parameters
Name | Tap1 | Tap2 | Tap3 | Units
Power | 0 | -12 | -15 | dB
Delay | 0 | 84 | 183 | ns
Doppler | 0 | 94 | -1176 | Hz
Profile | Static | Half BT | Half BT | 
Table 2: Urban Approaching LOS Parameters
Name | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -11 | -13 | -15 | dB
Delay | 0 | 222 | 334 | 533 | ns
Doppler | 0 | 224 | 1173 | 588 | Hz
Profile | Static | Half BT | Half BT | Half BT | 
Table 3: Crossing NLOS Parameters
Name | Tap1 | Tap2 | Tap3 | Tap4 | Tap5 | Units
Power | 0 | -3 | -4 | -7 | -15 | dB
Delay | 0 | 220 | 266 | 475 | 630 | ns
Doppler | 0 | -142 | -542 | -155 | 320 | Hz
Profile | Static | Half BT | Half BT | Half BT | Half BT | 
Table 4: Highway LOS Parameters
Name | Tap1 | Tap2 | Tap3 | Tap4 | Units
Power | 0 | -11 | -13 | -17 | dB
Delay | 0 | 167 | 433 | 600 | ns
Doppler | 0 | 1941 | -1176 | -391 | Hz
Profile | Static | Half BT | Half BT | Half BT | 
Table 5: Highway NLOS Parameters
Name | Tap1 | Tap2 | Tap3 | Tap4 | Tap5 | Units
Power | 0 | -2 | -5 | -7 | -15 | dB
Delay | 0 | 100 | 500 | 867 | 1152 | Ns
Doppler | 0 | 50 | 1157 | -2352 | 1573 | Hz
Profile | Static | Half BT | Half BT | Half BT | Half BT | 

## Slide 7: Oversampling
Topic 2

## Slide 8: Oversampling
Contribution 19/0017r4 proposed the use of oversampling (8x) when simulating NGV
Oversampling is useful for investigations on
  Spectrum mask compliance
  PA non-linearity
  Multi Channel Operation
  Adjacent channel rejection

## Slide 9: Oversampling
Investigation of baseband performance should not be affected by oversampling
  Baseband equivalence should hold
Example: PER vs SNR
  10 MHz vs 40 MHz
  No significant difference in performance observed
10 MHz (no oversampling)
40 MHz (oversampling x4)
Rural LoS – 300 bytes

## Slide 10: Power Amplifier model
Topic 3

## Slide 11: Power Amplifier model
Model introduced in 11-00/294
RAPP model
Indicative parameters
  p = 3
  Output back-off (OBO) = 8 dB
Fig. Power amplifier model, taken from [3]

## Slide 12: Phase noise
Topic 4

## Slide 13: Phase noise
Usually modelled with a pole-zero model (11-03/814r31)
  PSD(0) = -100 dBc/Hz
  pole frequency fp = 250 kHz
  zero frequency fz = 7905.7 kHz
PSD(0) is not realistic and produces a negligible effect in PER performance
Higher values are more appropriate

## Slide 14: Carrier Frequency Offset
Topic 5

## Slide 15: Carrier Frequency Offset
CFO is often modelled as a uniformly distributed R.V. between -40 and 40 ppm
This is a very pessimistic scenario with extreme values derived from the maximum allowed frequency error at both ends
The state-of-the-art 802.11p chipsets have frequency errors of 5ppm or less (some even on the ppb region)
Also, the distribution of total CFO error is not uniform due to the additive effect between the error in Tx and Rx
ωTx+Rx : U(-40, 40) ppm
ωTx : U(-5, 5) ppm + ωRx : U(-5, 5) ppm
ω
P(ω)
-40
-10
10
40

## Slide 16: Conclusions
Some recommendations for 11p/NGV PHY simulation were given
Our goal is to match the real-world performance as closely as possible while maintaining low simulation complexity
All information presented is available for evaluation as open source software
Comments or proposals for improvement of this work are always welcome

## Slide 17: References
[1] M. Kahn, "IEEE 802.11 Regulatory SC DSRC Coexistence Tiger Team V2V Radio Channel Models," IEEE 802.11-14/0259r0.
[2] P. Alexander et. al, "Cohda-GM V2X Fading Channels".
[3] E. Perahia et. al, “Next Generation Wireless LANs”.