## Slide 1: Simulation of Multi-channel Interference
Date: 2019-03-14
Authors:
Onn Haran, Autotalks

## Slide 2: Abstract
Multi-channel interference mitigation scheme was presented in the last meeting (IEEE802.11-19-48/r0)
In a nutshell, defer transmission when transmission in adjacent channels is detected
Network simulation results of concurrent multi-channel operation, with and without mitigation scheme, are presented
The expansion of V2X service depends on using multiple channels without degrading communication range
March 2019
Onn Haran, Autotalks

## Slide 3: Network Simulation Environment
Concurrent operation of all MACs is simulated
PHY is modeled. A packet is received when power exceeds sensitivity
  -95dBm sensitivity
  +23dBm transmission power
  Applying two-ray model with adding 2dB attenuation for each blocking vehicle
  Enhanced adjacent channel rejection (25dB for QPSK ½)
March 2019
Onn Haran, Autotalks
All vehicles include two MACs tuned to two different channels
Vehicles are statically placed 25 meters apart on two-lanes road

## Slide 4: Simulated Traffic
Packets are transmitted periodically
  Random delay between transmissions: 95-105mS
Packet length is distributed uniformly
  Safety channel packet length: 200-400 bytes
  Second channel packet length: 400-800 bytes
  Simulation was also performed while doubling those lengths
  Channel load
    Each vehicle observes ~34 other vehicles
    Safety channel: ~20% load
    Second channel: ~40% load
    No DCC
March 2019
Onn Haran, Autotalks

## Slide 5: Network Simulation Results Histogram of communication range
March 2019
Onn Haran, Autotalks
Communication range [m]
Co-adjacent channel
Communication range drops due to multi-channel interference
Communication range [m]
Occurrences
Occurrences
Adjacent channel

## Slide 6: Network Simulation Results Histogram of diameter of no communication zone
March 2019
Onn Haran, Autotalks
Adjacent channel
Co-adjacent channel
Interference mostly blinds one channel when vehicle transmits second channel
For example: if interfering vehicle is 150m away, then no communication only between 150-175m
Communication range [m]
Communication range [m]
Occurrences
Occurrences
Interference spans far beyond second channel transmitter

## Slide 7: Results when Transmission is Deferred to Avoid Interferences Histogram of communication range
March 2019
Onn Haran, Autotalks
Interference-free operation
Communication range [m]
Occurrences
Adjacent channel

## Slide 8: Probability of Shortened Communication Range 20% / 40% Channel load
March 2019
Onn Haran, Autotalks
Adjacent channel detection threshold | Occurrence of range <100m | Occurrence of range <200m | Occurrence of range <300m
Baseline: no mitigation | 11.2% | 21.4% | 27.1%
-62dBm detection | 5.7% | 16.9% | 23.1%
-67dBm detection | 3.2% | 15.1% | 22.1%
-72dBm detection | 0.5% | 10.6% | 17.9%
-77dBm detection | 0.4% | 5.6% | 13.7%
-82dBm detection | 0.4% | 0.6% | 9.5%

## Slide 9: Probability of Shortened Communication Range Double packet length (double channel load)
March 2019
Onn Haran, Autotalks
Adjacent channel detection threshold | Occurrence of range <100m | Occurrence of range <200m | Occurrence of range <300m | Latency >10mS | Max latency
Baseline: no mitigation | 21.2% | 40% | 50.4% | 0.2% | 16.5mS
-62dBm detection | 13.3% | 34.2% | 45.2% | 0.3% | 20mS
-67dBm detection | 7.2% | 30.5% | 42.7% | 0.2% | 13.6mS
-72dBm detection | 2.1% | 22.2% | 36.9% | 0.3% | 18mS
-77dBm detection | 2.6% | 13.5% | 30% | 0.3% | 17mS
-82dBm detection | 2.5% | 3.4% | 22.9% | 0.4% | 17.6mS

## Slide 10: Observations
  Adjacent channel cannot be used without a mitigation scheme
  Mitigation scheme, based on deferring transmission upon energy existence in adjacent channel, effectively protects close vehicles without impacting latency
    Each MAC detects adjacent channel activity
    Mitigation scheme applies to vehicles with single MAC or dual MAC
Co-adjacent interference mostly impacts same vehicle
  A vehicle with two MACs can condition a transmission in one channel by inactivity of other channel
March 2019
Onn Haran, Autotalks

## Slide 11: Adjacent Channel Activity Detection
  It is very challenging to estimate the energy of the adjacent channel from just analyzing the main channel
    Most implementations would determine either “some energy exists in the adjacent channel” or “no energy exists in the adjacent channel”
  Better adjacent channel detection sensitivity increases the interference-free communication range
  Adjacent channel detection threshold should be further studied
    -72dBm is back-of-the-envelope value, roughly assuring 200m interference free communication range in LOS
March 2019
Onn Haran, Autotalks