## Slide 1: PHY designs for 11bd
Date: 2019-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo choi |  |  |  | js.choi@lge.com
March 2019

## Slide 2: Introduction
Through the several contributions[1-3], the various potential PHY features to be considered for 11bd have been discussed.
  OFDM numerology
  Wide bandwidth, i.e., 20MHz
  Frame format for 11bd
  Encoding : LDPC
  High MCS, i.e., 256QAM
  Mid-amble
  Etc.
Among the above features, wide bandwidth, i.e., 20MHz [1][2] was discussed in the previous meeting for achieving 2x throughput.
In this contribution, we investigate the performance of 20MHz transmission of 11bd and propose some PHY features to support the 20MHz bandwidth.

## Slide 3: 20MHz bandwidth
In our previous contribution[1], we discussed the various candidate PHY features to increase the throughput of 11bd.
  We focused on wide bandwidth, i.e., 20MHz for 11bd.
    In 5.9Ghz ITS band, we can use two 20MHz channels (Ch. 175 and Ch. 181) that were already allocated.
  Because 11p uses the only 10MHz channel, generally, by using wide bandwidth larger than 10MHz we can expect more increasing of throughput.
    Also, additional features may be considered in order to use 20Mhz efficiently from 11bd.
To efficiently use the 20MHz BW, we can leverage OFDM numerology of advanced WLAN system such as 11ac and 11ax.
  for 20MHz, we can consider the following OFDM numerologies.
 | OFDM Numerology | NFFT | NSD | Symbol duration* | Tone spacing | Downclock Ratio
Op.1 | 11ac 40MHz | 128 | 108 | 8us* | 156.25KHz | 2
Op.2 | 11ax 20MHz/ 11ac 80MHz | 256 | 234 | 16us* | 78.125KHz | 4
* : For example, CP = 1.6us for Op.1, CP = 3.2us Op.2

## Slide 4: 20MHz bandwidth
Ideally expected data rate according to OFDM numerology
  For the mandatory Max MCS(i.e., 16QAM, coding rate =1/2) of 11p
    Op.1 : 27Mbps , Op.2 : 29.25Mbps *
  Regardless of options for OFDM numerology, by using the 20MHz, we can increase the throughput by 2 times more than 11p.
Also, by leveraging the conventional OFDM tone plans, we may not need to redesign the preamble sequence.
  Depending on which OFDM numerology is used for 20MHz, we can reuse the conventional preamble sequences of STF and LTF that are defined for this tone plan.
We can also take into account that leveraging 11ac OFDM numerology to achieve better efficiency in 10MHz.
  for example, tone plan for 11ac 20MHz can be used for tone plan for 10MHz 11bd.
    * : Data rate (Mbps) = NSD x M-order x Coding rate / Symbol duration

## Slide 5: Performance of 20MHz
Rural LoS channel
  In low Doppler channel, both options show good performance, but op.1 shows slightly better performance
    Mx means a period of midamble
To apply the same midamble overhead, different midamble periods were applied to each numerology.

## Slide 6: Performance of 20MHz
Highway LoS channel
  It tends to be similar to the result of rural LoS channel.
    Mx means a period of midamble
To apply the same midamble overhead, different midamble periods were applied to each numerology.

## Slide 7: Performance of 20MHz
Highway NLoS channel
  In high Doppler channel, both options have a similar performance, but in high order modulation, for example, 16QAM, op2 shows slightly better performance.
    Mx means a period of midamble
To apply the same midamble overhead, different midamble periods were applied to each numerology.

## Slide 8: PPDU format for 11bd
11bd can define the new PPDU format to support the advanced features such as 20MHz on transmission.
  10MHz PPDU Format
  20MHz PPDU Format
  the new NGV PPDU includes the L-part (i.e., L-STF, L-LTF and L-SIG in 11p frame) and this is located before 11bd part.
    For 20MHz, L-part duplicates per 10MHz.
    That will ensure coexistence with 11p devices.
  For indication of advanced features for NGV data field, NGV Signal field can be included in NGV PPDU format.
    In next slide, we discuss the details for NGV signal field.
  For AGC and channel estimation of NGV data fields, this format includes the NGV-STF and NGV-LTF.

## Slide 9: PPDU format for 11bd
To support the potential PHY features discussed in the previous meeting, we need to indicate this information to the 11bd device.
  Generally, mature 802.11systems have used the Signal field for this purpose.
For example, following information need to be indicated.
    BW : 10/20MHz
    MCS including 256 QAM
    Encoding : BCC/ LDPC
    DCM
    Mid-amble
    Etc.

## Slide 10: PPDU format for 11bd
As defined on the PAR, 11bd can operate at least one mode such as high throughput mode or lower sensitivity mode.
  So, we can consider that 11bd PPDU supports these two transmission modes.
    For example, in 11ax, the additional PPDU format (i.e., ER-SU PPDU) was defined for longer range.
  Due to the usage of various transmission mode, it needs a method to distinguish them.
    For the indication, we can consider using early indication or signal field

## Slide 11: Packet classification
As specified in PAR[4], 11bd devices can decode both 11p PPDU and 11bd PPDU.
So, it needs to differentiate 11bd PPDU from 11p PPDU as early as possible to reduce the unnecessary operation at 11bd receiver.
  In the 802.11n/ac, for distinguishing between PPDUs, the early auto-detection method based on Q-BPSK was used.
  Similar with this method, 11bd can detect the PPDUs by using the one Q-BPSK symbol after L-SIG.
    For example, by checking the constellation of the symbol after L-SIG, we can differentiate the packet whether it is 11p or not.
      We may consider using automatic detection to inform the some information .
      We need to check of feasibility of this method whether it is enough robust or not.
And, we can also consider other methods for packet classification.

## Slide 12: Doppler Impact
As shown in [5][6], since high mobility is considered in C2C channel, 11bd can be affected by high Doppler frequency.
  It can cause serious performance degradation.
So, we need to consider the method to reduce the impact of high Doppler frequency.
  To solve the Doppler effect by high mobility, midamble has been applied in 11ax.
  Thus, we can consider utilizing the midamble in 11bd to mitigate the Doppler effect.
    It is not complicated to implement.
For example, Mid-amble can be constructed as following figure.
  Midamble may be constructed by NGV-LTF sequence.
  Midamble can be periodically inserted and transmitted per M symbols.
    We can consider the following period of midamble
      One period for a simple implementation
      Various period to support the transmission environment efficiently.
    For supporting of various period of midamble, we can consider the indication of this information by using the NGV SIG field.

## Slide 13: Performance of Mid-amble
Rural LoS
  Similar performance can be achieved with midamble in low Doppler channel.

## Slide 14: Performance of Mid-amble
Highway NLoS
  The performance with midamble is slightly worse than that with DFE in high Doppler channel.
    In the DFE, the channel estimated by known symbol at the previous symbol is used for decoding the current symbol.
  But, we can get the comparable performance by using a simple midamble minimizing additional complexity and hardware impact in receiver sides.

## Slide 15: Conclusion
Using 20MHz bandwidth is a good approach to increase the throughput of 11bd as 2 times than 11p.
To support the 20MHz BW, we need to define the 20MHz PPDU format.
  This format includes the L-part(i.e., L-STF, L-LTF and L-SIG).
  And, L-part is duplicated in 20MHz PPDU format.
For supporting the mode operation of 11bd, we need to method for distinguishing of high throughput mode and lower sensitivity mode.
Also, we verified that midamble can reduce the Doppler effect well as shown in this contribution.

## Slide 16: SP1
Do you agree to add the following to section 3 in 11bd SFD ?
  11bd supports the 10MHz bandwidth PPDUs.
  11bd supports the 20MHz bandwidth PPDUs.
  Y/N/A
  24/0/13

## Slide 17: SP2
Do you agree to add the following to section3 in the 11bd SFD?
  11bd PPDU format includes the STF, LTF and SIG
    STF, LTF and SIG are same that of 10MHz 11p PPDU.
  STF, LTF and SIG are duplicated in 20MHz PPDU format.
  Y/N/A
  23/0/14
11p preamble
11bd PPDU
11p preamble
11bd PPDU
STF
LTF
SIG
STF
LTF
SIG
STF
LTF
SIG

## Slide 18: SP3
Do you agree that 11bd defines a indication way for differentiating of high throughput mode and lower sensitivity mode?
  Y/N/A
  Withdrawn

## Slide 19: SP4
Do you agree to use the midamble for mitigation of the Doppler impact in 11bd ?
  Y/N/A
  25/ 0/15

## Slide 20: Motion 1
Move to add the following text to section 3 in 11bd SFD.
  11bd PPDU format includes L-STF, L-LTF, and L-SIG fields as shown in Figure 3.x
    L-STF means short training field of 11p.
    L-LTF means long training field of 11p.
    L-SIG means signal field of 11p.
  Move :
  Second :
L-LTF
L-STF
L-SIG
11bd PPDU
Figure 3.x 11bd PPDU format

## Slide 21: Motion 2
Move to add the following text to section 3 in 11bd SFD.
  11bd supports the 10MHz bandwidth PPDUs.
  11bd supports the 20MHz bandwidth PPDUs.
  Move :
  Second :

## Slide 22: Motion 3
Move to add the following text to section 3 in 11bd SFD.
  In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.
  Move :
  Second :
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG
11bd PPDU

## Slide 23: Reference
[1] IEEE 802.11-19-0009/r0 , Consideration on Features for 11bd
[2] IEEE 802.11-19-0016/r0, Potential PHY Designs for NGV
[3] IEEE 802.11-18-860/r3, NGV PHY Feasibility Discussions
[4] IEEE 802.11-18-0862/r5 , 802.11 NGV Proposed PAR
[5] IEEE 802.11-18-0858r0, c2c-channel-model-overview
[6] IEEE 802.11-19-017/r2 Simulation of NGV Channel Models

## Slide 24: Appendix
Simulation parameters
  Bandwidth : 10MHz, 20MHz
  Number of spatial stream : 1
  Encoding : BCC
  Midamble: uses VHT-LTF
  Number of data bits: 300 Bytes
  No Impairment
    No CFO and ideal timing
  Car2Car Doppler channel model [5,6]
  OFDM numerology:
    11ac 20MHz / 11ac 40MHz/ 11ac 80MHz
    11ax 20MHz
  Channel tracking
    DFE based : only for 11p (assume that known the Tx symbol)
    Mid-amble : for 11bd