## Slide 1: Rate Buckets in P802.11bd
Date: 2019-03-08
Authors:

## Slide 2: Abstract
802.11bd will continue to allow the legacy 802.11p rates for backwards compatibility
802.11bd PAR has two differing goals that may lead to two different new PPDU formats
    Longer Range
    Highly Robust

## Slide 3: PAR [1]
5.2.b. Scope of the project: This amendment defines modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) for vehicle to everything (V2X) communications for 5.9 GHz band as defined in clauses E.2.3 and E.2.4 of IEEE Std 802.11(TM)-2016; and, optionally, in the 60 GHz frequency band (57 GHz to 71 GHz) as defined in clause E.1 of IEEE Std 802.11(TM)-2016. This amendment defines at least one mode that achieves at least 2 times higher throughput (measured at the MAC data service access point) than as in IEEE Std 802.11(TM)-2016 operating at maximum mandatory data rate as defined in the 5.9 GHz band (12 Mb/s in a 10 MHz channel), in high mobility channel environments at vehicle speeds up to 250 km/h (closing speeds up to 500 km/h); this amendment also defines at least one mode that achieves at least 3dB lower sensitivity level (longer range), than that of the lowest data rate defined in IEEE Std 802.11(TM)-2016 operating in 5.9 GHz band (3 Mb/s in a 10 MHz channel); and this amendment defines procedures for at least one form of positioning in conjunction with V2X communications. This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.

## Slide 4: Discussion
At least 3 modes … at least 3 PPDU types
Legacy PPDU (802.11p)
High throughput PPDU (802.11bd mode A)
Long range PPDU (802.11bd mode B)

## Slide 5: Target Ratesets
Legacy 802.11p[2] (any new text needed?)
802.11bd High Throughput PPDU (Actual rates are TBD)
802.11bd Long Range PPDU (Target the same rates)
*All still assuming 10MHz channels in 5.9GHz band
3 | 4.5 | 6 | 9 | 12 | 18 | 24 | 27
3 | 4.5 | 6 | 9 | 12 | 18 | 24 | 27
6 | ? | ? | ? | ? | ? | 54? | 100?

## Slide 6: Open issues
Any chance we can retroactively rename the legacy rate set (802.11a 10MHz aka 802.11p)?
  Note 802 EC objections to “referencing obsolete amendments”.
  However the industry still calls it 802.11n, 802.11ac, etc.
  Need to treat this issue carefully either way.
2) How do we enable the upper layer application to choose the rateset and rate that it needs? (legacy, high throughput, or long range)
  For example choosing 6Mbps legacy PPDU for transmitting BSM, 6Mbps long range PPDU for sending Platooning Discovery message and high throughput 100Mbps PPDU for sensor sharing.

## Slide 7: Straw poll 1
Should 802.11bd consider multiple PPDU formats?
Yes
No
Abstain

## Slide 8: Straw poll 2
What kind of rates should the 802.11bd long range PPDU target?
Same rates as 802.11p
Mostly the same plus some lower rates
Mostly the same plus some higher rates
Abstain
3 | 4.5 | 6 | 9 | 12 | 18 | 24 | 27

## Slide 9: Straw poll 3
Should the 802.11bd MAC provide multiple rate buckets to upper layer based on the features such as “legacy compatibility”, “high throughput” and “long range”?
Yes
No
Abstain

## Slide 10: References
IEEE P802.11bd PAR https://development.standards.ieee.org/P1080000033/par
IEEE 802.11-2016 Table 17-4