## Slide 1: Consideration on 320MHz Bandwidth and 16 Spatial Streams
Date: 2019-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Sunwoong Yun |  |  |  | sunwoong.yun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contribution [1], we discussed PHY features to be considered for enabling potential EHT candidates
  We focused on several PHY candidates such as 320MHz bandwidth, 16 spatial streams (SS), etc.
A bunch of contributions proposed 6GHz or multi-band aggregation [2-12], and, in this case, we need to clarify how to support 320MHz bandwidth and 16 SS for developing PHY features
We consider the following two approaches
  Approach 1: EHT allows only up to 160MHz and 8 SS in each band as in 11ax, and EHT can support 320MHz or 16 SS by utilizing multiple bands at the same time
  Approach 2: EHT can support up to 320MHz or 16 SS in one band (e.g., 6GHz) and EHT can support much larger bandwidth or more SS by additionally utilizing multi-band aggregation
Several PHY designs shown in [1] may depend on the approach
The purpose of this presentation is to discuss and compare these two approaches and to gather information on what members have in mind

## Slide 3: BW and SS Related PHY Features
In [1], the following features are discussed for 320MHz or 16 SS candidates
  Tone plan
  EHT-STF / EHT-LTF sequence
  Preamble puncturing
  Phase rotation for legacy part
  EHT-SIGB
  Feedback overhead reduction
  LTF overhead reduction
  P-matrix
  CSD
We should design the above features when supporting 320MHz or 16 SS in each band is considered (approach 2) whereas 11ax features may be reused in case that each band supports the same bandwidth and SS as in 11ax (approach 1)

## Slide 4: Approach 1
The maximum allowable bandwidth and the maximum number of spatial streams supported in each band are the same as those of 11ax
  This means that we can use up to (contiguous/non-contiguous) 160MHz in 5/6 GHz and up to 8 SS in 2.4/5/6GHz
  11ax PHY features related to bandwidth and spatial streams can be reused
  By utilizing multi-band aggregation, we can transmit signals through multiple bands at the same time and can obtain higher throughput than 11ax
    For example, we can consider 8 + 8 SS transmission in 160 + 160MHz using 5GHz and 6GHz simultaneously*, and in this case, a peak throughput increase by 2x can be achieved
    Even in the multi-band aggregation, it seems that we don’t have to design new PHY features listed in the previous slide, i.e., we can just apply the 11ax features to each band
  Note that the target maximum throughput of EHT is 30 Gbps at the MAC data service access point [13] and the peak PHY rate of 11ax is about 10 Gbps, and thus, to achieve the target, we need additional methods to further increase the peak throughput in Approach 1
* This is equivalent to 16 SS transmission in 160MHz or 8 SS transmission in 320MHz

## Slide 5: Approach 2 (1/3)
In each band, the maximum allowable bandwidth is contiguous / non- contiguous 320MHz or the maximum number of spatial streams is 16 SS
  This means that we can use up to 320MHz in 6GHz or up to 16 SS in 2.4/5/6GHz
    There are many contiguous 160MHz channels and even contiguous 320MHz channels in 6GHz as shown in Appendix A, and thus we don’t have to waste the capacity of this band
  We can achieve a peak throughput increase by 2x (using 160MHz and 16 SS in 5GHz) or 4x (using 320MHz and 16 SS in 6GHz) without multi-band aggregation
    With multi-band aggregation, much higher throughput can be expected
  To this end, PHY features in slide 3 need to be developed
    For example, a tone plan for 320MHz needs to be designed for the 6GHz band
Issues for supporting up to 16 SS in each band
  16 antennas are needed per band and it causes cost and size increase
  To reduce the cost and size, we can consider antenna sharing between 5GHz and 6GHz bands, and by doing so, we can even flexibly use them to support these two bands
  To enable the antenna sharing, several hardware factors such as optimal antenna length, frequency tunable filter, oscillator and so on should be considered

## Slide 6: Approach 2 (2/3)
Issues for supporting up to 320MHz in 6GHz
  We need to decide what new bandwidths EHT supports
    Note that new bandwidths mentioned below are not the ones constructed across multiple bands (i.e., not the ones constructed from the multi-band aggregation) but the ones used within 6GHz
  The candidates of new bandwidths can be as follows
    Contiguous 320MHz / non-contiguous 320MHz (160+160 / 160+80+80 / 80+80+80+80 MHz)
  Additionally, we can also consider the bandwidths as below
    Contiguous 240MHz / non-contiguous 240MHz (80+160 / 80+80+80 MHz)
  In terms of the frequency utilization, it would be better that various bandwidths are adopted
    Utilizing both 240MHz and 320MHz provides better throughput compared to using only 320MHz as shown in Appendix B
    Also, having a variety of non-contiguous bandwidths can further increase efficiency
    Furthermore, in conjunction with preamble puncturing, efficiency can be much more enhanced

## Slide 7: Approach 2 (3/3)
Issues for supporting up to 320MHz in 6GHz (cont.)
  When 320MHz with preamble puncturing is supported, supporting 240MHz may not offer an additional throughput gain
    Bandwidths constructed from 320MHz with preamble puncturing can include all the cases of 240MHz with preamble puncturing
  However, note that it is not always possible to support 320MHz because of hardware limit or insufficient available channels, hence it seems that supporting 240MHz definitely has an advantage
  The following aspects need to be also considered carefully
    Signaling overhead may become larger especially with preamble puncturing based on 20MHz CCA
    Various BW capable RF and DSP designs may increase hardware complexity

## Slide 8: Summary
Approach 1: EHT allows only up to 160MHz and 8 SS in each band as in 11ax
Approach 2: EHT can support up to 320MHz or 16 SS in one band
For achieving PAR requirement, we prefer Approach 2 which can attain a substantial peak rate increase
  More efficient tone plan in contiguous 160MHz can be considered
  To enhance efficiency, 240MHz bandwidth can be adopted
  Depending on the tone plan, STF and LTF sequences can be designed
  Feedback and LTF overhead reduction can be considered
  Dimension extension for P-matrix and CSD tables can be considered
 | Approach 1 | Approach 2
Pros | Reuse existing PHY features | Substantial increase in peak throughput
Cons | Relatively small increase in peak throughput | Need new PHY designs Need enhanced RF and DSP designs

## Slide 9: SP #1
Do you agree to support up to 16 SS in each band?
Y/N/A

## Slide 10: SP #2
Do you agree to support the bandwidth up to 320MHz in 6GHz?
Y/N/A

## Slide 11: SP #3
Do you agree to support the bandwidth of 240MHz in 6GHz?
Y/N/A

## Slide 12: Appendix A
Unlicensed 6GHz band
5.925GHz ~ 6.425GHz (500MHz) | U-NII-5
6.425GHz ~ 6.525GHz (100MHz) | U-NII-6
6.525GHz ~ 6.875GHz (350MHz) | U-NII-7
6.875GHz ~ 7.125GHz (250MHz) | U-NII-8

## Slide 13: Appendix B (1/2)
Average throughput gain with 240MHz capability
  Case 1: w/o 240MHz capa. (80/160/320MHz capa.)
  Case 2: w/ 240MHz capa. (80/160/240/320MHz capa.)
  Assume four 80MHz channels, i.e., primary, secondary 80MHz channels and secondary 160MHz channel which has two 80MHz channels
  Consider the probability that each 80MHz channel is idle is p
  When primary and secondary 80MHz channels are idle, assume the following
    If one of the two 80MHz channels in secondary 160MHz channel is busy, only 160MHz transmission is possible in case 1
    If one of the two 80MHz channels in secondary 160MHz channel is idle, 240MHz transmission is possible in case 2

## Slide 14: Appendix B (2/2)
Average throughput gain with 240MHz capability (cont.)
  Thus, we simply consider the following BW transmission in each case depending on each 80MHz channel status
  According to p, case 2 provides the average throughput gain compared to case 1 as follows
P | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
Gain [%] | 1.62 | 5.04 | 8.65 | 10.94 | 12.42 | 12.34 | 10.83 | 8.41 | 4.61
In each p, we simulated 50,000 times and obtained the average bandwidth size used in each case
throughput gain = (BW2-BW1)/BW1 x 100 [%]
BW1 = avg. BW size for case 1
BW2 = avg. BW size for case 2

## Slide 15: References
[1] 802.11-18/1967r1 Overview of PHY Features for EHT
[2] 802.11-18/0789r6 Extreme Throughput (XT) 802.11
[3] 802.11-18/1461r1 Discussions on the PHY features for EHT
[4] 802.11-18/1547r0 Technology Features for 802.11 EHT
[5] 802.11-18/1549r0 Recommended Direction for EHT
[6] 802.11-18/1184r1 Follow up Discussions on Throughput Enhancement
[7] 802.11-18/1155r1 Multi-AP Enhancement and Multi-Band Operations
[8] 802.11-18/1161r0 EHT Technology Candidate Discussions
[9] 802.11-18/1533r0 View on EHT Candidate Features
[10] 802.11-18/1171r0 View on EHT Objectives and Technologies
[11] 802.11-18/857r0 Beyond 802.11ax – Throughput Enhancement Utilizing Multi-bands across 2.4/5/6 GHz Bands
[12] 802.11-18/1525r1 EHT features for Multi-Band Operation
[13] 802.11-18/1231r4 802.11 EHT Proposed PAR