## Slide 1: Proposed TIG on MAC address randomization
Date: 2019-03-11
Authors:

## Slide 2: Abstract
Proposal for a Technical Interest Group (TIG), to do first analysis of impacts of randomized MAC addresses on features and facilities of 802.11, and determine if next steps are needed or desired.

## Slide 3: Random MAC addresses - Current status
Randomizing a device’s MAC address to anonymize users from “sniffing” is generally agreed as desirable for privacy
Most major mobile/portable operating systems are already deployed with some form of MAC address randomization capability, and periodic/frequent address changes, with:
  Varying approaches to opt-in/opt-out/default behaviors
  Varying conditions for use of random address and frequency of changes – pre-association or while associated
It is likely that randomization will see more use/deployment in the near future (based on disclosed plans, and rumors)
802.11aq amendment codified some uses
  mostly focused on pre-association,
  but mentions while-associated use, which may also need to be codified

## Slide 4: Random MAC addresses - Impacts
Randomized addresses can/are having effects on upper-layer objectives:
Disrupts networks using MAC address to identify users (which is now explicitly not recommended)
  Trade-off of user desire for individualized treatment versus their desire for privacy
Disrupts networks from tracking users by MAC address (also now explicitly not recommended)
  Businesses use MAC address to track foot traffic for their own value, value to users is indirect
The above, and other similar impacts, can be addressed with higher-layer solutions for user identification, without loss of privacy. (Recommended – See WBA liaison exchange, 11-18/1988r2.)

## Slide 5: Random MAC addresses – Impacts 2
But, randomized addresses can also affect purposes within layer 2:
Potentially disrupts networks’ layer-2 tracking and steering, through lack of understanding multiple device appearances are actually the same device in different contexts
Disrupts analytics and troubleshooting, through lack of correlation of actions/events to the same device
These result in direct impact on network management and operation, which in turn affects user experience.
It is valuable to investigate these impacts, and possible mitigations

## Slide 6: MAR TIG Formation motion
“Approve formation of a MAC address randomization (MAR) TIG to investigate the:
  current and planned implementations of random MAC addresses in devices, and current and planned 802.11/802 Standards treatment of random MAC addresses
  impact on 802.11 features from randomized MAC addresses and/or changing addresses during:
    Pre-association (stateless)
    Preparing for (creating shared state) and during associations
  potential mechanisms to address the above impacts, through:
    Implementation options, or possible guidelines document
    Modifications to the Standard, if any, and recommend continuing work (Study Group/PAR)
The TIG is to complete a report on this topic at or before the November 2019 session.”