## Slide 1: A simple solution to the problem related to Energy Detect of an 11ba signal
Date: 2019-03-12
Authors:

## Slide 2: Abstract
Concern has been expressed related to a that the 802.11ba signal may be OFF for 8us, and as a consequence a device performing Energy Detect may erroneously classify the channel as idle and start transmitting on top of the 11ba packet. This contribution presents a simple solution for this problem which is entirely transparent for the WUR receiver.

## Slide 3: Proposed solution
Transmit a ED signal in the unused part of the 20 MHz channel
  Will be filtered out by the channel selective filter of the WUR
  Will ensure that Energy detection works
Does not impact transmission power of WUS in PSD limited regions, which is the most challenging
5
WUS
4 MHz
20 MHz

## Slide 4: An example
  The ED signal may for instance be OOK, with the signal being ON if the WUS is OFF and vice versa. This would ensure that no ED signal is sent when not needed.
  If the signal is generated by an IFFT, this is conveniently done by just allocating some of thesub-carriers to the ED signal
  It is perfectly fine to still have a spectrum mask on the WUS, the ED signal can have a PSD more than 3 dB below the WUS
5
WUS
4 MHz
20 MHz