## Slide 1: Replay Attack to Secured TB Ranging
Date: 2019-03-12
      Mar. 2019

## Slide 2: Introduction
The secured TB ranging has the following features
  The SAC code for UL\DL NDPs is carried in TF for sounding
  DL NDP has separate HE-LTF fields for different ISTA
  ISTA’s HE-LTF field is constructed based on the ISTA’s SAC
  NDPA indicates HE-LTF field allocation of the ISTA
  NDPA is broadcast packet with no security protection
This submission relates to CID 1580 in TGaz LB240 Comment
      Mar. 2019

## Slide 3: Secured TB Ranging Sequence
For DL NDP, NDPA allocates HE-LTF 1 to ISTA1 and HE-LTF2 to ISTA2
DL NDP
UL
NDP
TF
RSTA
ISTA2
UL
NDP
UL
NDP
DL
NDPA
UL
NDP
TF
Preamble
HE LTF 1
HE LTF 2
SIFS
SIFS
SIFS
SIFS
SIFS
DL
LMR
SIFS
ISTA1
ISTA2
ISTA1
      Mar. 2019

## Slide 4: Replay Attack to Secured TB Ranging
DL NDP
UL
NDP
TF
RSTA
ISTA1
ISTA2
UL
NDP
UL
NDP
DL
NDPA
UL
NDP
TF
Preamble
HE LTF 1
HE LTF 2
SIFS
SIFS
SIFS
SIFS
SIFS
DL
LMR
SIFS
Attacker
fake
NDPA
HE LTF 1
Fake NDPA: HE-LTF 1 to ISTA2 and HE-LTF2 to ISTA1
Attacker copies HE-LTF1 of DL NDP and replays HE-LTF1 during HE-LTF2 of DL NDP
ISTA1 is attacked and ISTA2 gets an invalid ToA
      Mar. 2019

## Slide 5: Detection of Replay Attack
Option 1: NDPA frame includes SAC for authentication
  Requires to define SAC (16 bits) for UL NDP and DL NDP separately
  The sounding TF carries SAC for UL NDP and the NDPA carries SAC for DL NDP
    Cause two modes for random bits generation for TB ranging (two SAC) and NTB ranging (single SAC)
  If ISTA receives NDPA with unknown SAC, ISTA will discard the NDPA
Option 2: Include the HE-LTF allocation information in DL LMR
  Offset (6 bits), DL N_STS (3 bits) and DL Rep (3 bits)
  DL LMR is protected frame
  The ISTA compares the HE-LTF allocation information in NDPA and DL LMR
    If not match, ISTA will discard the measurements
      Mar. 2019

## Slide 6: Detection of Replay Attack (cont’d)
Option 3: For each ISTA, define ToD/ToA of DL NDP separately based on the start of each ISTA’s HE-LTF field
  According to legacy FTM, the ToD /ToA of the DL NDP is defined based on the timing when the start of the preamble of the DL NDP appears at RSTA’s or ISTA’s s transmit or receive antenna connector
  To detect the replay attacker, the RSTA and ISTA can define the ToD and ToA based on the start of the corresponding HE-LTF field
    The ToD is defined based on the timing when the start of the HE-LTF field appears at RSTA’s transmit antenna
    The ToA is defined based on the timing when the start of the HE-LTF field appears at ISTA’s receive antenna
    When there exists replay attack, the RTT will be significantly increased, such that it can be detected.
  Downside is it may need hardware change for derivation of ToD/ToA and if the real range is larger than 2160m, it may trigger false alarm
      Mar. 2019

## Slide 7: An example for Option 3
DL NDP
UL
NDP
TF
RSTA
ISTA2
UL
NDP
UL
NDP
DL
NDPA
UL
NDP
TF
Preamble
HE LTF 1
HE LTF 2
SIFS
SIFS
SIFS
SIFS
SIFS
DL
LMR
SIFS
ISTA1
ISTA2
ISTA1
Reference point for ISTA1 ToD and ToA
Reference point for ISTA2 ToD and ToA
In DL NDP, the reference point for ISTA1’s and ISTA2’s ToA and ToD
      Mar. 2019

## Slide 8: An example for Option 3 (cont’d)
DL NDP
UL
NDP
TF
RSTA
ISTA1
ISTA2
UL
NDP
UL
NDP
DL
NDPA
UL
NDP
TF
Preamble
HE LTF 1
HE LTF 2
SIFS
SIFS
SIFS
SIFS
SIFS
DL
LMR
SIFS
Attacker
fake
NDPA
HE LTF 1
RSTA derives ISTA1’s ToD based on the correct reference point, and ISTA1 derives the corresponding ToA based on the fake reference point
ISTA1’s RTT is increased by the duration of the field HE-LTF1
The minimum duration of HE-LTF1 is 14.4us -> 2160m increase in range (invalid)
Reference point for ISTA1 ToD
Reference point for ISTA1 ToA
      Mar. 2019

## Slide 9: Conclusions
A replay attack model for secured TB ranging was investigated
Different solutions are proposed for detecting the replay attacker
Will further investigate this attacker model and follow up in future meeting
      Mar. 2019