IEEE P802.11
Wireless LANs
Summary of discussions on randomized and changing MAC addresses 2014-2019
Date: 2019-04-01
Author(s):
Name	Affiliation	email
Amelia Andersdotter	ARTICLE19	amelia@article19.org

Abstract
This document summarizes the discussions on MAC randomization in IEEE P802.11 between 2017-2019, and presents a collection of academic research, as well as previous IEEE standardisation work relating to randomized and changing MAC addresses.
Background outside of IEEE 802.11

IEEE 1609 WAVE

The idea of randomizing a MAC address to enhance privacy protection is not new (Gruteser (2005)). IEEE 1609.4 WAVE introduced MAC "re-addressing" as a privacy enhancement measure as far back as 2012 following concerns relating to geolocation tracking of connected vehicles. There is a large body of research on the use of changing or randomized identifiers to mitigate privacy concerns in vehicular networks (Ch. 2.3.2, Förster, 2017).

IETF

Standards work external to the IEEE which takes into account randomized MAC addresses includes new methods for generating IPv6 addresses developed by the IETF. While previous versions of IPv6 have assumed the IPv6 can be generated from the MAC identifier, this is no longer required.

Regulatory

Regulatory requirements on network operators motivate closer investigation of stronger protections against non-consensual geolocation tracking (Autoriteit Persoongegevens (2014), Bouchenard (2015), Datainspektionen (2015), FCC (2015)). As regulatory requirements stabilize in this field, it may be an advantage to be able to offer network operators a "clean default". Namely, a situation wherein which an operator does not need to worry that default analytics and trouble-shooting mechanisms risk conflicting with such requirements.

Deployment

Leading mobile OSs have already started introducing various software-based MAC randomization mechanisms. They have been studied with respect to their efficiency in protecting privacy of their users (Matte et al (2016), Martin et al (2017)). Work on and deployment of MAC randomization is continuing in this sector.

Sufficiency

There is a lot of research on tracking of individual devices in wireless networks (f. ex. Cunche (2013), Sapiezynski (2015)). The IEEE 802 Privacy ECSG has further studied possibilities of profiling of individual devices in the absence of a permanent unique MAC address (privescg-16-0003-00-0000, Vanhoef et al (2016)). It is clear that MAC randomization is not in itself a sufficient guarantee for privacy of individual users, but one partial solution among many.

The background in IEEE 802 LMSC

MAC randomization has been visible in IEEE 802 LMSC since 2014. The future expected prevalence av MAC randomization techniques was, for instance, raised by commenters in the draft 0.3 ballot of what is now IEEE 802C.

The privacy threat mitigation potential of MAC randomization was also studied by 802 LMSC members at the Privacy ECSG in 2014 (privescg-14-0026-01-0000, privecsg-14-0025-01-0000) and 2015 (privescg-15-0028-00-0000).

Together with the assessment of software-driven MAC randomization referenced above, this work lead to the inclusion of MAC randomization as a privacy enhancing feature in the .11aq Pre-Association Service Discovery Task Group amendment to the 802.11-2016. This work can be revisited at the "TGaq (inactive)" repository of the 802.11 mentor website. The .11aq amendment was approved by the IEEE Standards Association Standards Board in June 2018.

In September 2018, three months after the publication of the official 802.11aq amendment, the IEEE 802.11 WG received a liaison statement from the Wireless Broadband Alliance (WBA) detailing network operator concerns with the disappearance of clear-text sufficiently-permanent unique device identifiers (11-18-1579-00-0000).

The ARC SC made efforts to address the concerns raised by the WBA in a response approved by the 802.11 Working Group in November 2018 (11-18-1988-02-0arc). In this response, the Working Group noted that some issues raised by WBA merit further consideration.

MAC randomization issues identified by ARC SG

1. The WBA had raised with IEEE 802.11 that "A single device using different MAC addresses in different bands and/or different SSIDs."

   The IEEE 802.11 responses was: "[W]e agree that band steering in this scenario is likely an issue. 802.11 WG should look into this, perhaps providing recommendations about SSID assignment, depending on network deployment and goals. 802.11 should coordinate with Wi-Fi Alliance on this topic."
2. WBA expressed concern that "Even if the MAC address is “stable” for a given SSID, many clients will use the broadcast SSID in probe requests, and hence there is again no stability in MAC address."

   The IEEE 802.11 response was: "[C]lient steering is likely an issue. 802.11 WG should look into this. 802.11 should coordinate with Wi-Fi Alliance on this topic, depending on our findings."
3. WBA raised that "Analytics may rely on MAC addresses for identification."

   The IEEE 802.11 response was: "We realize that some types of network analytics and troubleshooting are done at the low layers of the network stack, and don’t have access to high-level concepts for identification. 802.11 WG should look into this."

In relation to the last point, the IEEE 802.11 also observed that they agreed with WBA that "identification of manufacturer, based on OUI portion of the MAC address" would not be possible for devices with a randomized MAC address.

Work in other IEEE 802 LMSC Working Groups

The network analytics and device identification issue was discussed in the IEEE 802.1 OmniRAN Task Group in its F2F meeting on 15 January 2019 (omniran-19-0005-02-00TG). The assertion was made that device manufacturer identification and network analytics and troubleshooting would be an issue in the absence of MAC identifiers (omniran-19-0002-00-CQ00).

It has been agreed that OmniRAN should be presented with a "draft protocol proposal for secure signaling of a static device identifier to the access network" and "functional requirements describing the need to provide the possibility of fixed device identifiers" (omniran-19-0005-02-00TG).

Summary of work going ahead

Bearing this in mind, RCM TIG was created to investigate

- Current and planned implementations of random and changing MAC addresses in devices, and
- Current and planned 802.11/802 Standards treatment of randomized MAC addresses
- Impact on 802.11 features from randomized MAC addresses and/or changing addresses during:
  - Pre-association (stateless)
  - Preparing for (creating shared state) and during associations
- Potential mechanisms to address the above impacts, through:
  - Implementation options, or possible guidelines document
  - Modifications to the Standard, if any, and recommend continuing work (Study Group/PAR)

References:

Autoriteit Persoongegevens, z2014-00944, Wifi-tracking van mobiele apparaten in en rond winkels door Bluetrace.

C. Bouchenard, JC Decaux’s pedestrian tracking system blocked by french data regulator, Marketinglaw, 2015. http://marketinglaw.osborneclarke.com/advertisingregulation/jc-decauxs-pedestrian-tracking-system-blockedby-french-data-regulator/.

M. Cunche. I know your MAC Address: Targeted tracking of individual using Wi-Fi, International Symposium on Research in Grey-Hat Hacking - GreHack, Nov 2013, Grenoble, France. <hal-00858324>

Datainspektionen, 31702-2015, Tillsyn enligt personuppgiftslagen (1998:204) av Västerås Citysamverkan AB.

Federal Trade Commission, Retail tracking firm settles FTC charges it misled consumers about opt out choices, 2015. https://www.ftc.gov/news-events/press-releases/2015/04/retail-tracking-firm-settles-ftc-charges-it-misled-consumers

D. Förster, Verifiable Privacy Protection for Vehicular Communication Systems, Dissertation, Ulm University, Germany, 2017.

M. Gruteser, D. Grunwald, Enhancing Location Privacy in Wireless LAN Through Disposable
Interface Identifiers: A Quantitative Analysis, Mobile Networks and Applications 10, 315–325, 2005.

J. Martin, T. Mayberry, C. Donahue, L. Foppe, L. Brown, C. Riggins, E. C. Rye, D. Brown, A Study of MAC Address Randomization in Mobile Devices and When it Fails, Proceedings on Privacy Enhancing Technologies ; 2017 (4):268–286

C. Matte, M. Cunche, F. Rousseau, M. Vanhoef, Defeating MAC Address Randomization Through Timing Attacks, in Proceedings of the 9th ACM Conference on Security; Privacy in Wireless and Mobile Networks, WiSec ’16, pages 15–20. ACM, 2016.

P. Sapiezynski, A. Stopczynski, R. Gatej, S. Lehmann, Tracking Human Mobility Using
WiFi Signals, PLoS ONE 10(7): e0130824, 2015, doi:10.1371/journal.pone.0130824

M. Vanhoef, C. Matte, M. Cunche, L. Cardoso, F. Piessens. Why MAC Address Randomization is not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms, in ACM AsiaCCS, 2016.