## Slide 1: Midamble Compression
Date: 2019-05-13
Authors:

## Slide 2: Introduction
Midamble is an effective Doppler-mitigation technology that has a simple receiver design.
Dense Midamble will reduce the system goodput.
Sparse Midamble may not support higher modulation order.
In this contribution, we will investigate compressed Midamble.

## Slide 3: Compressed Midamble
In 11ax, 2xLTF and 1xLTF are adopted to reduce preamble overhead.
Similar concept can be used in 11bd Midamble design to reduce Midamble overhead.
2x compressed Midamble can be generated by
  Populating every even tone in frequency domain and
  Taking half of the waveform in time-domain.
  Same GI duration as normal LTF may be prepended to resolve channel delay spread.
With 2x compression, the Midamble overhead is reduced almost by half.

## Slide 4: Design Considerations
Receiver channel interpolation
  Channel on even tones can be directly estimated using Midamble.
  Channel on odd tones needs to be interpolated, which adds some receiver complexity.
New Pilot locations
  Current 11ac pilots are located on the odd tones.
  Using interpolated pilot channel for CPE/CFO tracking can affect performance.
  Need to move pilot location to adjacent even tones.

## Slide 5: Midamble Design
With compressed Midamble introduced, 11bd Midamble can use the following options.
  Option 1: one regular NGV-LTF (default design)
  Option 2: one 2x compressed NGV-LTF (LTF-2x)
    Achieves better efficiency
  Option 3: repeated 2x compressed NGV-LTFs (Repeated-LTF-2x)
    Similar to L-LTF.
    Same efficiency as regular NGV-LTF, but better channel estimation, and better performance.
  Option 4: repeated regular NGV-LTFs (Repeated-LTF)
    Lower efficiency, but better channel estimation.

## Slide 6: Simulation Settings
10MHz DSRC channel @5.9GHz
CFO: uniform [-10 10]ppm on both Tx and Rx side.
Channel model: C2C channel with pure Doppler
Ideal Timing
1x1, 1ss, LDPC with Midamble
  11n LDPC codes
  Midamble period of 6 for all MCS (BPSK-1/2 to 256QAM-3/4)
Data: 300 bytes
OFDM numerology: 11ac 20MHz DC2

## Slide 7: Rural LOS
Repeated LTF-2x shows goodput advantage at medium to low SNR
LTF-2x shows goodput advantage at high SNR

## Slide 8: Urban Approaching LOS
Repeated LTF-2x shows goodput advantage at medium to low SNR
LTF-2x shows goodput advantage at high SNR

## Slide 9: Urban Crossing NLOS
Repeated LTF-2x shows goodput advantage at medium to low SNR
LTF-2x shows goodput advantage at high SNR

## Slide 10: Highway LOS
Repeated LTF-2x shows goodput advantage at medium to low SNR
LTF-2x shows goodput advantage at high SNR

## Slide 11: Highway NLOS
Repeated LTF-2x shows goodput advantage at medium to low SNR
LTF-2x shows goodput advantage at high SNR (< 29dB)

## Slide 12: Discussions
2x compressed NGV-LTF can reduce Midamble overhead almost by half.
Repeated LTF can improve channel estimation.
Repeated LTF-2x shows goodput gain at low-medium SNR.
LTF-2x is preferred for high SNR.

## Slide 13: Reference
[1] Bo Sun and etc., “802.11 NGV SG Proposed PAR”, IEEE 802.11-18/0861r9.
[2] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016r0.
[3] Dongguk Lim and etc., “Consideration on Features for 11bd”, 802.11-19/0009r0.

## Slide 14: Straw Poll 1
Do you agree that 11bd shall support compressed LTF in Midamble?
Y:
N:
A:

## Slide 15: Appendix

## Slide 16: Rural LOS
Repeated 2xLTF shows the best performance. ~1dB LTF averaging gain, and ~0.5dB interpolation gain.

## Slide 17: Urban Approaching LOS
Repeated LTF-2x shows the best performance. ~1dB LTF averaging gain, and ~0.5dB interpolation gain.

## Slide 18: Urban Crossing NLOS
Repeated LTF-2x shows the best performance. ~1dB LTF averaging gain, and ~0.5dB interpolation gain. Some interpolation loss for 256QAM

## Slide 19: Highway LOS
Repeated LTF-2x shows the best performance. ~1dB LTF averaging gain, and ~0.5dB interpolation gain.

## Slide 20: Highway NLOS
Repeated LTF-2x shows the best performance for most MCSs.
64QAM and 256QAM prefers regular LTF